## Slide 1: Performance of Coordinated Null Steering in 802.11be
Date: 2019-08-22
Authors:
Name | Affiliation | Address | Phone | Email
David Lopez-Perez | Nokia |  |  | 
Adrian Garcia-Rodriguez |  |  |  | 
Lorenzo Galati Giordano |  |  |  | 
Mika Kasslin |  |  |  | 
Olli Alanen |  |  |  | 
Enrico Rantala |  |  |  | 
July 2019

## Slide 2: Introduction
Coordinated beamforming and null steering have attracted considerable attention in previous 802.11be meetings
[1] Ron Porat (Broadcom), Comparison of Coordinated BF and Nulling with JT, 19/0799
[2] Eunsung Park (LG), Performance Investigation on Multi-AP Transmission, 19/0779
[3] Roya Doostnejad (Intel), Multi-AP Collaborative BF in IEEE 802.11, 19/0772
[4] Roya Doostnejad (Intel), Implicit Channel Sounding in IEEE 802.11, 19/0768
[5] Roya Doostnejad (Intel), Implicit Channel Sounding in IEEE 802.11(Feasibility Study), 19/0767
[6] Sungjin Park (LG), Multi-AP Transmission Procedure, 19/0804
[7] Sigurd Schelstraete (Quantenna), Nulling and coordinated beamforming, 19/0638
[8] Adrian Garcia-Rodriguez (Nokia), Coordinated Null Steering for EHT, 19/0401
[9] Sungjin Park (LG), Multi-AP Transmission Procedure, 19/0448
[10] Sigurd Schelstraete (Quantenna), Nulling and coordinated beamforming, 19/0445
[11] Kome Oteri (InterDigital), Coordinated Multi-AP Transmission for EHT, 19/0071
[12] Kiseon Ryu (LG), Consideration on multi-AP coordination for EHT, 18/1982
[13] Sameer Vermani (Qualcomm), Terminology for AP Coordination, 18/1926
July 2019

## Slide 3: Introduction
In this contribution, we
  Analyse the performance gains introduced by inter-AP coordination and coordinated beamforming/null steering
  Consider a scenario with both
    broad-band traffic—modelled as a file transfer protocol (FTP) service —, and
    low-latency traffic—modelled as an augment reality (AR) application
  Study the system performance as a function of
    the number of radiation nulls, and
    the traffic load
  Compare implicit versus explicit CSI acquisition procedures
July 2019

## Slide 4: When is coordinated beamforming/null steering useful?
July 2019
BB
BB
BB
BB
Dense scenarios with high interference
  There must be inter-AP interference to null
  where, in addition, the served STAs enjoy high SNRs
  Placing a radiation null reduces the degrees of freedom (d.o.f.) for beamforming, and thus the beamforming gain, penalizing cell cell-edge STAs
  where, in addition, the number of spatial streams to serve is reasonably smaller than the available d.o.f. at the antenna array in the AP
  As for the Shannon-Hartley theorem, multiplexing gains are linear, while SINR gains are logarithmic in terms of capacity, and the later gains should not come at the expense of the former

## Slide 5: Coordinated null steering in 802.11be
Simultaneous access and interference mitigation at expense of beamforming gain
July 2019
802.11be with no coordinated null steering
APs with up to 16 antennas
Multiple STAs per AP to serve
Spectrum shared according to CSMA/CA
Under utilization of the array capabilities – number of spatial streams << available spatial degrees of freedom of the array
802.11be with coordinated null steering
Coordination and nulling in place to
enhance spatial reuse,
fully utilize the available spatial degrees of freedom of the array, and
mitigate OBSS interference
BB
BB
BB
BB
simultaneous access
nulls
nulls
APs listen to each other
BB
BB
URLLC
BB
BB
URLLC
AP
1
AP
2
BB
time sharing
beam
beam
APs listen to each other
BB
BB
BB
URLLC
BB
BB
BB
BB
URLLC

## Slide 6: System model
X
July 2019
Frequency/Bandwidth | 5.18GHz/80MHz (1 channel)
AP deployment | Ceiling mounted ¦ Inter-AP distance = 15m ¦ AP height = 3m
AP characteristics | AP Tx power = 24dBm ¦ 8x2 antenna array (0.5λ separation) ¦ omni antenna element ¦ NF = 7dB
STA deployment | 4 broadband STAs/AP (≈5m from AP) ¦1 low-latency STA/AP (≈3m from AP) ¦ STA height = 1m (see previous figure)
STA characteristics | STA Tx power = 15dBm ¦ 1 omni antenna ¦ NF = 9dB
Channel model | 3D spatial channel model (3GPP TR38.901 – InH [14])
Channel estimation | a) Implicit channel est. with perfect CSI (fixed pilot overhead) b) Explicit channel est. with perfect CSI (Uncompressed BF feedback)
MAC layer conf. | No EDCA ¦ No RTS/CTS ¦ TXOP = 4ms ¦ IP/MAC header overhead considered ¦ Minstrel MCS selection
PHY layer conf. | Precoder = MU ZF (with and without nulls) ¦ PHY header overhead considered ¦ Omni PLCP header ¦ 11ax MCSs

## Slide 7: Traffic models
July 2019
Broadband STAs
FTP3 traffic model [15]
File size = 0.5 MBytes
Offered traffic = [25 50 75 100] Mbit/s exponential arrival rate
Low-Latency STAs
AR traffic model [16]
File size = 32 bytes
Frequency = 10 ms
constant arrival rate
AP
1
AP
2
AP
1
AP
2
Per STA traffic
time
Mix of broadband and low-latency traffic models
Per STA traffic
time

## Slide 8: Broadband performance as function of nulls number and offered traffic
Null steering provides significant capacity gains, up to 2.7x
July 2019
Coordination and null steering provides significant throughput (TP) gains due to
  more aggressive spectrum access
  inter-AP interference mitigation
For 25Mbps/STA offered traffic,
  2 nulls provide 43% 5%-tile TP gain w.r.t. no nulling.
  Placing more nulls does not improve performance, as the number of simultaneously active STAs is low
For 100Mbps/STA offered traffic,
  2 nulls provide 76% 5%-tile TP gains w.r.t. no nulling
  3 nulls provide 2.3x 5%-tile TP gains
  4 nulls provide 2.7x 5%-tile TP gains.
  The nulling gain decreases with the number of nulls as the UEs most vulnerable to interference are nulled first
Implicit CSI

## Slide 9: Latency performance as function of nulls number and offered traffic
Null steering provides lower latencies and jitter variances
July 2019
Coordination and null steering also provide lower latencies
  due to the more aggressive spatial reuse and interference mitigation
  Further lower latencies could be achieved through reduced TXOP durations
For 100Mbps/STA offered traffic,
  with 0 nulls, 22% of the low-latency packets do not make it within the 10ms deadline
  with 4 nulls, all low-latency packets make it on time
  Further SINR increases due to more nulls do not bring substantial latency advantages, since the low-latency packets are small and utilize low MCSs
TCP/IP will benefit from the ‘narrower’ delay distributions
Implicit CSI

## Slide 10: Implicit versus Explicit CSI acquisition
Implicit CSI is desirable to make the most out of null steering
July 2019
Explicit CSI is penalized by the overhead of NDPA+NDP+TF+feedback
  This overhead grows with the number of spatial streams and nulls scheduled
  The more nulls, the larger the overhead
  With 0 nulls, implicit CSI provides 28% median TP gains w.r.t. explicit CSI
  With 2, 3 and 4 nulls, such gains are 19%, 28% and 36%, respectively
  When using explicit CSI, the gain provided by the more nulls may be lost due to CSI acquisition overhead
Offered Traffic = 100Mbps

## Slide 11: What does coordinated null steering require?
July 2019
EHT
EHT
 in line with other EHT targets
 more specific work required
EHT
EHT
APs with multiple antennas
No severe spatial channel correlation among STAs
Efficient CSI acquisition procedures
Methods to acquire CSI from STAs served by other APs
Coordination procedures for null steering transmissions

## Slide 12: Conclusions
July 2019
In this contribution, we analysed the performance gains introduced by coordination and null steering
  Null steering provides significant throughput gains—up to 2.7x—and latency reductions—22% more packets meet their deadlines—due to both
    More aggressive spectrum access
    Inter-AP interference mitigation
  Null steering significantly benefits from implicit CSI—up to 36% throughput gains—, as the overhead incurred by explicit CSI acquisition to place a null may counteract its SINR benefits.

## Slide 13: References
[1] Ron Porat (Broadcom), Comparison of Coordinated BF and Nulling with JT, 19/0799.
[2] Eunsung Park (LG), Performance Investigation on Multi-AP Transmission, 19/0779.
[3] Roya Doostnejad (Intel), Multi-AP Collaborative BF in IEEE 802.11, 19/0772.
[4] Roya Doostnejad (Intel), Implicit Channel Sounding in IEEE 802.11, 19/0767.
[5] Roya Doostnejad (Intel), Implicit Channel Sounding in IEEE 802.11(Feasibility Study), 19/0767.
[6] Sungjin Park (LG), Multi-AP Transmission Procedure, 19/0804.
[7] Sigurd Schelstraete (Quantenna), Nulling and coordinated beamforming, 19/0638.
[8] Adrian Garcia-Rodriguez, Coordinated Null Steering for EHT, 19/0401.
[9] Sungjin Park (LG), Multi-AP Transmission Procedure, 19/0448.
[10] Sigurd Schelstraete (Quantenna), Nulling and coordinated beamforming, 19/0445.
[11] Kome Oteri (InterDigital), Coordinated Multi-AP Transmission for EHT, 19/0071.
[12] Kiseon Ryu (LG), Consideration on multi-AP coordination for EHT, 18/1982.
[13] Sameer Vermani (Qualcomm), Terminology for AP Coordination, 18/1926.
[14] 3GPP TR 38.901, “Study on channel model for frequencies from 0.5 to 100 GHz,” Jun. 2018.
[15] 3GPP TR 36.814, “Evolved Universal Terrestrial Radio Access (E-UTRA); Further advancements for E-UTRA physical layer aspects,” Mar. 2017.
[15] 3GPP TR 38.824, “Study on physical layer enhancements for NR ultra-reliable and low latency case (URLLC),” Mar. 2019.
July 2019

## Slide 14: Appendix
May 2019

## Slide 15: Capacity analysis
July 2019

## Slide 16: Delay analysis
July 2019