## Slide 1: Extended Range Modes in 11bd
Date: 2019-07-16
r0 (July 16, 2019): Initial version

## Slide 2: Summary
The 11bd PAR requires, among other things, “at least one mode that achieves at least 3dB lower sensitivity level (longer range), than [3 Mb/s in a 10 MHz channel]” [1].
A proposal under consideration [2] defines exactly one mode, that achieves almost exactly 3 dB lower sensitivity level than the referenced mode.
The proposal under consideration meets the PAR. But by itself it isn’t a game-changer, and probably isn’t sufficient (again by itself) to motivate market uptake of an entire new amendment.
Us. “The new, improved amendment adds new functionality that extends range!”
Adopters. “Sounds great! I’m interested—how, and how much extra range?”
Us. “There is one new rate, getting about 3 dB lower sensitivity level.”
Adopters. … well, what do we expect adopters to say?.
It would be better to extend to much more range, via a family of related modes

## Slide 3: DCM
DCM (for BPSK) involves duplicating the left-half tones onto the right-half tones
This ignores the extra rotations, but those don’t affect sensitivity
So the data rate is halved, and the sensitivity in a pure AWGN channel with no preamble losses would be exactly 3 dB better (from combining)
  In a pure AWGN channel with preamble processing, 3 dB lower Rx power would give worse packet detect, channel estimation, L-SIG decoding, etc., so net gain is slightly less than 3 dB
    (This is an issue with any range extension modes)
  With realistic multipath, we expect an extra 1-2 dB in diversity gain (cf. MRC results)
  Net DCM sensitivity improvement should be expected to be 3-4 dB in most realistic channels
We could adapt STBC from 11n to repeat across frequency instead of time, and it would come to essentially the same thing
DCM (or equivalently (adapted) STBC) can be seen as simple inner code, taking one bit in and yielding two bits out; easy to decode for LLRs to send to the ‘outer’ BCC

## Slide 4: A more general framework
We could define a family of ‘inner’ codes with successively lower rates and better sensitivities, spaced at reasonable gaps in sensitivity
Along the lines of 802.11a/g’s OFDM rates: one basic architecture yielding multiple rates
Here is one example of how this could work (retaining DCM and extending it; we could also investigate more complex inner codes with—perhaps—better sensitivities)
Mode 1: DCM (inner (2, 1, 2) code, rate 1.5 Mbps, 3 dB better sensitivity
Mode 2: Inner (6, 2, 4) code, rate 1 Mbps, circa 6 dB better sensitivity
Mode 3: Inner (12, 2, 8) code, rate 0.5 Mbps, circa 9 dB better sensitivity
  (same rotations for PAPR—whichever we choose--across all three modes)

## Slide 5: Simple modes, contd.—II
DCM divides tones into two equal sets, 1 tone on left maps to 1 on right
Mode 2 divides tones into three equal sets, replicates pairs of tones according to (6, 2, 4) code, with, e.g., generator matrix (101110, 010111)
  Each two tones on left maps to two tones in middle and two more tones on right
  (1,0) in leftmost pair of tones  1,0,1,1,1,0
    I.e., 1,1 in middle, 1,0 on right
  (0,1) in leftmost pair of tones  0,1,0,1,1,1
  (1,1) in leftmost pair of tones  1,1,1,0,0,1 (i.e., sum of codewords)
To decode, run BCJR algorithm on (6,2,4) code to get LLRs
  Or just calculate p(b1 = 0) = constant x ( p(r1 | c0) + p(r1 | c2)), p(b1 = 1) = constant x ( p(r1 | c1) + p(r1 | c3)), etc.
Extending pure DCM would give us a (3,1,3) code
  Even easier to decode, but around10 log10 (4/3) = 1.25 dB less improvement in sensitivity
  (Assuming there is no significant change in delta after applying outer code)

## Slide 6: Simple modes, contd.—III
So data is encoded by BCC, then interleaved
  Assume we use the regular 48-tone interleaver, then wrap in time
  This is probably fine, but we could use any other (e.g. 96-tone, more wrapping)
Post-interleaver data map to tones in left 1/3, which are grouped into blocks of 2 and then generate data on right as follows:
  00  0000
  01  1110 (so 4x Hamming distance overall)
  10  0111 ( “ )
  11  1001 (so 2x Hamming distance overall)
BCC interleavers are designed to prevent low-weight codewords from mapping to interleaved data with 1’s in close proximity
  Minimum distance probably increased by 4x, asymptotic coding gain 6 dB (TBV)
  Even if not, number of nearest neighbors is substantially thinned

## Slide 7: Other issues
Other issues (preamble robustness, OBSS interference) can be handled orthogonally
One straightforward approach for preambles is to reuse the structure from 11n that indicates new SIG data to follow:
  I.e., legacy preamble encoded via QPSK, with presence of quadrature component indicating that some number (2 or 3) extra SIG fields are present
  This could apply to all extended range modes or to some subset

## Slide 8: Conclusion
If we’re going to extend range, we should go beyond the bare minimum, and provide a really noticeable extension
Other things being equal, we should follow the historic path of generating multiple modes from a basic unified architecture
There are many ways of achieving this (and we should do due diligence), but a very simple approach can provide lower sensitivities by 3, 6, 9 dB
  Reuses and extends modes present in 11ax

## Slide 9: References
Doc. IEEE 802.11/18-0861r9, “802.11 NGV Proposed PAR”, Bo Sun (ZTE), Hongyuan Zhang (Marvell), November 2018
Doc. IEEE 802.11/19-0774r1, “Modulation Scheme for 11bd Range Extension Update, Jianhan Liu, Gary Anwyl, Thomas Pare (MediaTek), May 2019