## Slide 1: ULDR (ultra low date rate)
Date: 2019-07-16
Authors:

## Slide 2: Introduction
According to IEEE P802.11ba/D3.0 [1]
  The WUR PHY provides support LDR (low data rate) indicates 62.5 kb/s, and HDR (high data rate) indicates 250 kb/s.
  Manchester coding: Under sampling is prevented
  MC-OOK: Differential operation is prevented [5]
This contribution introduces ULDR (ultra low date rate) that leads to lower power consumption and lower noise.

## Slide 3: Simulation of the lifespan of a node [4]

## Slide 4: ULDR
ULDR (ultra low data rate) indicates 15,625 kb/s (quarter of LDR)
Approx. 4 x longer data packets than LDR
Approx. 4 x lower power consumption than LDR

## Slide 5: Radiation
Radiation behavior at different data rates from IEEE 802.11-18/0479r2 [3]

## Slide 6: Straw poll
Do you support the specification of the ULDR (ultra low date rate)?
Y
N
A

## Slide 7: References
[1] IEEE P802.11ba/D3.0, May 2019
[2] IEEE 802.11-17/0964r4 Signal Bandwidth and Sequence for OOK Signal Generation
[3] IEEE 802.11-18/0479r2 MC-OOK Symbol Design
[4] G.U. Gamm, M. Kostic, M. Sippel, L.M. Reindl Low power sensor node with addressable wake-up on demand capability; 2012 Int. J. Sensor Networks, Band: 11, Nummer: 1, Page: 48 – 56
[5] IEEE 802.11-18/770r0 Differential OOK for WUR