## Slide 1: Synchronous Multi-Link Transmission
Date: 2020-01-10
Authors:

## Slide 2: Recap: Synchronous Multi-link Transmission
When a STA simultaneously transmits and receives frames on multi-link, it may have some in-device coexistence (IDC) interference.
  When simultaneous Tx and Rx is happened between 2.4 GHz band and 5 GHz band, the IDC interference is probably negligible.
  But, the IDC interference caused by simultaneous Tx and Rx between 5 GHz band and 6 GHz band may be significantly problematic worse depending on some implementation capability like the RF filter performance.

## Slide 3: Recap: Synchronous Multi-link Transmission
For avoiding the IDC interference, a STA shall not transmit and receive frames on multi-link simultaneously.
  The STA may perform independent IDFT/DFT on each links.

## Slide 4: Motivation
To avoid that a STA transmit and receive frames on multi-link simultaneously, it may synchronize the starting times and ending times of the PPDU transmissions on multi-link.
This contribution discusses a synchronization requirement of the PPDU transmissions.

## Slide 5: Synchronization Requirement in Synchronous Multi-link Transmission
It can be a complicated issue to make OFDM symbol alignment for PPDUs transmitted on multi-link.
  Scenario 1) A STA may transmit frames on multi-link with different TXVECTOR parameters (e.g., FORMAT, HE_LTF_MODE, GI_TYPE).
    OFDM symbol misalignment between the ending times of the transmissions is within a maximum 16 μs (i.e., OFDM symbol duration with quadruple GI).
    Such OFDM symbol misalignment may not be resolved by current MAC padding and PHY padding.
5GHz
6GHz
AP
STA
L-STF | L-LTF | L-SIG | RL-SIG | HE-SIG-A | HE-STF | HE-LTF | … | HE-LTF | Data | PE
L-STF | L-LTF | L-SIG | RL-SIG | HE-SIG-A | HE-STF | HE-LTF | … | HE-LTF | Data | PE
AP
STA
TXVECTOR parameter FORMAT, HE_LTF_MODE, and GI_TYPE can be different for each PPDUs
OFDM symbol misalignment

## Slide 6: Synchronization Requirement in Synchronous Multi-link Transmission
It can be a complicated issue to make OFDM symbol alignment for PPDUs transmitted on multi-link.
  Scenario 2) A STA can have some constraint to use same TXVECTOR parameters for PPDUs simultaneously transmitted on multi-link. But, a STA can access a WM to transmit frames on multi-link at different times.
    It makes the same OFDM symbol misalignment issue as the scenario 1.
    Such OFDM symbol misalignment may not be resolved by current MAC padding and PHY padding.
5GHz
6GHz
AP
STA
TXVECTOR parameter FORMAT, HE_LTF_MODE, and GI_TYPE may be same for each PPDUs
L-STF | L-LTF | L-SIG | RL-SIG | HE-SIG-A | HE-STF | HE-LTF | … | HE-LTF | Data | PE
L-STF | L-LTF | L-SIG | RL-SIG | HE-SIG-A | HE-STF | HE-LTF | … | HE-LTF | Data | PE
OFDM symbol misalignment
AP
STA

## Slide 7: Synchronization Requirement in Synchronous Multi-link Transmission
Proposed synchronization requirement
  A difference between the ending times of PPDU transmissions shall be less than SIFS - (10%×aSlotTime).
    Because a minimum inter-frame space is not less than SIFS, Tx and Rx are not overlapped.
      A margin of 10%×aSlotTime considers the SIFS accuracy of the IEEE 802.11-2016 spec.
5GHz
6GHz
Data
MAC Padding
AP
STA
AP
STA
PHY Padding
PE
Data
MAC Padding
PHY Padding
PE
SIFS
Ack
MAC Padding
PHY Padding
PE
Block Ack
Difference between the ending times of the transmissions is less than SIFS - (10%×aSlotTime).
SIFS

## Slide 8: Synchronization Requirement in Synchronous Multi-link Transmission
Proposed synchronization requirement
  The solicited PPDU containing a control response (e.g., Ack or BlockAck) may also need the MAC padding and PHY padding mechanisms to the synchronization requirement.
  So, the solicited PPDU can be sent in any PPDU format (i.e., non-HT/HT/VHT/HE/EHT).

## Slide 9: Synchronization Requirement in Synchronous Multi-link Transmission
Proposed synchronization requirement
  If a STA transmits non-HT PPDUs that initiates a TXOP on multi-link (e.g., the RTS and CTS frame exchange),
    Those non-HT PPDU transmissions shall be started on multi-link within the SIFS - (10%×aSlotTime).
5GHz
6GHz
RTS
AP
STA
AP
STA
Difference between the starting times of the transmissions is less than SIFS - (10%×aSlotTime).
RTS
CTS
CTS
SIFS
SIFS
Data
MAC Padding
PHY Padding
PE
Data
MAC Padding
PHY Padding
PE
SIFS
SIFS

## Slide 10: Straw Poll 1
Do you support that in a synchronous multi-link transmission a difference between the ending times of PPDU transmissions shall be less than SIFS - (10%×aSlotTime)?

## Slide 11: Straw Poll 2
Do you support that in a synchronous multi-link transmission the solicited PPDU containing a control response (e.g., Ack or BlockAck) can be sent in any PPDU format?

## Slide 12: Straw Poll 3
Do you support that in a synchronous multi-link transmission non-HT PPDUs that initiates a TXOP on multi-link (e.g., the RTS and CTS frame exchange) shall be started within SIFS - (10%×aSlotTime)?