## Slide 1: Synchronous Multi-Link Operation
Date: 2020-04-17
Authors:

## Slide 2: Recap: Synchronous Multi-link Operation
When a STA simultaneously transmits and receives frames on multi-link, it may have some in-device coexistence (IDC) interference.
  When simultaneous Tx and Rx is happened between 2.4 GHz band and 5 GHz band, the IDC interference is probably negligible.
  But, the IDC interference caused by simultaneous Tx and Rx between 5 GHz band and 6 GHz band may be significantly problematic worse depending on some implementation capability like the RF filter performance.

## Slide 3: Recap: Synchronous Multi-link Operation
For avoiding the IDC interference, a STA shall not transmit and receive frames on multi-link simultaneously.
  The STA may perform independent IDFT/DFT on each links.

## Slide 4: Motivation
To avoid that a STA transmit and receive frames on multi-link simultaneously, it may synchronize the ending times of the PPDU transmissions on multi-link.
  If the ending times of the PPDU transmissions on multi-link are synchronized, the starting times of the following PPDU transmissions are naturally synchronized.
This contribution discusses a synchronization requirement of the PPDU transmissions.

## Slide 5: Synchronization Requirement in Synchronous Multi-link Operation
It can be a complicated issue to make OFDM symbol alignment for PPDUs transmitted on multi-link.
  Scenario 1) A STA may transmit frames on multi-link with different TXVECTOR parameters (e.g., FORMAT, HE_LTF_MODE, GI_TYPE).
    OFDM symbol misalignment between the ending times of the transmissions is within a maximum 16 μs (i.e., OFDM symbol duration with quadruple GI).
    Such OFDM symbol misalignment may not be resolved by current MAC padding and PHY padding.
5GHz
6GHz
AP
STA
L-STF | L-LTF | L-SIG | RL-SIG | HE-SIG-A | HE-STF | HE-LTF | … | HE-LTF | Data | PE
L-STF | L-LTF | L-SIG | RL-SIG | HE-SIG-A | HE-STF | HE-LTF | … | HE-LTF | Data | PE
AP
STA
TXVECTOR parameter FORMAT, HE_LTF_MODE, and GI_TYPE can be different for each PPDUs
OFDM symbol misalignment

## Slide 6: Synchronization Requirement in Synchronous Multi-link Operation
It can be a complicated issue to make OFDM symbol alignment for PPDUs transmitted on multi-link.
  Scenario 2) A STA can have some constraint to use same TXVECTOR parameters for PPDUs simultaneously transmitted on multi-link. But, a STA can access a WM to transmit frames on multi-link at different times.
    It makes the same OFDM symbol misalignment issue as the scenario 1.
    Such OFDM symbol misalignment may not be resolved by current MAC padding and PHY padding.
5GHz
6GHz
AP
STA
TXVECTOR parameter FORMAT, HE_LTF_MODE, and GI_TYPE may be same for each PPDUs
L-STF | L-LTF | L-SIG | RL-SIG | HE-SIG-A | HE-STF | HE-LTF | … | HE-LTF | Data | PE
L-STF | L-LTF | L-SIG | RL-SIG | HE-SIG-A | HE-STF | HE-LTF | … | HE-LTF | Data | PE
OFDM symbol misalignment
AP
STA

## Slide 7: Synchronization Requirement in Synchronous Multi-link Operation
Proposed synchronization requirement
  A difference between the ending times of PPDU transmissions shall be less than SIFS - (10%×aSlotTime).
    Because a minimum inter-frame space is not less than SIFS, Tx and Rx are not overlapped.
      A margin of 10%×aSlotTime considers the SIFS accuracy of the IEEE 802.11-2016 spec.
5GHz
6GHz
Data
MAC Padding
AP
STA
AP
STA
PHY Padding
PE
Data
MAC Padding
PHY Padding
PE
SIFS
Ack
MAC Padding
PHY Padding
PE
Block Ack
Difference between the ending times of the transmissions is less than SIFS - (10%×aSlotTime).
SIFS

## Slide 8: Synchronization Requirement in Synchronous Multi-link Operation
Proposed synchronization requirement
  The solicited PPDU containing a control response (e.g., Ack or BlockAck) may also need the MAC padding and PHY padding mechanisms to the synchronization requirement.
  So, the solicited PPDU can be sent in any PPDU format (i.e., non-HT/HT/VHT/HE/EHT).

## Slide 9: Straw Poll 1
Do you support the following PPDU transmission restriction for the constrained multi-link operation?
  If an AP MLD intends to align the ending time of DL PPDUs carrying a frame soliciting an immediate response simultaneously sent to the same non-STR non-AP MLD on multiple links, the AP MLD shall ensure that the difference between the ending times of transmitting DL PPDUs is less than TBD (<=SIFS) time.
    Where the reference of the ending time of the PPDU is TBD.
  Yes/No/Abstain/No Answer: 50/4/35/10 (Passed)