## Slide 1: HARQ Applicable A-MPDU
Date: 2019-11-11
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Yanyi Ding |  |  |  | 
Rojan Chitrakar |  |  |  | 
Yoshio Urabe |  |  |  | 

## Slide 2
Background
Many contributions have discussed how HARQ operation is applied to A-MPDU [1]-[3].
  Codeword level HARQ operation may be a natural choice for 11be [1].
In this contribution, we like to discuss the applicability of HARQ operation to A-MPDU and introduce a new terminology called HARQ Applicable A-MPDU.
  We then discuss codeword level HARQ feedback for HARQ applicable A-MPDU.

## Slide 3
  A-MPDU pre-EOF padding includes any A-MPDU subframes with 0 in the MPDU Length field and 0 in the EOF field inserted in order to meet the minimum MPDU start spacing requirement.
Rules for MPDU ordering in an A-MPDU:
  if an Ack, Compressed BlockAck or Multi-STA BlockAck frame is present in an A-MPDU, it shall be the first MPDU in the A-MPDU.
  if one or more Trigger frame is present in an A-MPDU, the one or more Trigger frame is the first MPDU of the A-MPDU unless the A-MPDU also carries an Ack, Compressed BlockAck or Multi-STA BlockAck frame in which case the one or more Trigger frame is included immediately after the Ack, Compressed BlockAck or Multi-STA BlockAck frame.
Recap: A-MPDU Format

## Slide 4
Applicability of HARQ Operation to A-MPDU
The purpose of applying HARQ operation to A-MPDU is to improve link throughput by minimizing MAC-level retransmission.
When an A-MPDU does not include any MPDU that solicits acknowledgement, no MAC-level retransmission is required for the A-MPDU.
  In this case, it does not make sense to apply HARQ operation to the A-MPDU.
Our view:
  HARQ operation shall be disabled for an A-MPDU that is not a HARQ applicable A-MPDU, e.g. an A-MPDU that is transmitted in the Control Response context.
    HARQ Applicable A-MPDU is an A-MPDU containing at least one MPDU that solicits acknowledgement, e.g.
      ack-enabled single-TID A-MPDU
      non-ack-enabled multi-TID A-MPDU
      ack-enabled multi-TID A-MPDU

## Slide 5
HARQ Applicable A-MPDU
In a HARQ Applicable A-MPDU, one or more MPDUs may not solicit acknowledgement.
A HARQ Applicable A-MPDU may comprise two MPDU groups:
  MPDU group 1 comprises MPDU(s) that do not solicit acknowledgement
  MPDU group 2 comprises MPDU(s) that solicit acknowledgement
Example HARQ Applicable A-MPDU | MPDU group 1 | MPDU group 2
ack-enabled single-TID A-MPDU | zero or one Ack, Compressed BlockAck or Multi-STA BlockAck frame; zero or more Action No Ack frames; One or more QoS Null frames with No Ack ack policy and/or Trigger frames. | one QoS Data frame with Normal Ack or HTP Ack ack policy or Management frame that solicits an immediate response.

## Slide 6
Codeword Level HARQ Feedback
Group 1 MPDUs do not require MAC level retransmissions and thus it is meaningless to apply codeword level retransmissions to Group 1 MPDUs.
Our view:
  HARQ feedback is not required for codewords that do not correspond to group 2 MPDUs.
Pros: HARQ feedback overhead may be reduced.
Cons: MAC needs to inform PHY the boundary between group 1 MPDUs and group 2 MPDUs.

## Slide 7: Summary
A new terminology HARQ Applicable A-MPDU is introduced.
In our view, HARQ operation shall be disabled for an A-MPDU that is not a HARQ Applicable A-MPDU. Furthermore, HARQ feedback is not required for codewords not corresponding to MPDUs that solicit acknowledgement in a HARQ Applicable A-MPDU.

## Slide 8: Reference
IEEE 802.11-19/0873r1, HARQ Framing, July 2019
IEEE 802.11-19/1038r1, HARQ with A-MPDU, July 2019
IEEE 802.11-19/1131r0, Consideration on HARQ Unit, July 2019