## Slide 1: NGV Frame Format: follow-up
Date: 2019-09-16
Authors:

## Slide 2: Introduction
In previous meetings, some preamble design has been decided [1].
  L-STF, L-LTF, L-SIG is pre-appended to each PPDU
  RL-SIG is added after L-SIG
  NGV-SIG is included after RL-SIG
  10MHz preamble is duplicated for 20MHz PPDU
In this contribution, we will discuss the leftover items for frame format design of 10MHz and 20MHz PPDU.

## Slide 3: NGV Frame Format
LSTF, LLTF, LSIG, RL-SIG fields are agreed on to be pre-appended to each 11bd frame [1].
The fields after RL-SIG is undefined or not specified:
  NGV-SIG: to signal NGV PHY parameters
  NGV-STF: to re-adjust Rx power gain, necessary for multi-stream case.
  NGV-LTF: to estimate channel for NGV data decoding, according to NGV tone plan, stream number, and etc.
  NGV-Data: the modulated data symbols.
NGV Data
10MHz
LLTF
LSTF
LSIG
RL-SIG
NGV SIG
NGV STF
NGV LTF
NGV Data
10MHz
LLTF
LSTF
LSIG
RL-SIG
NGV SIG
NGV STF
NGV LTF
10MHz
LLTF
LSTF
LSIG
RL-SIG
NGV SIG

## Slide 4: NGV-SIG
NGV SIG Format:
  Two symbols: the second symbol is repetition of the first symbol.
  Each symbol uses 11p 10MHz tone plan with 24 information bits.
  Each NGV SIG symbol uses MCS0 modulation,
  The same as L-SIG and RL-SIG, to match SIG decoding performance and support extended range
NGV SIG Content: 24 bits
  BW: 1 bit, MCS: 4 bits, Nss: 1 bit
  LDPC Extra symbol: 1bit
  Midamble period: 2 bit (TBD), Midamble Format: 1 bit (TBD)
  Reserved: TBD bits (e.g. 4 bits)
  CRC: TBD bits (e.g. 4 bits), Tails: 6 bits

## Slide 5: NGV Training Fields
NGV-STF and NGV-LTF will be need to be added
  Transmitter may deploy multiple antennas, steering matrices can be different from 11p preamble to 11bd portion.
  NGV supports two spatial streams as an optional feature
  For both cases, need to readjust power for data decoding
Format
  10MHz PPDU: NGV-STF and NGV-LTF use 2x DC 20MHz VHT-STF and VHT-LTF
  20MHz PPDU: TBD depending on 20MHz mask definition
    E.g. NGV-STF and NGV-LTF use 11ac 40MHz VHT-STF and VHT-LTF with 2x downclock.

## Slide 6: Summary
In this contribution, we propose the frame format of 11bd PPDUs.
  NGV-SIG has two symbols, the second symbol repeats the first symbol
  NGV-STF and NGV-LTF use 11ac OFDM numerology with 2x downclock.

## Slide 7: Reference
[1] 11-19/0514, “11bd FRD SFD Motion Booklet”

## Slide 8: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “The NGV-SIG field has two symbols, and the second symbol is the repetition of the first symbol.”
  “The NGV-SIG field is modulated with MCS0.”
Y:
N:
A:

## Slide 9: Straw Poll 2
Do you agree to add the following text into Section 3 of SFD?
  “11bd shall include NGV-STF and NGV-LTF symbols after NGV-SIG”.
Y:
N:
A:

## Slide 10: Straw Poll 3
Do you agree to add the following text into Section 3 of SFD?
  “The NGV-STF in 11bd 10MHz PPDU shall use 11ac 20MHz VHT-STF with 2x downclock.”
  “The NGV-LTF in 11bd 10MHz PPDU shall use 11ac 20MHz VHT-LTF with 2x downclock.”
Y:
N:
A: