## Slide 1: NGV Midamble Design: Follow-up
Date: 2019-09-16
Authors:

## Slide 2: Introduction
In July meeting, some Midamble simulation results are provided to select Midamble period choice [1].
  one midamble format: regular LTF
  one spatial stream
More simulation results are added to support the choice of Midamble format and periods for 11bd.
  Different Midamble formats
  Two spatial streams

## Slide 3: Midamble Formats
We have shown four different midamble formats [2]
  Option 1: one regular NGV-LTF (LTF)
  Option 2: one 2x compressed NGV-LTF (C-LTF)
  Option 3: repeated 2x compressed NGV-LTFs (RC-LTF)
  Option 4: repeated regular NGV-LTFs (R-LTF)
Pros and Cons:
  LTF and R-LTF enable simpler receiver processing, and can support all channel and Nss cases.
  LTF, especially R-LTF, will lose efficiency in good channel conditions.
  C-LTF shows peak goodput gains for one ss in most C2C channels.
  RC-LTF shows goodput gain for one ss in low SNR region.
  C-LTF and RC-LTF will need channel interpolation, and define new pilot location on even tones.

## Slide 4: Midamble Periods
Number of Midamble periods:
  The more supported Midamble periods, the more transmitter/receiver implementation complexity.
  Need to minimize the number of Midmable periods.
  Choose Midamble periods based on simulations.

## Slide 5: Simulation Settings
10MHz PPDU: 11ac 20MHz DC2 with LDPC.
Pkt size: 300 bytes baseline.
  Round to integer number of periods.
  Randomize bits with +/- 1/2 period.
CFO, Ideal timing.
Goodput is the maximum achievable effective data rate.
Goodput(SNR, M) = maxMCS{Rate(MCS) * (1-PER(MCS, SNR, M))* M/(M+1)}
  M is the midamble period
New results compared to July Meeting:
  BPSK-DCM simulations
  Different Midamble formats
  Two spatial stream simulations.

## Slide 6: Rural LOS: 1x1-1ss, Range Extension
At low SNR, R-LTF and RC-LTF shows goodput advantage over single LTF. Extending the range by ~2dB. R-LTF similar to RC-LTF.
LTF repetition is needed to take advantage of new lowest modulation (BPSK-DCM).

## Slide 7: Highway LOS : 1x1-1ss, Range Extension
At low SNR, R-LTF and RC-LTF shows goodput advantage over single LTF. Extending the range by ~2dB. R-LTF similar to RC-LTF.
LTF repetition is needed to take advantage of new lowest modulation (BPSK-DCM).

## Slide 8: Highway NLOS: 1x1-1ss, Range Extension
At low SNR, R-LTF and RC-LTF shows goodput advantage over single LTF. Extending the range by 2~3dB.
LTF repetition is needed to take advantage of new lowest modulation (BPSK-DCM).

## Slide 9: Rural LOS: 1x1-1ss, Peak Goodput
C-LTF shows ~5% peak goodput gain, from shorter Midmable duration.
M=10 shows the best goodput.

## Slide 10: Highway LOS : 1x1-1ss, Peak Goodput
C-LTF shows ~8% peak goodput gain.
M=6 shows the best goodput.

## Slide 11: Highway NLOS: 1x1-1ss, Peak Goodput
C-LTF shows ~10% peak goodput gain.
M=4 shows the best goodput.

## Slide 12: D2D 15Km/h NLos: 2x2-2ss
For 2ss in NLos D2D channel, at high SNR region, C-LTF show big disadvantage due to interpolation loss from frequency-selective channel and single-stream pilot.
Regular LTF is preferred. M=6,8,10 provide the best goodput.

## Slide 13: D2D 45Km/h NLos: 2x2-2ss
For 2ss in NLos D2D channel, at high SNR region, C-LTF show big disadvantage due to interpolation loss from frequency-selective channel and single-stream pilot.
Regular LTF is preferred. M=4 provides the best goodput.

## Slide 14: Discussion: Midamble Format
Repeated LTF (R-LTF, RC-LTF):
  shows important range-extension gain for lowest MCS.
Compressed LTF (C-LTF or RC-LTF):
  Provide peak goodput gain for one stream.
  Does not perform well in high-frequency selective channel and multi-stream cases.
Options:
  Use R-LTF or RC-LTF only for BPSK modulation (with and without DCM), match with preamble power boost.
  Use LTF or C-LTF for non-BPSK modulation of both single-stream and multi-stream.

## Slide 15: Discussion: Midamble Periods
Number of periods:
  It seems two choices may not provide sufficient optimization
  Three seems to be a good design.
  The possible options are: 10, 6, 4 for both 1ss and 2ss.
Signaling:
  2 bits of signaling will be needed.
  The fourth option, we can leave it RESERVED or define some large Midamble to support potential long transmission.

## Slide 16: Reference
[1] Rui Cao and etc., “NGV Midamble Period Choice”, IEEE 802.11-19/1073.
[2] Rui Cao and etc., “Compressed Midamble”, IEEE 802.11-19/0685.

## Slide 17: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “The Midamble and NGV-LTF format of 11bd 10MHz PPDU shall use Repeated LTF or Repeated compressed LTF for NGV-Data modulated with BPSK.”
Y:
N:
A:

## Slide 18: Straw Poll 2
Do you agree to add the following text into Section 3 of SFD?
  “11bd shall use two bits in NGV-SIG to signal the Midamble period.”
Y:
N:
A:

## Slide 19: Straw Poll 3
Do you agree to add the following text into Section 3 of SFD?
  “11bd shall define at least three Midamble periods.”
Y:
N:
A:

## Slide 20: Straw Poll 4
Do you agree to add the following text into Section 3 of SFD?
  “One of the Midamble periods is 4.”
Y:
N:
A:

## Slide 21: Straw Poll 5
Do you agree to add the following text into Section 3 of SFD?
  “The one of the Midamble periods is 6.”
Y:
N:
A:

## Slide 22: Straw Poll 6
Do you agree to add the following text into Section 3 of SFD?
  “The one of the Midamble periods is 10.”
Y:
N:
A:

## Slide 23: Straw Poll 7
Which one do you prefer for the Midamble format:
  Option 1: only regular LTF is allowed
  Option 2: both regular LTF and compressed LTF are allowed
Option 1:
Option 2:
A:

## Slide 24: Appendix

## Slide 25: D2D 15Km/h Los: 2x2-2ss
At low doppler with Los, M=6,8,10 provides similar goodput.

## Slide 26: D2D 15Km/h NLos: 2x2-2ss
For low speed with Nlos, N=8, 10 provides the best goodput.

## Slide 27: D2D 45Km/h NLos: 2x2-2ss
For medium speed with NLos, N=4 provides the best peak goodput.

## Slide 28: D2D 70Km/h NLos: 2x2-2ss
For relatively high speed with NLos, N=4 provides the best peak goodput.