## Slide 1: Frame format for 11bd
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insun Jang |  |  |  | Insun.jang@lge.com
Suhwook Kim |  |  |  | Suhwook.kim@lge.com
Jeongki Kim |  |  |  | Jeongki.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Sept. 2019

## Slide 2: Introduction
In previous meeting, the various motions related to Frame format had passed as below
  FRD&SFD Motion #9 and #21
    “11bd PPDU includes a NGV-Signal field to indicate the transmission information”
    “ NGV-SIG is located right after the RL-SIG in 11bd PPDU.”
  FRD&SFD Motion #10
    “11bd PPDU design shall support Midamble(s) in Data field”
  FRD&SFD Motion #24
    “ The preamble of 11bd PPDU shall include repeated LSIG symbol after LSIG.”
However, we didn’t determine completely the specifics of what fields to be included and how to configure them.
Thus, in this contribution, we discuss the contents and configuration of NGV-SIG and how to configure the other fields for 11bd PPDU.

## Slide 3: Baseline for 11bd frame
Based on passed motions in [1], 11bd frame can be configured as follow.
  The details for NGV-STF and NGV-LTF are not discussed and determined yet.

## Slide 4: NGV-SIG Fields (1/2)
Based on the discussion[5][6], NGV-SIG may include the following information for 11bd transmission.
  Contents for NGV-SIG field
    BW : 1bit
      10MHz /20MHz
    MCS : 3/ 4 bits
      3 bits case
        Exclusion of BPSK with ¾ rate which is not used in 11n/11ac/11ax and Inclusion of 256 QAM
      4 bits case => Inclusion of 256 QAM and DCM+BPSK
    DCM : 1bit
      Indicates the usage of DCM in the data field
      If DCM+BPSK may be included in MCS, this field can be omitted.
    LDPC extra symbol : 1bit
      Indicates the presence of the extra OFDM symbol segment for LDPC
    NSTS : 1bit
      11bd device can support to upto2 spatial streams according to passed motion

## Slide 5: NGV-SIG Fields (2/2)
    Midamble periodicity : 1/2bit
      As described in [2~4], two values can be considered.
        One short period for high MCSs or high Doppler channel
        One long period for low MCSs or low Doppler channel
    LTF/Mid-amble configuration : 1bit
      Indicated whether Normal LTF or compressed LTF is used for NGV-LTF/Mid-amble
    STBC : 1bit
      Since multiple antennas may be considered in V2X transmission, STBC can be considered for reliable transmission.
    CRC : 4bit / parity : 1bit
      NGV-SIG can be configured with one symbol like 11a, the parity bit instead of CRC can be considered for valid check.
    Tail bit : 6bit
    More bit for indication of other information : TBD
  Since the max number of bits required for above NGV-Signal field may be less than 24 bit, NGV-SIG can be configured with one OFDM symbol with MCS0.

## Slide 6: Composition of NGV-SIG
For range extension of 11bd, NGV-SIG field also requires the same reliability as L-SIG.
In order to achieve the reliability of NGV-SIG field for range extension of 11bd, following two options can be considered for NGV-SIG configuration.
  Option 1 : Repetition of NGV-SIG
    Similar with RL-SIG, NGV-SIG is repeated in 11bd PPDU.
      The same NGV-SIG symbol is repeated.
      For the robust transmission in Doppler channel, MCS0 is applied to NGV-SIG.
    enable range extension by NGV-SIG and repeated NGV-SIG MRC

## Slide 7: Composition of NGV-SIG
  Option 2 : apply the DCM in NGV-SIG field
    NGV-SIG is composed with 2 symbols
    NGV-SIG field is encoded at R=1/2 with BCC and mapped to a BPSK DCM
    Since BPSK DCM is applied to NGV-SIG field, it may need an indication for this. (otherwise fix the frame format with DCM)
      For example, for the early indication, we can consider the method using phase rotation.

## Slide 8: Performance of NGV-SIG
Rural LoS channel
  By using either repetition or DCM on NGV-SIG field, we can achieve similar performance at 1% PER with that of L-SIG*.
    Both schemes have 2 dB more gain compare to one transmission for NGV-SIG.
  The difference between repetition and DCM is very small.
  In an aspect of implementation, repetition is very simple.
PER of L-SIG means PER of L-SIG and RL-SIG MRC

## Slide 9: Performance of NGV-SIG
Urban C2C channel
  DCM shows slightly better performance than the repetition.
  The repetition provides comparable performance with L-SIG.

## Slide 10: Performance of NGV-SIG
Highway C2C channel
  The trend is similar to that of urban channels.

## Slide 11: NGV-STF and NGV-LTF
Based on the passed motions [ #15, #26 ], we can consider the followings
  Because two spatial streams accepted in unicast transmissions, NGV-STF is required to support smooth multiple stream transmission.
    By using NGV-STF, it can improve automatic gain control estimation in a MIMO transmission.
  Also, for the channel estimation per each stream, NGV-LTF should be transmitted.
    Number of LTF symbol can be extended up to 2.
Therefore, NGV-STF and NGV-LTF should be included in 11bd PPDU.

## Slide 12: Conclusion
We took a look at the contents of NGV-SIG field and corresponding transmission method for range extension.
  NGV-SIG field can be configured with 24 data bits by considering all the given available information.
  To meet the range extension requirement, the two methods are considered for the transmission of NGV-SIG field, i.e., repetition and DCM.
    While the performance of the two methods are comparable, the repeated NGV-SIG transmission is preferred in terms of simpler implementation.
To provide the reliable performance of 11bd for MIMO transmission, NGV-STF and NGV-LTF should be included in 11bd PPDU.

## Slide 13: SP1
Do you agree to add the following to section 3 in 11bd SFD?
  “ The NGV-SIG field carries information required to interpret 11bd PPDU. The NGV-SIG field is composed of one symbol containing 24 data bits.
  The contents for 24 data bits are TBD”
  The NGV-SIG symbol shall be BCC encoded at rate, R = 1/2, be interleaved, be mapped to a BPSK constellation.”
  Y/N/A

## Slide 14: SP2
Do you agree to add the following to section 3 in 11bd SFD?
  “The preamble of 11bd PPDU shall include repeated NGV-SIG after NGV-SIG.
  The RNGV-SIG is configured identically to the NGV-SIG.”
  Y/N/A

## Slide 15: SP3
Do you agree to add the following to section 3 in 11bd SFD?
  “The preamble of 11bd PPDU shall include NGV-STF and NGV-LTF after repeated NGV-SIG.
  The composition of NGV-STF and NGV-LTF is TBD”
  Y/N/A

## Slide 16: Reference
[1] IEEE 802.11-19/0514r6, Motion Booklet for IEEE 802.11 TGbd
[2] IEEE 802.11-19/1073r0, NGV Midamble Choice
[3] IEEE 802.11-19/1151r0, Midamble in NGV
[4] IEEE 802.11-19/1109r0, Further investigation of mid-amble performance
[5] IEEE 802.11-19/1153r0, NGV PPDU Format
[6] IEEE 802.11-19/739r2, PPDU format for 11bd