## Slide 1: Auto-detection method for 11bd
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insun Jang |  |  |  | Insun.jang@lge.com
Suhwook Kim |  |  |  | Suhwook.kim@lge.com
Jeongki Kim |  |  |  | Jeongki.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Sept. 2019

## Slide 2: Introduction
In the previous meeting, we have been decided to include the RL-SIG and NGV-SIG in 11bd PPDU.
Based on passed motions in [1], 11bd preamble can be configured as follow.
In this contribution, we investigate the auto-detection method with given 11bd preamble structure so far.

## Slide 3: Auto-detection (1/2)
For the classification of 11bd, we can consider the following two methods.[1][2]
  Option 1 : check of repetition and contents
    Since RL-SIG is included in 11bd PPDU, the auto-detection method which is adopted in 11ax can be used for distinction of 11bd.
Repetition check
MRC & Contents check
11p
Received PPDU
N
N
Y
11bd
RL-SIG
Auto-detection with RL-SIG
  First step : Repetition check
    As introduced in [3], multiple ways in frequency domain can be considered
  Second step : L-SIG contents check
    Parity check = OK
    Rate check = 6Mbps
    Length field (mod 3) = 0

## Slide 4: Auto-detection (2/2)
  Option 2 : Check of phase rotation of symbol(s) after L-SIG
    It is similar way with conventional method(e.g., 11n/11ac)
    Here, we can take a look at the two cases.
      Case 1 : checking of one symbol
        QBPSK is applied on RL-SIG.
      Case 2 : checking of two symbol
        QBPSK is applied on RL-SIG.
        BPSK is applied on NGV-SIG.

## Slide 5: Simulation setup
BW : 10MHz
1Tx and 1Rx
C2C channel
  Rural LoS, Urban approaching LoS, Urban crossing NLoS, Highway LoS, Highway NLoS
Ideal timing and ideal CFO estimation
Auto-detection
  L-SIG repetition check and contents check (i.e., Hamming Distance and length field ( mod3 =0) )
  Constellation check (i.e., QBPSK or QBPSK and BPSK)

## Slide 6: Miss/False Error Probability
Rural LoS
  P-miss of repetition is lower than error rate of L-SIG.
  On the other hand, we can verify that P-miss of QBPSK is high and even higher than PER of L-SIG.
    In addition, even if two OFDM symbols after L-SIG are used in the classification of 11bd, it can not provide reliable performance.

## Slide 7: Miss/False Error Probability
Urban channel
  The repetition and contents check provide the more reliable miss/false detection performance.

## Slide 8: Miss/False Error Probability
Highway channel

## Slide 9: Summary
In this contribution, we evaluate the various auto-detection method by using the RL-SIG.
By simulations, we confirmed that repetition and contents check showed reliable miss detection and false detection error probability in C2C channels.

## Slide 10: SP1
Do you agree to add the following sentence into section 3 of 11bd SFD?
  ‘RL-SIG is modulated with BPSK‘
  Y/N/A

## Slide 11: Motion 1
Move to include the following text to section 3 in 11bd SFD
  ‘RL-SIG is modulated with BPSK'
  Move : Dongguk Lim
  Second :

## Slide 12: Reference
[1] IEEE802.11-19/1108r1, Preamble design and auto-detection for 11bd
[2] IEEE802.11-19/1153r0, NGV PPDU Format
[3] IEEE802.11-15/0579r2, 802.11ax Preamble Design and Auto-detection