## Slide 1: 11be tone plan
Date: 2019-11-05
Authors:
Name | Affiliation | Address | Phone | Email
Ross Jian Yu |  | F3-6A, Huawei Base, Bantian, Shenzhen |  | ross.yujian@huawei.com
Ming Gan |  |  |  | 

## Slide 2: Background
In last meeting, the following SPs passed with plenty of supports:
  SP1: Do you support adding 320MHz and 160+160MHz PPDUs to 11be?
  SP2: Do you support the 11be uses the same subcarrier spacing for the data portion of EHT PPDU as 11ax data portion?
  SP3: Do you support the following EHT tone plans?
    Reuse 11ax tone plan for 20/40/80/160/80+80MHz
    320MHz and 160+160MHz use duplicated HE160 for OFDMA tone plan
  Note: puncturing design TBD. Non-OFDMA 320MHz/160+160MHz tone plan TBD
Whilst the followings are still pending:
  Non-OFDMA 320MHz/160+160MHz tone plan
  Non-OFDMA 240MHz tone plan

## Slide 3: Two existing proposals
Proposal 1: Non-OFDMA 320MHz tone plan proposal in [1]:
Proposal 2: Non-OFDMA 320Mhz tone plan proposal in [2]
4068 or 4066 or …
DC: 5 or 7 or …
12 left guard
11 right guard
996 + 5 subband DC
996 + 5 subband DC
12 Edge
11 Edge
996 + 5 subband DC
SU tone plan:
23
Null
996 + 5 subband DC
23
DC
23
Null
 | Proposal 1 | Proposal 2
Pro | Easy for implementation, can reuse per segment Tx/Rx procedure Unified tone plan for OFDMA and non-OFDMA | Higher Efficiency (2% gain) considering additional occupied tones and fewer pilot tones, hence higher max. data rate/Tput.
Con | Lose efficiency | Different tone plan/implementation for OFDMA and non-OFDMA

## Slide 4: Harmonized tone plan
A harmonized tone plan is proposed below:
  2% efficiency gain assuming same pilots as 11ax are used per subband. Efficiency can be higher with fewer pilots per subband.
The usage of the additional RU(s) can be indicated in the signal fields.
  If additional RUs are used, higher efficiency is achieved
  If additional RUs are not used, four duplicated subbands as in proposal 1
A good tradeoff between efficiency and complexity.
Applicable to many different scenarios:
  Also applicable to 160MHz + 160Mhz if additional RUs are not occupied.
  Each of the four subbands is also applicable to 80MHz-only devices

## Slide 5: Harmonized tone plan
Applicable to many different scenarios:
  Can be applied to both non-OFDMA and OFDMA transmission
Used for non-OFDMA:
  Can achieve higher efficiency
  4*996 and additional RUs can be seen as a big RU if additional RUs are used.
Used for OFDMA:
  Can achieve higher efficiency
  Can be used for both SU and MU transmission
  Reuse the existing RUs
Used for both:
  A unified tone plan

## Slide 6: Signaling
In EHT-SIG-A, there exists signaling if additional RU is used or not.
  Through a separate bit
  Through an entry in BW:
Exact signaling method can be further studied.
BW | Meaning
20…160/80+80 | BW modes as in 11ax
320/160+160 with 4*996 only | Low complexity Mode
320 with 4*996+2/3*26 tone RU | High Efficiency Mode
Other punctured modes | TBD

## Slide 7: Wrap up
A Harmonized tone plan is discussed, which considers both efficiency and complexity.
The proposed method can also help to ease the complexity of filter/spectral mask design if additional RUs are not used.
The method can be applied to:
  Both non-OFDMA mode and OFDMA mode
  Also applicable to 160MHz + 160Mhz if additional RUs are not occupied.
  Each of the four subbands is also applicable to 80MHz-only devices

## Slide 8: SP 1
Do you support the following EHT tone plans?
  For non-OFDMA 320MHz tone plan, uses the following tone plans shown below.
  Note: puncturing design TBD. Non-OFDMA 160+160MHz tone plan TBD

## Slide 9: SP 2
Do you support the following EHT tone plans?
  For OFDMA 320MHz tone plan, uses the following tone plans shown below.
  Note: puncturing design TBD. OFDMA 160+160MHz tone plan TBD

## Slide 10: Reference
1. https://mentor.ieee.org/802.11/dcn/19/11-19-0797-01-00be-11be-320mhz-channelization-and-tone-plan.pptx
2. https://mentor.ieee.org/802.11/dcn/19/11-19-1066-00-00be-tone-plan-discussion.pptx