## Slide 1: Secure LTF Required and Secure LTF Support[ed] subfields
Date: 2019-09-04
Authors:

## Slide 2: Motivation/Background
The Ranging Parameters element includes a Ranging Parameters field which has Secure LTF Required and Secure LTF Support[ed] subfields
The Extended Capabilities element has a Secure LTF Support[ed] bit
In this presentation, we
  Propose how to render the description in the specification complete (and consistent)

## Slide 3: Terminology
Secure LTF Support[ed]
  In the Extended Capabilities element included in the Beacon/Probe Response indicates that the RSTA is capable of generating and transmitting; and receiving and parsing secure LTF
  In IFTMR:Ranging Parameters element:Ranging Parameters field indicates that the ISTA is capable of generating and transmitting; and receiving and parsing secure LTF
  In IFTM:Ranging Parameters element:Ranging Parameters field Reserved

## Slide 4: Terminology
Secure LTF Required
  In IFTMR:Ranging Parameters element:Ranging Parameters field indicates that the ISTA is requesting a FTM session with Secure LTF enabled.
  In IFTM:Ranging Parameters element:Ranging Parameters field when the Status Indication subfield is set to Successful (1), indicates that the RSTA has setup a FTM session with Secure LTF enabled.

## Slide 5: What does D1.3 say?
In 11.22.6.3.3 Trigger-based and non-Trigger-based Ranging Measurement Negotiation
  RSTA shall set Max DL Rep and Max UL Rep in IFTM based on the values in IFTMR, if Secure LTF Req[uired] subfield in IFTMR is set to 1
In 11.22.6.3.4 Secure LTF measurement setup
  ISTA may set Secure LTF Support[ed] subfield in IFTMR based on Secure LTF Support[ed] field in the Extended Capabilities element in the Beacon from the RSTA set to 1 and dot11SecureLTFImplemented set to true in the ISTA
  Under the above condition, the RSTA may set Secure LTF Req[uired] subfield in IFTMR to 1
  IFTM includes a Secure LTF Parameters element if (and only if) the IFTMR had Secure LTF Req[uired] subfield set to 1 and the corresponding IFTM had Secure LTF Req[uired] subfield set to 1

## Slide 6: Can the RSTA Require Secure LTF for a session without the ISTA requiring it?
Not without having a PASN established between the ISTA and the RSTA
  Why would the ISTA establish PASN without requiring Secure LTF?
Without PASN between ISTA and RSTA, the following will not work
  RSTA sets Secure LTF Support[ed] in Extended Caapabilities element to 1
  ISTA in IFTMR sets Secure LTF Req[uired] to 0 AND Secure LTF Support[ed] to 1
  RSTA in IFTM sets Secure LTF Req[uired] to 1

## Slide 7: What is the issue?
Do we need the Secure LTF Support[ed] subfield in the Ranging Parameters field?
  No.
How does it work without the Secure LTF Support[ed] subfield?
  If IFTMR has the Secure LTF Required subfield set to 1, it implies that the ISTA supports Secure LTF
  If IFTM has the Secure LTF Required subfield set to 1, it implies that the corresponding FTM session has Secure LTF enabled
  The Secure LTF Required subfield should be renamed to Secure LTF Required/Enabled subfield.
How about non-secure sessions with LTF repetitions?
  Managed by Max {UL|DL} Rep subfields.

## Slide 8: Actions
Remove Secure LTF Support[ed] subfield from the Ranging Parameters field of the Ranging Parameters element.
Rename Secure LTF Required subfield to Secure LTF Required/Enabled subfield.

## Slide 9: Straw Poll
We support the following:
  Remove Secure LTF Support[ed] subfield from the Ranging Parameters field in the Ranging Parameters element.
  Rename Secure LTF Required subfield to Secure LTF Required/Enabled subfield.
Y: N: Abstain:

## Slide 10: Backup