## Slide 1: Phase Rotation for 320MHz
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinmin Kim |  |  |  | jinmin1230.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com

## Slide 2: Introduction
Several contributions discussed a preamble structure for 11be and most of them considered PPDUs starting with the legacy preamble for coexistence with legacy devices [1-3]
Conventional Wi-Fi systems including 11ax apply phase rotation to the legacy preamble to reduce PAPR
Phase rotation can be definitely employed in 11be as well, and thus, a new design is required for 320MHz PPDUs
This contribution first discusses what we need to consider to come up with the phase rotation, and then, proposes three design options

## Slide 3: Consideration Points (1/2)
Design metric
  Phase rotation needs to be designed to reduce PAPR
  PAPR for L-STF,L-LTF or L-SIG parts can be considered
Preamble puncturing
  Preamble puncturing can be considered in 11be similar to 11ax MU PPDU to enhance the efficiency
  Whatever the size of the preamble puncturing unit, various puncturing patterns can be created in 320MHz PPDUs and each pattern may lead to different PAPR
  We need to find unified phase rotation values which minimize the worst PAPR by considering various preamble puncturing cases
  We can consider redesigning the phase rotation values even in 80 / 160MHz (1~2 dB lower PAPR can be achieved)

## Slide 4: Consideration Points (2/2)
RF capability regarding the bandwidth
  11be may support 160+160 / 320 MHz as new bandwidth modes and PPDUs for those bandwidth can be transmitted using two RFs which can deal with up to 160MHz bandwidth or one RF which can generate 320MHz PPDU
  Each part generated by different RFs may have different PAPR
  We need to find unified phase rotation values which minimize the worst PAPR by considering diverse RF capabilities
5 null
12 left guard
2x2020
5 null
23 DC
11 right guard
320MHz capable RF
160MHz capable RF
160MHz capable RF

## Slide 5: Design Options
Option 1
  Repeat 11ax / new 80MHz phase rotation
    [1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1]
  The coefficients in all 80MHz segments remain the same but it may cause somewhat high PAPR (Please see Appendix)
Option 2
  Repeat 11ax / new 80MHz phase rotation and apply additional phase rotation to each 80/160MHz segment
    [a*[1 -1 -1 -1] b*[1 -1 -1 -1] c*[1 -1 -1 -1] d*[1 -1 -1 -1]]
    Coefficients of a, b, c and d can be selected out of 1, -1, i and -i for simplicity
  Relatively low PAPR can be expected (about 1~3dB reduced)
Option 3
  Find optimal phase rotation for each 20MHz channel
    Each coefficient can be selected out of 1, -1, i and -i for simplicity
  Lowest PAPR can be achieved (about 3~4dB reduced) but each 80MHz segment may have totally different coefficients

## Slide 6: Summary
We have discussed the phase rotation for 320MHz in 11be
Two consideration points have been presented
  Preamble puncturing
  RF capability
Three design options have been presented
  Repeat 11ax / new phase rotation
  Repeat 11ax / new phase rotation and apply additional phase rotation
  Find optimal phase rotation

## Slide 7: Straw Poll #1
Do you agree to add the following to the TGbe SFD?
  Phase rotation is applied to the legacy preamble part of EHT PPDU
    Coefficients applied to each 20MHz channel are TBD
    Application to the other fields is TBD
Y/N/A: //

## Slide 8: Straw Poll #2
Do you agree to redesign phase rotation applied to the legacy preamble part of 80/160/80+80MHz EHT PPDU?
Y/N/A: //

## Slide 9: Straw Poll #3
Which option do you prefer for the phase rotation applied to the legacy preamble part of 320/160+160 MHz EHT PPDU?
  Option1
    Repeat 11ax / new 80MHz phase rotation
  Option2
    Repeat 11ax / new 80MHz phase rotation and apply additional phase rotation to 80/160 MHz segment
  Option3
    Optimal phase rotation
Option1/Option2/Option3/None of them/Abstain:

## Slide 10: References
[1] 802.11-19/1099r0 Preamble Structure
[2] 802.11-19/1142r0 Discussion on the preamble for 11be
[3] 802.11-19/1214r0 Preamble Design Consideration for 11be

## Slide 11: Appendix
PAPR when the 11ax 80MHz phase rotation is repeated
  4 times IFFT is applied
  80MHz: [1 -1 -1 -1]
  160MHz: [1 -1 -1 -1 1 -1 -1 -1]
  320MHz: [1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1 1 -1 -1 -1]
Bandwidth | Full bandwidth (PAPR) |  | Preamble puncturing (max PAPR) | 
 | L-STF | L-LTF | L-STF | L-LTF
80MHz | 4.4380 | 5.3962 | 6.8606 | 7.9370
160MHz | 5.9144 | 6.4716 | 9.8709 | 10.9473
320MHz | 8.2600 | 9.1864 | 12.8812 | 13.9576
Unit: dB