## Slide 1: EHT Power saving considering multi-link
Date: 2019-09-15
Authors:
Name | Affiliations | Address | Email
Jeongki Kim | LG Electronics | LG Seocho R&D Campus, Korea | jeongki.kim@lge.com
Suhwook Kim |  |  | suhwook.kim@lge.com
Jinsoo Choi |  |  | js.choi@lge.com
Insun Jang |  |  | insun.jang@lge.com
Sungjin Park |  |  | allean.park@lge.com
Taewon Song |  |  | taewon.song@lge.com

## Slide 2: Introduction
PAR for TGbe [1]
  5.5 Need for the Project:
    …
    With the high throughput and stringent real-time delay requirements of these applications, users expect enhanced throughput, enhanced reliability, reduced latency and jitter, and improved power efficiency in supporting their applications over WLAN.
In this contribution, we propose the enhanced power saving mechanism for EHT STAs in 11be

## Slide 3: Background
Operating Mode (OM) Control in 11ax [2]
  Non-AP STA can inform its AP of the bandwidth and number of spatial stream to receive the DL PPDU or transmit the UL PPDU by using OM Control field
  AP sends DL frame to the STA based on the requested Receive Operating Mode Indication (ROMI) and allocates the UL resource to the STA based on the requested Transmit Operating Mode Indication (TOMI)
  Example of ROMI
STA
AP
UL Data
BA
Rx NSS =2, Rx BW= 40MHz
RX
RX
RX
DL Data
BA
TX
STA requests new Rx NSS=1, Rx BW=20MHz
STA receives BA using
Rx NSS=2, Rx BW=40MHz
Rx NSS=1, Rx BW=20MHz
Accept
AP sends DL Data with new changed Rx values
(Rx NSS=1, Rx BW=20MHz)

## Slide 4: Background
TWT operation in 11ax [2]
  Individual TWT: Non-AP STA wakes up every TWT service period negotiated with TWT REQ&RSP and sends/receives the frames with the associated AP
    The STA can enter the doze state until its TWT SP
  Broadcast TWT: Non-AP STA obtains the TWT information from the received Beacon every its TBTT negotiated with TWT REQ&RSP
    The STA can enter the doze state until the TBTT or its TWT service period
TWT req
TWT rsp
TWT SP
STA(1..n)
AP
Trigger
PS-Poll
M-BA
DL MU PPDU
BA
Doze

## Slide 5: Background
Intra-PPDU Power save in 11ax [2]
  When an HE non-AP STA receives a PPDU, the STA can enter the doze state until the end of the PPDU if the PPDU is determined as Intra-BSS PPDU using the following field
    In HE-SIGs: BSS Color, UL/DL flag, STA ID
    In VHT-SIG: Partial AID of UL PPDU
    In MAC header: MAC address fields (e.g., RA, TA, BSSID)
Legacy Preamble
(L-SIG)
HE Preamble
(RL-SIG, SIG-A, …)
PSDU
BSS Color, UL/DL Flag, STA_ID
Doze State

## Slide 6: Motivation
One of main features in TGbe is multi-band/multi-link operation [1], [3]~[8]
  A single device can support the multiple links and the data of the device can be delivered to another device through the multiple links
  Multi-link feature can increase the peak/average throughput of the device but require more complexity, cost, or power of the device
In this contribution we propose some enhanced power saving mechanisms considering multi-link feature
Device(/MLLE) A
Device(/MLLE) B
Link 1
Link 2
Data 1
Data 2
Data 3
Data 4

## Slide 7: OM Control for multi-link
When an EHT STA supporting the multi-link wants to reduce its power consumption, the STA can request to disable the other link(s) within the same MLLE* to its AP
The STA can request to enable the disabled links when the STA wants it
Link 1
Link 2
UL frame
BA
STA requests to disable Link 2
After receiving BA, link2 is disabled
BA
Link 1
Link 2
UL frame
AP MLLE
STA MLLE
Link 1 &2 are enabled
UL frame
BA
Disabled
DL frame
BA
Accept
* Multi-link logical entity [6]

## Slide 8: TWT operation for multi-link (1/2)
A STA can setup the TWT SPs for multi-links through a link
The TWT operation can be performed in partial links (e.g., only one link) among multiple links in a non-AP MLD (i.e., STAs for the other links enter in doze state)
STA/Link 1
STA/Link 2
Non-AP MLD
TWT setup (link1&2)
TWT SP
TWT SP
TWT SP
TWT SP
STA/Link 1
STA/Link 2
Non-AP MLD
TWT setup (only STA 1, doze state for STA2)
TWT SP
TWT SP
Power saving (e.g.,
doze state)
Power saving (e.g.,
doze state)

## Slide 9: TWT operation for 11be (2/2)
An AP within AP MLD can send a non-AP STA within a non-AP MLD a frame to wake up other non-AP STA(s) within the same non-AP MLD
A non-AP STA within an non-AP MLD can also send its associated AP a frame to indicate that other non-AP STA(s) within the same non-AP MLD is awake state currently
STA/Link 1
STA/Link 2
STA MLD
TWT setup (only STA 1,
Doze for STA2)
TWT SP
AP/Link 2
AP/Link 1
AP MLD
PS-Poll
DL frame
Wake up STA2
Awake
DL frame
DL frame
Power saving (e.g.,
doze state)
ACK

## Slide 10: Intra-BSS PPDU PS for 11be
When an AP sends EHT PPDU via only a link, the AP can indicate if the other link (s) is (are) available or not
The other link (s) of AP may not be available because
  Intra-BSS STA sends UL frame to the AP via the other link
  OBSS STA sends a frame via the other link and thus the strong interference exists
In that case, Intra-BSS STAs can enter the doze state until the end of DL frame
Link 1
Link 2
STA
Link 2
Link 1
AP
Doze state of STA for link 2
DL frame TX
UL frame RX
Unavailability of link 2
Power saving (e.g.,
doze state)

## Slide 11: Conclusion
We need to consider the power efficiency of EHT STAs for 11be
We proposed some enhanced power saving mechanisms considering the multi-link concept
  OM Control
  TWT operation
  Intra-BSS PPDU Power save

## Slide 12: Reference
[1] 11-18/1231r6, EHT Proposed PAR
[2] Draft P802.11ax D4.3
[3] 11-18/1171, View on EHT objectives and technologies
[4] 11-18/1525, EHT features for Multi-Band Operation
[5] 11-18/1908, Overview of Full Duplex over Multi- Band (FD-MB) for EHT
[6] 11-19/773, Multi-link Operation Framework
[7] 11-19/777, Performance on Multi-band Operation
[8] 11-19/823, Multi-Link Aggregation

## Slide 13: Straw Poll 1
Do you agree to add the following into the TGbe SFD?
  A STA within a non-AP MLD can send its associated AP a request frame to request the TWT Service Period(s) for other link(s) within the same non-AP MLD
  An AP within an AP MLD can send a STA within a non-AP MLD a response frame including the information for TWT Service Period(s) for other link(s) within the same non-AP MLD in response to the request frame if the AP receives the request frame from the STA

## Slide 14: Straw Poll 2
Do you agree to add the following into the TGbe SFD?
  An AP within AP MLD can send a non-AP STA within a non-AP MLD a frame to wake up other non-AP STA(s) within the same non-AP MLD that has(have) entered doze state
  If a STA within a non-AP MLD receives a frame to wake up other STA(s) within the same non-AP MLD that has(have) entered doze state, the other STA(s) indicated by the frame shall transition from doze state into awake state

## Slide 15: Straw Poll 3
Do you agree to add the following into the TGbe SFD?
  A non-AP STA within an non-AP MLD can send its associated AP a frame to indicate that other non-AP STA(s) within the same non-AP MLD that has(have) entered doze state is(are) in awake state currently