## Slide 1: 11be Preamble Structure
Date: 09/15/19
Name | Affiliation | Email
Xiaogang Chen | Intel | Xiaogang.c.chen@intel.com
Qinghua Li |  | 
Feng Jiang |  | 
Minyoung Park |  | 
Kenney Thomas |  | 
Laurent Cariou |  | 
Stacey Robert |  | 
Authors:

## Slide 2: Outline
Recap of the 11be preamble design;
Structure of the 11be preamble;
Auto-detection;
Summary.

## Slide 3: Recap of the 11be preamble design
The 11be preamble design was discussed in [1][2][3][4][5].
Takeaways from [1~5]:
  Reuse (or simply extend) existing functions in the legacy WiFi system, instead of re-developing similar functions in every new WiFi generation;
  The features developed in 11be can be leveraged by 11be beyond;
Considerations in 11be: Minimize the efforts on the preamble development, and focus more on the features that improve the WiFi user experience.

## Slide 4: 11be Preamble Structure - Overview
    11be reuse the 11ax preamble up to RL-SIG;
    Add Pre-SIG field after RL-SIG;
    EHT Preamble (EHT-SIG, EHT-STF, EHT-LTF) follows Pre-SIG;
    Keep the per 20MHz repetition up to Pre-SIG (may extend to EHT-SIG).

## Slide 5: 11be Preamble Structure - Legacy preamble & RL-SIG
Use the same structure as 11ax;
  Keep legacy fields for backward compatibility;
  Keep L-SIG and RL-SIG structure;
    Reuse the auto detection mechanism developed in 11ax;
    For range extension.

## Slide 6: 11be Preamble Structure - Pre-SIG (1/2)
The Pre-SIG is perpetual, and has fixed structure since 11be;
Future proof and stabilize the WiFi preamble[1,2,3,4];
  E.g. introducing version ID to simplify the auto-detection;
  No need to revisit the auto-detection and PPDU type detection in every generation.
Cross-generation coexistence [2,5];
  The Coex info can be decoded/parsed by 11be STA and post-11be STA;
  STAs of different WiFi generations can enjoy the same feature.

## Slide 7: 11be Preamble Structure - Pre-SIG (2/2)
Anticipation of the contents in the Pre-SIG:
  Wifi version independent info:
    Wifi version: 3 or 4 bits;
    DL/UL: 1 bit;
    BSS Color: >= 6 bits;
    TxOP: >= 7 bits;
    CRC: >=4;
    Tail: 6 bits;
    Total: >= 27 bits
  Wifi version dependent info:
    PPDU format: 3 bits;
    MCS, SS, coding, etc.
Propose to use 2 symbols in Pre-SIG
  2 symbols is roomy even the group decide to extend the size of BSS color and TxOP;
  Any residual version dependent info that cannot fit in the Pre-SIG can be carried by the EHT-SIG.

## Slide 8: Auto-detection (1/2)
RL-SIG has done most work on auto-detection already;
  Only need to differentiate 11be and 11ax.
Design principles for auto-detection:
  Maximum reuse the tools already supported in legacy WiFi;
    Reduce the HW for preamble detection.
  Enable early indication to gain buffer time for AGC.

## Slide 9: Auto-detection (2/2)
Opt 1): LENGTH field in L-SIG/RL-SIG (e.g. LENGTH%3 == 0);
  Reuse 11ax processing;
  Enable early indication for the 11be STA.
Opt 2): Mask of the RL-SIG.
  A good approach for early indication;
  But need extra correlator for the mask.

## Slide 10: Summary
Agree with the design principles of the 11be preamble in [1~5];
  Propose to add Pre-SIG after RL-SIG to achieve the design goals.
Discussed the auto-detection mechanism, and proposed to leverage the LENGTH field plus RL-SIG for auto-detection.

## Slide 11: SP 1
Do you agree that 11be keeps the RL-SIG fields (repeated L-SIG) after L-SIG?

## Slide 12: SP 2
Do you agree to add a Pre-SIG field right after the RL-SIG in 11be?
Note 1: The contents of the Pre-SIG are TBD.
Note 2: The Pre-SIG field is used for (but not limited to):
1) future proof: e.g. differentiates different wifi version beyond 11be;
2) feature sharing between different wifi generations: e.g. share the spatial reuse feature between 11be and 11be beyond.

## Slide 13: SP 3
Do you agree that the Pre-SIG field has two OFDM symbols and each symbol has the same duration as RL-SIG?

## Slide 14: References
[1] 11-19/1021, Preamble Design Harmonization.
[2] 11-19/1085, High-level EHT Preamble Structure.
[3] 11-19/1099, Preamble structure in 11be.
[4] 11-19/1142, Discussion on the preamble for 11be.
[5] 11-19/1214, Preamble Design Consideration for 802.11be.