## Slide 1: TDD beamforming configuration
Date: 2019-09-18
Name | Affiliation | Address | Phone | Email
Payam Torab | Facebook |  |  | torab@ieee.org
Djordje Tujkovic |  |  |  | djordjet@fb.com
Krishna Gomadam |  |  |  | kgomadam@fb.com
Lakshmi Pradeep |  |  |  | lpradeep@fb.com

## Slide 2: TDD beamforming Background
TDD beamforming operations other than Initial Beamforming* are referred to as Beam Measurement in the standard
Before Draft 4.0, these operations were exclusively initiated by (and results reported to) SME
  Requiring connection to (proprietary) network controller
  For client devices (non-AP STAs) connection to (proprietary) controller is undesirable
    Proprietary connection (software) impedes commercialization
We review some TDD beam measurements operations for some gaps

## Slide 3: TDD beamforming Background
Proprietary
Network Controller
802.11ad PHY
802.11ad|ay MAC
Proprietary Management
802.11ad PHY
802.11ad|ay MAC
Proprietary Management
Standard
Standard
Proprietary
Proprietary
management port
Proprietary
management port
DN (AP)
CN (non-AP)
Proprietary
Network Controller
802.11ad PHY
802.11ad|ay MAC
802.11 Management
802.11ad PHY
802.11ad|ay MAC
802.11 Management
Standard
Standard
Standard
Proprietary
management port
DN (AP)
CN (non-AP)
Before Draft 4.0
Standard 802.11ay MAC plus some proprietary functions
DNs and CNs requiring proprietary software
Improvement
Standard 802.11ay MAC including standard management functions
DNs requiring proprietary software
CNs 60 GHz operation entirely specified by 802.11 (no need for proprietary software)
CN with standardized data plane and management plane
TDD Sector Config

## Slide 4: Example -- Periodic beamforming (PBF)
Example implementation
Initiator transmitting on different Tx beams during beamforming slot every 400 µs, cycling through all Tx beams (Note 1)
Transmission pattern repeated 31 times, with responder measuring on a different receive beam during each transmit cycle
Responder reporting the result through the controller
Notes
Equivalent to an 802.11ad I-TXSS (directional receive)
Some or all of Tx beams can be the same, e.g., for averaging
Knowing the TDD SSW multiplicity can help with averaging decisions
Set of Rx beams can be null to leave the Rx selection to responder
Generalized
Initiator trying Ntx transmit beams against Nrx responder’s receive beams, during periodic or irregular (but scheduled) beamforming slots (Nrx = 1 for current implementation)
Initiator trying a generally different Tx Beam at every new Beamforming slot (taking Ntx slots for Tx sweep) (Note 2)
Responder receiving on each Rx beam Ntx times, so it can try them against all different Tx beams
Start time pointing to start of the first beamforming slot used for operation; schedule assumed consistent with beamforming pattern and duration
Allow TDD SSW Feedback and TDD SSW Ack, with option to skip
Responder sends SNR report to initiator through TDD Route IE (TDD Sector Feedback subelement)
Initiator does not send a SNR report
Initiator MLME (and TDD Sector Config fields)
Start time
Period P or schedule (already provided)
TDD SSW multiplicity (Note 3)
Set of Rx beams (Note 4)
Non-AP (CN) can also be the initiator
Can be locally decided by non-AP, or administered through the AP/controller
Decided by non-AP: Send up the request (same arguments minus the schedule), get acknowledgement, schedule, start time (exchange of TDD Sector Config subelement)
Decided by AP: Same as runtime Rx calibration, except Tx beam selection is left to non-AP (see the runtime Rx calibration slide)

## Slide 5: Example – Transmit beam calibration
Example implementation
Initiator transmitting on generally different Tx beams during beamforming slot every 400 µs (Note 1, 2)
Responder measuring signal in corresponding beamforming slots using the current Rx beam
Responder reporting the result through the controller
Notes
Equivalent to an 802.11ad I-TXSS (directional receive)
Some or all of Tx beams can be the same, e.g., for averaging
Knowing the TDD SSW multiplicity can help with averaging decisions
Set of Rx beams can be null to leave the Rx selection to responder
Generalized
Initiator trying Ntx transmit beams against Nrx responder’s receive beams, during periodic or irregular (but scheduled) beamforming slots (Nrx = 1 for current implementation)
Initiator trying a generally different Tx Beam at every new Beamforming slot (taking Ntx slots for Tx sweep) (Note 2)
Responder receiving on each Rx beam Ntx times, so it can try them against all different Tx beams
Start time pointing to start of the first beamforming slot used for operation; schedule assumed consistent with beamforming pattern and duration
Allow TDD SSW Feedback and TDD SSW Ack, with option to skip
Responder sends SNR report to initiator through TDD Route IE (TDD Sector Feedback subelement)
Initiator does not send a SNR report
Initiator MLME (and TDD Sector Config fields)
Start time
Period P or schedule (already provided)
TDD SSW multiplicity (Note 3)
Set of Rx beams (Note 4)
Non-AP (CN) can also be the initiator
Can be locally decided by non-AP, or administered through the AP/controller
Decided by non-AP: Send up the request (same arguments minus the schedule), get acknowledgement, schedule, start time (exchange of TDD Sector Config subelement)
Decided by AP: Same as runtime Rx calibration, except Tx beam selection is left to non-AP (see the runtime Rx calibration slide)

## Slide 6: Example – Rx Beam calibration
Example implementation
Initiator trying generally different Rx beams during each beamforming slot every 400 µs (Note 1, 2)
Responder transmitting TDD SSW frames in corresponding beamforming slots on the current Tx beam
Initiator reporting the result through the controller
Notes
Equivalent to an 802.11ad I-RXSS
Some or all of Rx beams can be the same, e.g., for averaging
Initiator specifying the TDD SSW multiplicity to control averaging decisions
Set of Rx beams can be null to leave the Rx selection to responder
Generalized
Initiator trying Nrx receive beams against Ntx responder’s transmit beams, during periodic or irregular (but scheduled) beamforming slots (Ntx = 1 for current implementation)
Initiator trying a generally different Rx Beam at every new Beamforming slot (taking Nrx slots for Rx sweep) (Note 2)
Responder transmitting on each Tx beam Nrx times, so initiator can try them against all different Rx beams
Start time pointing to start of the first beamforming slot used for operation; schedule assumed consistent with beamforming pattern and duration
Allow TDD SSW Feedback and TDD SSW Ack, with option to skip
No SNR report exchanged
Initiator MLME (and TDD Sector Config fields)
Start time
Period P or schedule (already provided)
TDD SSW multiplicity (Note 3)
Set of Tx beams (Note 4)
Non-AP (CN) can also be the initiator
Can be locally decided by non-AP, or administered through the AP/controller
Decided by non-AP: Send up the request (same arguments minus the schedule), get acknowledgement, schedule, start time (exchange of TDD Sector Config subelement)
Decided by AP: Same as runtime Tx calibration, except Rx beam selection is left to non-AP (see the runtime Tx calibration slide)

## Slide 7: Example – Interference measurement
Example implementation
Initiator transmitting on generally different Tx beams during beamforming slot every 400 µs (Note 1, 2)
  Broadcast RA for TDD SSW frames
Multiple responders measuring signal in corresponding beamforming slots using their current Rx beams
  With invert scan polarity measurement slots are sometimes scheduled in the Tx subframe (i.e., where the device is normally expected to transmit) (supported by Slot Schedule IE general format, no standard change needed)
Responders reporting the result through the controller
Any device can be the initiator (DN or CN)
No notion of BSS association for different responders (network-level operation)
Notes
Sweep can be repeated (is ended administratively)
Some or all of Tx beams can be the same, e.g., for averaging
Responder knowing the TDD SSW multiplicity can help with averaging decisions
Set of Rx beams can be null to leave the Rx selection to responder
TDD Sector Config exchange for another TA not in BSS
Generalized
Number of beamforming slots in the schedule given to initiator does not have to be a multiple of number of scanned Tx beams
  For example, 100 slots may be allocated for interference scan using 31 Tx beams
Different responders schedules (and obviously Rx beams)(this is more generalizing the procedure than generalizing any protocol)
  For example, one responder scanning during a portion of the 100 slots in the above example, while another responder scanning during the entire 100 slots
Initiator or AP MLME (and TDD Sector Config fields)
Start time
Period P or schedule (already provided)
TDD SSW multiplicity (Note 3)
Set of responders
Set of Rx beams (Note 4)
TA address (Note 5)
Non-AP (CN) can also be the initiator
Can be locally decided by non-AP, or administered through the AP/controller
Decided by non-AP: Send up the request (same arguments minus the schedule, plus list of responders (e.g., some of RAs that have been received), get acknowledgement, schedule, start time (exchange of TDD Sector Config subelement)
Decided by AP or another STA outside BSS (request coming to AP through the controller): MLME/AP config parameters above

## Slide 8: Coordinated beamforming – Transmit training
Example implementation
Network level interference nulling operation involving an aggressor link and multiple victim links: Finding the Tx beam with least interference to multiple victims
Initiator (on aggressor link) transmitting on generally different Tx beams during beamforming slot every 400 µs (Note 1, 2)
Multiple responders (on multiple victim links) receiving on a given Rx beam during beamforming slots allocated to them (with invert scan polarity sometimes this may happen in the opposite subframe)
Responders reporting the result through the controller
Any device can be the initiator (DN or CN)
No notion of BSS association for different responders (network-level operation)
Aggressor link
ATX (initiator)
ARX
Victim link 1
VTX1
VRX1
Victim link 2
VTX2
VRX2
Initiator or AP MLME (and TDD Sector Config fields)
Start time
Period P or schedule (already provided)
TDD SSW multiplicity (Note 3)
Set of responders
Set of Rx beams (Note 4)
TA address (Note 5)
Non-AP (CN) can also be the initiator
Probably can be administered through the AP/controller only (under study)
Generalized
Number of beamforming slots in the schedule given to initiator does not have to be a multiple of number of scanned beams
  For example, 100 slots may be allocated to scan 31 Tx beams
Different receive schedules (and Rx beams) for each victim link (this is more generalizing the procedure than generalizing the protocol)
  For example, one responder receiving during a portion of the 100 slots in the above example, while another responder receiving during the entire 100 slots
Notes
Sweep can be repeated (is ended administratively)
Some or all of Rx beams can be the same, e.g., for averaging
Knowing the TDD SSW multiplicity can help with averaging decisions
Set of Rx beams can be null to leave the Rx selection to responder
TDD Sector Config exchange for another TA not in BSS
Operation is runtime Tx calibration on aggressor (responders receiving on constant receive beams) + TA filtering

## Slide 9: Coordinated beamforming – Rx training (Rx CBF)
VRX
(initiator)
Example implementation
Network level interference nulling operation involving multiple aggressor links and a victim link: Finding the Rx beam with least interference from multiple aggressors
Initiator (on victim link) receiving on generally different Rx beams during beamforming slot every 400 µs (Note 1, 2)
Multiple responders (on multiple aggressor links) transmitting on a given Tx beam during beamforming slots allocated to them (with invert scan polarity sometimes this may happen in the opposite subframe)
Initiator reporting the result through the controller
Any device can be the initiator (DN or CN)
No notion of BSS association for different responders (network-level operation)
Victim link
VTX
Aggressor link 1
ATX1
ARX1
Aggressor link 2
ATX2
VRX2
Initiator or AP MLME (and TDD Sector Config fields)
Start time
Period P or schedule (already provided)
TDD SSW multiplicity (Note 3)
Set of responders
Set of Rx beams (Note 4)
TA addresses (Note 5)
Non-AP (CN) can also be the initiator
Probably can be administered through the AP/controller only (under study)
Generalized
Number of beamforming slots in the schedule given to initiator does not have to be a multiple of number of scanned beams
  For example, 100 slots may be allocated to scan 31 Rx beams
Different transmit schedules (and Tx beams) for each aggressor link (this is more generalizing the procedure than generalizing the protocol) (Note 7)
  For example, one responder transmitting during a portion of the 100 slots in the above example, while another responder transmitting during the entire 100 slots
Notes
Sweep can be repeated (is ended administratively)
Some or all of Rx beams can be the same, e.g., for averaging
Knowing the TDD SSW multiplicity can help with averaging decisions
Set of Rx beams can be null to leave the Rx selection to responder
TDD Sector Config exchange for other TAs not in BSS
Operation is runtime Rx calibration on victim (responders transmitting on constant transmit beams) + TA filtering
Interference measurement with simultaneous transmission is problematic – 802.11ad/ay directional channel measurement (ANIP and RSNI) with TDD extensions may be applicable

## Slide 10: Next step Enhancing the TDD Sector Config subelement
Add more information about
  Sweeping pattern/schedule
  Information from outside the BSS
    For example, list of aggressor TA addresses during Rx CBF