## Slide 1: Forward Compatibility for WiFi Preamble Design
Date: 2019-09-15
Authors:
Name | Affiliations | Address | Phone | Email
Sameer Vermani | Qualcomm |  |  | 
Alice Chen |  |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Notes: September 2012

## Slide 2: Abstract
Traditionally, WiFi preamble design has only focused on backward compatibility
These slides are a continuation of the ideas proposed in [1], and propose to bring forward compatibility to WiFi preambles (in the main-stream WiFi bands) starting with 802.11be
  Desire to solve the auto-detection issue for all future standards starting with EHT, once and for all
  Better coexistence than just L-SIG based deferral among future generations of 802.11 through universal fields

## Slide 3: Introduction
Historically, 802.11 preambles of every PHY version contain following types of information
  Information needed by intended receivers
    E.g., Nss, MCS, Coding etc.
  Basic Co-existence info for by-standers of previous PHY versions
    L-SIG duration
  Richer Co-ex info (medium re-use or power save) for by-standers of current PHY version
    E.g., BSS Color, UL/DL bit and TxOP fields in 802.11ax
Hitherto, information of type 3 is not understood by previous generations
  E.g., 11ac devices do not understand BSS Color and TxOP in SIG fields of 802.11ax packets
  Only basic L-SIG duration based co-existence is achieved
Better future compatibility starting with 802.11be
  Richer co-existence among future WiFi versions starting with 11be
    E.g. 11be devices will respond in a more sophisticated way (compared to just L-SIG based deferral) to the PHY version(s) after that

## Slide 4: Forward compatibility: Universal Fields (1)
Fix the preamble ‘structure’ across multiple 802.11 generations for at-least a few symbols after legacy preamble
  Starting with EHT
  ‘Structure’ here means the number of OFDM symbols and encoding method
  Legacy preamble and a ‘Pre-SIG’
Have some universal fields in the ‘structurally-common’ preamble section for all standards, EHT and beyond
  Version independent fields whose presence is independent of the standard version (11be/bf/bg…)
    All devices compliant with EHT or beyond standards can count on this information being present
    At a known location in Pre-SIG
  For example BSS Color, TxOP etc
Legacy preamble
(may include RL-SIG)
Common structure for EHT and beyond
802.11be preamble
Pre-SIG
Pre-SIG contains
universal fields
at certain fixed locations

## Slide 5: Forward compatibility: Universal Fields (2)
We think of universal fields as fields satisfying the following properties
  Presence and location is independent of PHY version
    Same for 11be/11bf/11bg etc…
  Mainly used for better co-existence among 802.11 generations starting from 11be
    Should be useful for by-stander devices of multiple generations
Based on above, good candidates for universal fields are
  PHY Format Identifier (Same as PHY Version Identifier proposed in [1])
    Value of the format identifier field differentiates between different WiFi versions starting with EHT
    Auto-detection problem of multiple WiFi generations gets solved together
  TxOP duration
  BSS Color
  UL/DL flag
PPDU type (MU/SU/Trigger-based/ER/) may not be a good candidate for universal fields because
  Every PHY version might have a different set of PPDU types
  This information is mainly useful for intended receivers and not by-standers

## Slide 6: Thoughts on the Pre-SIG field -I
Ideally, the universal information should be localized to just the pre-SIG
  Don’t want universal fields to be scattered in multiple parts of the preamble
One symbol does not seem to be enough
  If we have BSS Color (>=6 bits), TxOP (>=7 bits), UL/DL flag and PHY Format Identifier (>=3), adds up to a minimum of 17 bits
  With CRC (>=4 bits) and 6 bits tail, already exceeds the bit carrying capacity of 1 symbol
Three symbols (encoded together) might become a performance bottle neck (in outdoor channels)
Two symbols seems to achieve a reasonable balance
L-STF
L-LTF
L-SIG
EHT SIG fields
RL SIG
Pre- SIG
Common structure for EHT and beyond

## Slide 7: Thoughts on the Pre-SIG field -II
Pre-SIG will be sent on 26 data tones (just like HE-SIG-A)
  Extra tones will be added to L-SIG and RL-SIG for channel estimation
  Leaving aside tail and CRC, 2 symbols offer a bit carrying capacity of <=42 bits
42 bits seems like an overkill for universal fields alone
  Need to manage preamble overhead; can’t be profligate with bits in preamble
    Try to keep extra overhead of 11be to one symbol
  Can incorporate version dependent fields (e.g. MCS, Nss etc) in the pre-SIG
Propose a mix of universal and version-dependent fields in a 2 symbol pre-SIG
  ER mode (need for which is TBD) may need a longer pre-SIG
L-STF
L-LTF
L-SIG
EHT SIG fields
RL SIG
Pre- SIG
2 symbols jointly encoded.
Contains universal and
version dependent fields
Common structure for EHT and beyond

## Slide 8: Summary
We proposed to bring future compatibility to WiFi preambles starting with 802.11be
  Solve the auto-detection issue for multiple standards starting with EHT, together
  Better coexistence than just L-SIG based deferral among future generations of 802.11
Have a structurally common portion of the preamble for multiple WiFi generations starting with 802.11be
  Legacy preamble followed by a Pre-SIG
  The Pre-SIG contains universal fields which are version independent
Proposed a 2 symbol Pre-SIG with a mix of universal (version independent) and version dependent fields

## Slide 9: Straw-poll 1
Do you agree with introducing “universal fields” in the EHT preamble ?
  The intent of the universal fields is to allow for certain “version independent” content for better co-existence among future 802.11 generations
  The exact field definition, location and number of bits are TBD

## Slide 10: Straw-poll 2
Do you agree to incorporate a PHY format identifier field as one of the universal fields in the EHT preamble?
  The intent is to simplify auto-detection for future 802.11 generations
  Size of this field is TBD

## Slide 11: Straw-poll 3
Do you agree to have a 2 OFDM symbol long, jointly encoded SIG field in the EHT preamble immediately after RL-SIG ?
  This SIG field will have universal fields
  Extended Range Mode is TBD
  The name for this field can be chosen in future based on consensus in the group

## Slide 12: Straw-poll 4
Do you agree that the SIG field immediately after the RL-SIG will be sent using 52 data tones and 4 pilot tones per-20MHz?

## Slide 13: Straw-poll 5
Do you agree that the SIG field immediately after the RL-SIG can have some version dependent fields as well?

## Slide 14: Motion 1
Move to add the following to the spec-framework document
  The EHT preamble will have universal fields. The intent of the universal fields is to carry “version independent” content for better co-existence among future 802.11 generations.
  PHY version identifier field shall be one of the universal fields in the EHT preamble
    Purpose is to simplify auto-detection for future 802.11 generations, i.e, value of this field is used to identify the exact PHY standard version starting with 802.11be
    Size and exact location of this field is TBD
  The definition, location and number of bits for other universal fields is TBD

## Slide 15: Motion 2
Move to add the following to the spec-framework document
  There shall be a 2 OFDM symbol long, jointly encoded SIG field in the EHT preamble immediately after RL-SIG
    This SIG field will contain universal fields
    In addition, this SIG field can have some version dependent fields
    The size of this SIG field for the case of an Extended Range Mode (if such a mode were to be adopted) is TBD
    This SIG field will be sent using 52 data tones and 4 pilot tones per-20MHz
    The name for this SIG field will be chosen in the future based on consensus in the group

## Slide 16: References
[1] Sameer Vermani et al, “Preamble Design Harmonization” , IEEE Document 11/19-1021r1