## Slide 1: Latency enhancement for EHT
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Taewon Song |  |  |  | taewon.song@lge.co
Sungjin Park |  |  |  | allean.park@lge.com

## Slide 2: Abstract
Supporting low latency traffic is major goal of communication technology these days
  We have adopted OFDMA in IEEE 802.11ax, thus an AP can manage data transmission in DL and UL both side
  However, some studies have shown that the OFDMA in 11ax may be not sufficient to support the extremely low latency traffic
So we will discuss how we support low latency traffic in EHT

## Slide 3: Low Latency Queue
There were submissions that suggested new queue for low latency traffic [1][2]
Also IEEE 802.11aa defines intra-AC prioritization
  It provides six transmit queues and gives more priorities to AV streams or voice streams
  VO(VI) and alternative VO(VI)
  share each EDCAF and has same
  EDCA parameters

## Slide 4: Low Latency Queue
If we define a new EDCA or revise current EDCAF for low latency traffic, we may reuse 11aa feature
  We may use shorter IFS, different EDCA parameters for low latency EDCAF
  Contention free access such as HCCA, TB-access
  can be considered for low latency
  These new or revised channel
  access rules can be used for
  reducing latency in the worst case

## Slide 5: Low Latency Queue
The low latency queue/EDCAF may have following characteristics
  Temporarily activated/terminated
  Only buffered by deterministic traffic
  Operate differently in the worst case scenario
  Detail operation should be negotiated between AP and STA

## Slide 6: Worst case handling
Improving worst case latency and jitter is one of our scope in PAR document
Following features may be defined to improve worst case latency
  Sensing/prediction: It is important for a STA/AP to quickly recognize/predict the worst case
  Prevention: AP may allocate redundant resource to prevent the worst case
  Transmission: If the worst case has occurred, exceptionally new transmission rule can be used under a specified condition
Notes: 그림: Worst case 를 위해 Resource를 미리 할당하는 것

## Slide 7: Worst case handling
If the STA joins UL OFDMA by trigger-based access, it shall follow MU EDCA parameters instead of EDCA parameters
  However, the STA may fail to transmit data within bounded latency when the worst case has occurred because MU EDCA parameters are not optimized for latency
  So we may need to define new transmission rule for worst case

## Slide 8: OFDMA enhancement
OFDMA which has been adopted in 11ax is a powerful tool for supporting latency traffic because AP can manage DL and UL transmission
  However, current OFDMA may need more enhancement when we want to support extremely low latency traffic i.e. AR/VR, UHD
As evaluated in 1523r0[3], satisfying UL latency is more challenge so we need to focus on
  Instant time information should be delivered to AP and considered when AP assign UL resource for low latency traffic
    For example, frame arrival time, remaining time, etc..
  OFDMA random access only for low latency traffic may be helpful to mitigate UL latency
Notes: 그림: Latency를 위한 OFDMA RA

## Slide 9: OFDMA enhancement
If traffic arrival information of STA side is reported to the AP, the AP can allocate UL resource to the proper time to the STA

## Slide 10: Summary
We have addressed several features for support low latency traffic in EHT
  Low latency queue/EDCAF based on 11aa can reduce channel access delay for low latency traffic
  It is important to prevent and cope with the worst case for latency traffic, so we may need signaling how to handle it
  OFDMA is a powerful for latency traffic, but it is necessary further improve from the latency perspective

## Slide 11: References
[1] 11-19-1175-00-00be-considerations-of-new-queue-mechanisms-for-real-time-applications.pptx
[2] 11-19-1207-04-00be-views-on-latency-and-jitter-features-in-tgbe.pptx
[3] 11-19-1523-00-00be-Performance-evaluation-of-deterministic-service-for-EHT.pptx

## Slide 12: Straw poll 1
Do you agree to add the following into the TGbe SFD?
An EHT non-AP STA may use a new EDCAF for low latency traffic when the worst case has occurred
  Definition of worst case is TBD

## Slide 13: Straw poll 2
Do you agree to add the following into the TGbe SFD?
An EHT non-AP STA can report instant time information related with low latency traffic
  Detail information is TBD