## Slide 1: Multi-link Association Setup
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Date: 2019-06-04

## Slide 2: Overview
A multi-link architecture was presented in the past [1, 2, 3] with the objective to provide a unified framework for addressing aggregation, link availability and power management topics.
Other contributions [1, 4] have discussed how the unified framework can support packet-level aggregation and dynamic transfer of a TID between links.
This contribution describes a scheme for multi-link association to supports both forms of multi-link operation.

## Slide 3: Motivation
An AP entity can setup BSSs on different links
  It may do so for supporting legacy clients
  Should a multi-link capable non-AP entity associate on each link?
A non-AP entity may hear an AP’s beacon on any link.
  How would the entity know if the AP can operate on multiple link? And if so, what are the capabilities and operational parameters of the AP entity’s BSS(s) on other link(s)?
  How would a multi-link capable single radio non-AP entity know the beacon TBTT on other link(s) that the AP supports?
Multi-link framework needs to define an association scheme that addresses the above and works for different forms of multi-link operation

## Slide 4: Multi-link vs Single link setup
Discovery phase
  Advertisement of capabilities and operational parameters
Association and setup
  Exchange of capabilities & operational parameters, setting up of security keys, and establish association context (AID assignment)
Dynamic link activation
  Enable/disable one or more configured links based on various criteria
    Applies to MLA case only

## Slide 5: Multi-Link Discovery
A non-AP entity can discover an AP entity on any link that the AP entity has setup a BSS (and transmits a Beacon frame).
The beacon from the AP entity on any link carries information (attributes) about all the links that the entity is operating on
  This would provide non-AP entity with sufficient information on capabilities, operating parameters and any constraints for each link that the AP operates on.
  It can further aid a non-AP entity in selecting a suitable AP entity for multi-link association

## Slide 6: Link Attributes
On each operating link, the beacon from the AP entity provides info. about the other link(s) that it can operate on.
  Identifies each link as a tuple: {operating class, channel and BSSID}
  For a given link, identifies if the links can operate independently with respect to other link(s)
    i.e., the Tx/Rx can be independent between the pair of links
  Provides beacon interval and TSF offset information
    Aids an MLO capable single radio non-AP entity
  Provides link specific information
    e.g., capabilities, operational parameters etc
The link information is also carried in AP’s probe and association response.
A non-AP entity provides information about its capabilities to operate on multiple link during probing and association

## Slide 7: Multi-link Association
A non-AP entity performs multi-link association with the AP entity on one of the link
Multi-link association sets-up a single association context that extends to all the links supported by both entities
  Establishes the affiliation of MAC-SAP end-point to the lower MAC/PHY (STA) instances for each peer entity
  Establishes a single security context between the MAC-SAP end-points
    Single encryption key, PN space etc between the two MAC-SAPs

## Slide 8: Summary
In this presentation, we describe a scheme for multi-link discovery and a single association setup that extents across multiple links.
  AP’s beacon advertises capabilities and operational parameters of all the links that AP entity operates on.
  Non-AP entity provides its capabilities information during probing and association.
  Both entities exchange capabilities and operations parameters during multi-link association

## Slide 9: Straw Poll 1
Do you support that the 802.11be amendment shall define mechanism(s) for multi-link operation that enables the following:
  Indication of capabilities and operating parameters for multiple links of a multi-link logical AP entity
  Negotiation of capabilities and operating parameters for multiple links during a single setup signaling exchange.
Passed with unanimous concent
  Y:
  N:
  A:

## Slide 10: Motion
Move to add the followings to the 11be SFD:
  Define mechanism(s) for multi-link operation that enables the following:
    Indication of capabilities and operating parameters for multiple links of an AP multi-link device (AP MLD)
    Negotiation of capabilities and operating parameters for multiple links during a single setup signaling exchange.
Mover: Abhishek Patil
Second:

## Slide 11: Reference
[1]: 11-19-0773 Multi-link Operation Framework (Po-Kai Huang - Intel)
[2]: 11-19-0823 Multi-Link Aggregation (Abhishek Patil - Qualcomm)
[3]: 11-19-0821 multiple band discussion (Liwen Chu - Marvell)
[4]: 11-19-1082 Multi-link Operation: Dynamic TID Transfer (Abhishek Patil - Qualcomm)