## Slide 1: Multi-Link Operation: Anchor Channel
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Date: 2019-09-04

## Slide 2: Overview
A multi-link architecture was presented in the past [1, 2, 3] with the objective to provide a unified framework for addressing aggregation, link availability and power management topics.
Other contributions [1, 4] have discussed how the unified framework can support packet-level aggregation and dynamic transfer of a TID between links.
This contribution focuses on how the unified framework aids power-save on clients.

## Slide 3: Motivation
Power-save:
  Allow a STA to monitor only a single link and to not be forced to monitor multiple links when multiple links are enabled
Control/Data separation:
  allows sending management frames on one of the links, leaving the other links primarily for data exchange

## Slide 4: Concept of Anchor link
Anchor* link:
  The link where a non-AP entity monitors beacon, expects group addressed frames and may perform keep-alive functionality
  Default link used for mgmt. signaling
Non-anchor link:
  The non-AP STA instance(s) on other link(s) are not required to perform basic BSS operation and can be in doze state, unless explicitly indicated otherwise.
* Note: the exact name is TBD

## Slide 5: Selection of an anchor link
AP entity: May perform basic BSS functionalities on one or more of it’s enabled link(s)
  Such link(s) are referred to as AP selected Anchor link(s)
    On Non-Anchor links: AP may perform a reduced set of BSS functionalities (e.g., TSF maintenance), data delivery etc
  All 11be devices will parked on anchor channel
Non-AP entity: selects an anchor link from the list.
  Non-AP entity informs AP regarding it choice
  Monitors the anchor link for basic functionality
  Expects (D)TIM beacons and group addressed DL BU deliveries in this link
  STA may declare its PM mode in any link by sending a frame directly on those links

## Slide 6: Anchor Channel Operation
Beacon sent on anchor channel carries traffic-indication for the non-AP STA entity
  AP knows the anchor channel of each of its STA
  AP duplicates group addressed traffic on all the anchor links
  An AP is expected to trigger a non-AP STA on the anchor link
Non-AP entity may send keep alive messages on its anchor link

## Slide 7: Waking up of additional links
During idle conditions, a non-AP entity camps on the anchor link
  The non-AP STA instance on other link(s) can be in doze state
For DL traffic, an AP entity notifies the non-AP entity if it intends to send traffic on non-anchor link(s)
  Non-AP STAs on non-anchor links wake-up based on the notification
For UL traffic, a non-AP entity may transmit a frame on any link that is enabled as part of Multi-Link setup
  ‘Any link’ includes non-anchor links

## Slide 8: Summary
We propose the concept of anchor link where non-AP entity is always available to perform basic BSS operations.
  The proposed framework facilitates power-save for a non-AP entity while making additional links available when there is an active data session

## Slide 9: Straw Poll 1
Do you support that the 802.11be amendment shall define a mechanism for multi-link operation that enables the following:
  A non-AP entity monitors and performs basic operations (such as timing information, traffic indication, BSS parameter updates, etc.) on one or more link(s)
  Y:
  N:
  A:

## Slide 10: Reference
[1]: 11-19-0773 Multi-link Operation Framework (Po-Kai Huang - Intel)
[2]: 11-19-0823 Multi-Link Aggregation (Abhishek Patil - Qualcomm)
[3]: 11-19-0821 multiple band discussion (Liwen Chu - Marvell)
[4]: 11-19-1082 Multi-link Operation: Dynamic TID Transfer (Abhishek Patil - Qualcomm)