## Slide 1: EHT Preamble Design
Date: 2019-11-11
Authors:

## Slide 2: Introduction
802.11 standards have evolved from 802.11a to 802.11ax over past two decades.
Preamble design is important in each generation.
  Provide backward compatibility with exiting standards.
  Enable PPDU format auto-detection.
  Signal important information to support various PHY/MAC features.
From EHT, we propose to advance the preamble design philosophy to support an unified structure enabling future coexistence and simple PPDU format detection.

## Slide 3: EHT Preamble Design Philosophy
Till 11ax, the preamble design has piled up features for each PPDU format to support auto-detection.
  QBPSK, L-LENGTH%3, RL-SIG
  Auto-detection complexity and latency have significantly increased.
  Limit complexity in EHT for auto-detection
Across-generation coexistence using preamble.
  Mainly L-LENGTH is used across generations for CCA detection.
  In 11ax, more coexistence bits are added, e.g. BSS color, TXOP, etc.
  Only understood by 11ax STAs, and different bit definition across PPDU
  EHT as a switch point to include future coexistence.
EHT
11a/g/n/ac/ax
EHT and beyond
Backward compatibility
Future compatibility and coexistence

## Slide 4: EHT Preamble Structure
Based on this design philosophy, we discussed high-level EHT preamble structure in our previous contribution [1].
  Backward compatible: legacy preamble is appended
  RLSIG: kept for range extension and PPDU format signaling
Common SIG field
  Static bits are common across generations, signaling co-existence bits.
  Includes bits to indicate PPDU formats
EHT-SIG field
  Signal other PPDU decoding related information, MU info, etc.
Common SIG
L-STF
L-LTF
L-SIG
RLSIG
Common SIG
L-STF
L-LTF
L-SIG
RLSIG
Common SIG
EHT SIG
L-STF
L-LTF
L-SIG
RLSIG
EHT-STF, EHT-LTF, EHT-DATA
…
…
…
;;;
…

## Slide 5: Common-SIG Structure
Common SIG exists in all EHT and future generations
  Defined on 20MHz bandwidth, similar to HE-SIGA.
  Modulation: BPSK with BCC-1/2
  Duplicated over entire PPDU bandwidth.
  Resilient to preamble puncturing
Common SIG includes both Version-independent bits and Version-dependent bits
  Version-independent bits have static location and bit definition across different generations/PHY versions.
    Co-existence bits will be included in this field.
  Version-dependent bits may have variable bit definition in each PHY version.

## Slide 6: Common-SIG Content
Version-independent bits:
  PHY version identifier field: 3 bits.
  BSS color (6 bits), TXOP (7 bits), DL/UL (1).
  Others
Version-dependent bits:
  PPDU format: 2 bits.
  EHT-SIG: MCS (4 bits), Number of symbols (6 bits).
  Others
Version-independent Bits
Version-dependent Bits

## Slide 7: PPDU Format Signaling
Unified two-step PPDU format signaling for EHT and beyond.
Step 1: Implicit signaling of EHT and beyond PPDU
  One bit information whether the PPDU is EHT and beyond
  E.g. LENGTH%3, RLSIG, QBPSK and etc.
  Need to be simple and robust
  Auto-detection complexity is limited to design of this part.
Step 2: Explicit signaling of specific PPDU format
  Use PHY format bits and PPDU bits in Common SIG symbols to signal PPDU formats.

## Slide 8: EHT and beyond PPDU Identifier
Design criterion: Limited complexity and latency.
  Detect EHT and beyond PPDU format as early as possible.
    Sufficient time for AGC, enable power saving, etc.
  The minimum amount of change to 11ax to limit complexity.
    Reduce the amount of hypothesis in the classification state-machine
Proposed design:
  LENGTH%3 == 0 + RL-SIG + BPSK Common SIG1
    Same complexity level and detection latency as 11ax.
    Simple modification in the logic to detect EHT PPDU.
    Mature design endorsed by existing 11ax STAs.

## Slide 9: EHT SIG
EHT SIG contains all PPDU-dependent signaling bits that are not included in Common SIG field.
To simplify EHT SIG design, EHT SIG may use unified structure for SU/MU formats.
The detailed structure of EHT SIG structure is TBD.

## Slide 10: Summary
EHT preamble can be a pivoting generation to support future coexistence.
Define Common SIG with Version-independent bits to coexist with future generations.
Two-step PPDU format classification for EHT and beyond
  LENGTH%3 == 0 + RLSIG + BPSK Common SIG1
  PPDU bits in Common SIG.

## Slide 11: Reference
[1] High-level EHT Preamble Structure, IEEE 11-19/1085.

## Slide 12: SP1
Do you agree to add the following to 11be SFD?
  The next SIG field following the BPSK symbol after LSIG, is modulated on 20MHz basis.
    The number of symbols is TBD
    The SIG field name is TBD
    The content of the SIG field is TBD
20MHz SIG
L-STF
L-LTF
L-SIG
BPSK
20MHz SIG
L-STF
L-LTF
L-SIG
BPSK
20MHz SIG
L-STF
L-LTF
L-SIG
BPSK
…
…
…
…
…

## Slide 13: SP2
  Do you agree to add the following to 11be SFD?
  EHT and beyond PPDU format is classified by the following combination:
    LENGTH%3 == 0 + RL-SIG + BPSK on next symbol
Y:
N:
A:

## Slide 14: SP3
Do you agree to add the following to 11be SFD?
The 20MHz SIG includes Version-independent bits followed by Version-dependent bits
  Y:
  N:
  A:
Version-independent Bits
Version-dependent Bits

## Slide 15: SP4
Do you agree to add the following to 11be SFD?
20MHz SIG field includes the following bits in Version-independent bits portion:
    BSS color, number of bits >=6bits
    TXOP duration, number of bits >= 7bits
  Y:
  N: A:

## Slide 16: Reference
[1] EHT Preamble Design, Marvell

## Slide 17: Appendix: Existing PPDU Formats
HT-GF: Third symbol QBPSK detection can classify.
HT-MM: LENGTH%3 == 0 + SIG1 QBPSK (+ SIG2 QBPSK) can classify
VHT: LENGTH%3 == 0 + SIGA1 BPSK + SIGA2 QBPSK
HE SU/MU: LENGTH%3 ~= 0 + RLSIG + SIGA1 BPSK + SIGA2 BPSK
HE ER SU: LENGTH%3 ~= 0 + RLSIG + SIGA1 BPSK + SIGA2 QBPSK
L-STF
L-LTF
L-SIG
RLSIG
HE-SIGA2
HE-SIGA, HE-SIGB, HE-STF, HE-LTF, HE-DATA
HE-SIGA1
L-STF
L-LTF
L-SIG
L-DATA
L-STF
L-LTF
L-SIG
HTSIG1
HT-STF
HT-LTFs
HT-DATA
11a
HT-MM
HTSIG2
HT-GF-STF
HT-LTF1
HTSIG1
HT-DATA
HTLTF2~NLTF
HTSIG2
HT-GF
L-STF
L-LTF
L-SIG
VHTSIGA1
VHTSTF
VHTLTFs
VHT-DATA
VHT
VHTSIGA2
VHTSIGB
L-STF
L-LTF
L-SIG
RLSIG
HE-SIGA2
HE-SIGB, HE-STF, HE-LTF, HE-DATA
HE SU/MU
HE-SIGA1
HE_ER
QBPSK
BPSK