## Slide 1: Multi-link Broadcast Addressed frame Reception
Date: 2019-08-27
Authors:
Name | Affiliations | Address | Phone | Email
Po-Kai Huang | Intel |  |  | 
Laurent Cariou |  |  |  | 
Dan Bravo |  |  |  | 
Arik Klein |  |  |  | 
Ofer Schreiber |  |  |  | 
Notes: September 2012

## Slide 2: Background
Multi-link framework has been proposed below. We discuss how to receive broadcast addressed frame for non-AP MLD.
AP1
AP2
AP3
STA1
STA2
STA3
AP MLD
Non-AP MLD

## Slide 3: Consideration for Broadcast Addressed Data Reception
Broadcast addressed data reception is done mainly by DTIM mechanism
We think that due to existence of legacy STAs in each link, the most common case is that a broadcast addressed data frame is transmitted in each link
  For a non-AP MLD, it then does not make sense to follow DTIM of each link to receive duplicate broadcast addressed frame. Non-AP MLD only needs to follow one DTIM to receive broadcast addressed data frame
  For one radio non-AP MLD, follow DTIM in one link enables further power save and avoid complexity of constant switching among links
Link 1
Link 2
Broadcast addressed delivery
Broadcast addressed delivery
DTIM
DTIM
Notes: l

## Slide 4: Consideration for Broadcast Addressed Management Frame Reception
There are many other broadcast addressed management frame to deal with management of configuration/parameters of each link
  It again does not make sense for non-AP MLD to constantly wake up in different links to receive update on link management
  It is also useful for AP MLD to know the link that non-AP MLD camps to receive broadcast addressed management frame for link management
Proposal:
  a non-AP MLD only needs to follow one configured link among the links setup with the an AP MLD to receive broadcast addressed frame
AP
1
AP
2
AP MLD
Non
-
AP MLD
1
Non
-
AP
1
Non
-
AP
2
Link
1
Link
2
–
Configured link

## Slide 5: Can the configured link be different for different non-AP MLDs?
We think that different non-AP MLDs, specifically the one that only supports one radio, may want to camp on different links for broadcast addressed frame
  There may not be common link available for non-AP MLD. For example, some non-AP MLD may setup only 2 links, and other non-AP MLD may setup 3 links.
  Different non-AP MLD may see different congestion environment or camp on different links for load balancing reason
Proposal:
  Have a TBD mechanism to determine configured link to receive broadcast addressed frame
AP
1
AP
2
AP MLD
Non
-
AP MLD
1
Non
-
AP
1
Non
-
AP
2
Link
1
Link
2
–
Configured link
AP
1
AP
2
AP MLD
Non
-
AP MLD
2
Non
-
AP
1
Non
-
AP
2
Link
1
–
Configured link
Link
2

## Slide 6: Summarized Proposal
a non-AP MLD only needs to follow one configured link among the links setup with the an AP MLD to receive broadcast addressed frame
have a TBD mechanism to determine configured link to receive broadcast addressed frame

## Slide 7: Conclusion
We discuss the consideration of multi-link broadcast addressed frame reception
  It makes sense for a non-AP MLD to follow only one configured link to receive broadcast addressed frame based on the consideration of duplicate data frame detection, power save, and complexity of constant switch
We propose to have a TBD mechanism to change the configured link of a non-AP MLD

## Slide 8: Straw Poll
Do you support that
  a non-AP MLD that wants to receive all broadcast addressed Data frames is allowed to receive broadcast addressed Data frame from a link among the links setup with an AP MLD
  The link used by the non-AP MLD to receive broadcast addressed Data frame can be changed, and the method to change the link is TBD