## Slide 1
Secure-LTF: Unintentional Beamforming Problem and A Solution Proposal
Date: 2019-09-1217-12-14
Authors:
Name | Affiliations | Address | Phone | email
Mengchang Doong | Broadcom | 250 Innovation Drive San Jose, CA 95134 | +1 408-922-1037 | mengchang.doong@broadcom.com
Manas Deb |  | 250 Innovation Drive San Jose, CA 95134 | +1 408-922-5984 | manas.deb@broadcom.com
Marcellus Forbes |  |  |  | marcellus.forbes@broadcom.com
Rethna Pulikkoonattu |  | 16340 West Bernardo Dr, San Diego, CA, 92127 | +1 858-521-4840 | rethna@broadcom.com
Vinko Erceg |  | 16340 West Bernardo Dr, San Diego, CA, 92127 | +1-858-521-5885 | verceg@broadcom.com

## Slide 2: Abstract
This document highlights a potential problem with the present design of secure LTF sequence. In its present form, while in multi stream scenario, unintentional Beamforming (constructive and destructive addition of signal) could take place during the secure LTF transmission portion, and lead to dynamic range complications at the receiver. We propose a possible solution to mitigate the problem.

## Slide 3: Secure-LTF Generation (from .11az/D1.0)
Additional notes from .11az/D1.0
  No single stream pilot subcarriers in the secure HE-LTFs, all subcarriers are mapped using the full P-HE-LTF matrix.
  No CSD is applied to the space-time streams.
  No spatial mapping, the Q matrix is a block identity matrix.
  P ={7, 8, 9, 10} for {20, 40, 80,160/80+80} MHz PHY BW.
2P 8PSK symbols
CSD Value Generator
P bits
8PSK Sequence Generator
3P+3
bits
Subcarrier Mapper
CSD
tCS
PHE_LTF Matrix Mapping
…
IDFT
Zero-GI and Windowing
Randomized LTF Sequence
IDFT
Zero-GI and Windowing
IDFT
Zero-GI and Windowing
Frame Format Construction

## Slide 4: Secure-LTF (Present Design): N_STS=2 and LTF_REP = 2
The waveforms on TX stream 1 and stream 2 are aligned exactly (in time domain, either in-phase or 180 degrees out of phase), causing unintentional beamforming, by way of constructive/destructive addition of signal.
Seq1, Seq2, Seq3 and Seq4 are generated from 4 different sets of 4P+3 bits.
Seq1
TX Stream 1
TX Stream 2
- Seq2
Seq3
- Seq4
Seq1
Seq2
Seq3
Seq4
HE-STF
…
HE-STF
…

## Slide 5: Secure-LTF (Present Design): N_STS=2 and LTF_REP = 2
In case of in-phase LOS or some flat-fading cases
(small indoor environment)
RX RSSI
9.6us
Destructive
interference
Constructive
interference
RX signal energy stays low for 9.6us, which may cause RX packet abortion.
Zero GI
Seq1
TX Stream 1
TX Stream 2
- Seq2
Seq3
- Seq4
Seq1
Seq2
Seq3
Seq4
3dB
3dB average power increase.
HE-STF
…
HE-STF
…

## Slide 6: Simulated RX Waveform (.11nB channel model)
If no per-STS CSD is applied, unintentional beamforming can take place, resulting in larger signal amplitude fluctuation in the time domain. This behavior eats up the receiver circuit dynamic range.
HE-LTF1
HE-LTF2
PE
HE-STF
HE-SIG
L-STF
L-LTF
L-SIG
RL-SIG
Smaller-than-usual signal amplitude caused by un-intentional beamforming (destructive interference).
Larger-than-usual signal amplitude caused by un-intentional beamforming (constructive interference).
AGC in work
chan_indx = 2

## Slide 7: Potential Problems
Circuit dynamic range
  The secure-LTF signal at the receiver may end up boosted by up to 10*log10(N_STS) dB of power. Similarly, a part of the LTF signal could be completely nulled out due to the destructive addition.
  N_STS=2, can result in 3dB boost or a nulling.
  RX power can increase by up to 9 dB (for 8 TX stream case) when coherent interference happens. Extra circuit dynamic range will be required to accommodate the excessive power swing.

## Slide 8: Secure LTF design Proposal: Illustration for N_STS=2 and LTF_REP = 2
A1, A2, A3 and A4 are different secure-LTF sequences, which can be generated by the procedure described in .11az. With the following rule, the complexity increment for channel estimation is kept minimum comparing to current .11az. No matrix inversion is needed !!
  Only need extra phase rotations on H12 and H22 after the typical channel estimation method.
The (time-domain) waveforms on TX stream 1 and TX stream 2 look totally different.
  Highly secured.
  No unintentional beamforming issue
Rule:
  Sequence A1, A2 are generated from 2 different (and independent) sets of 4P+3 bits.
  The 8PSK sequence of A3 are generated from another independent set of 3P+3 bits. The az_csd of A3 is the same as A1.
  The 8PSK sequence of A4 is generated from 3P+3 bits which are a simple function of the previous 3 sets of 3P+3 bits. The az_csd of A4 is the same as A2.
  The function to generate 3P+3 bits for A4 is described in the following pages.
A1
TX Stream 1
- A2
B1
- B2
A3
TX Stream 2
A4
B3
B4

## Slide 9: Simulated RX Waveform with Proposal
With this proposal, the unintentional beamforming behavior is minimized. RX signal power stays even.
HE-LTF1
HE-LTF2
PE
HE-STF
HE-SIG
L-STF
L-LTF
L-SIG
RL-SIG
AGC in work

## Slide 10: Recap about the 4P+3 bits and the iterative process
The 4P+3 bits can be divided into groups as shown below:
b0, b1, … bP-1,
bP, bP+1, bP+2,
bP+6, bP+7, bP+8,
bP+9, bP+10, bP+11,
b4P, b4P+1, b4P+2
…
secure az_csd
s1(0) = exp(jq1)
j1= exp(jf1)
j2= exp(jf2)
jP-1= exp(jfP-1)
…
The iterative process
s2(0) = exp(jq2)
These 3P+3 = 3(P+1) bits are used to generate the 8PSK secured sequence.
These P bits are used to generate the az_csd.
A sequence of 2P 8PSK symbols are generated by P-1 iterations.
Initial values
bP+3, bP+4, bP+5,

## Slide 11: “The Rule” and notations
b0, b1, … bP-1,
bP, bP+1, bP+2,
b4P, b4P+1, b4P+2
…
secured az_csd
tCS
s1(0) = exp(jq1)
j1= exp(jf1)
j2= exp(jf2)
jP-1= exp(jfP-1)
…
s2(0) = exp(jq2)
For A1
For A2
For A3
tCS_A1
tCS_A2
tCS_A3=tCS_A1
q1_A1
q1_A2
q1_A3
q2_A1
q2_A2
q2_A3
f1_A1
f1_A2
f1_A3
f2_A1
f2_A2
f2_A3
fP-1_A1
fP-1_A2
fP-1_A3
For A4
tCS_A4=tCS_A2
q1_A4
= -q1_A1 + q1_A2 + q1_A3
q2_A4
= -q2_A1 + q2_A2 + q2_A3
f2_A4
= -f2_A1 + f2_A2 + f2_A3
f1_A4
= -f1_A1 + f1_A2 + f1_A3
…
…
…
fP-1_A4
= -fP-1_A1 + fP-1_A2 + fP-1_A3
bP+6, bP+7, bP+8,
bP+9, bP+10, bP+11,
bP+3, bP+4, bP+5,
…
We will explain why we choose this “-++” rule in the following pages.

## Slide 12: Notations and Equations to represent the function
The 4P+3 bits for A1,A2, A3 and A4 are denoted by
  For A1: b1i for i=0,…4P+2.  Secure bits required: 4P+3
  For A2: b2i for i=0,…4P+2.  Secure bits required: 4P+3.
  For A3: b3i for i=0,…4P+2.  Secure bits required: 3P+3.
  For A4: b4i for i=0,…4P+2.  Secure bits required: 0.
b3i= b1i for i=0,…P-1  same az_csd for A1 and A3
b4i= b2i for i=0,…P-1  same az_csd for A2 and A4
For A4 s1(0)
For A4 s2(0)
For A4 jp
    for p=1,…,P-1

## Slide 13: The iterative process
initialization
s1(0) = exp(jq1)
s2(0) = exp(jq2)
Iteration 1
s1(1) = [ exp( jq1 ) , exp( jq2 ) ]
s2(1) = [ exp( j(q1+f1) ) , exp( j(q2+f1+p) ) ]
Note: -jp= - exp(jfp) = exp( j(fp+p) )
Iteration 2
Phase of s1(0) | q1 |  |  |  |  |  |  | 
Phase of s2(0) | q2 |  |  |  |  |  |  | 
Phase of s1(1) | q1 | q2 |  |  |  |  |  | 
Phase of s2(1) | q1+f1 | q2+f1+p |  |  |  |  |  | 
Phase of s1(2) | q1 | q2 | q1+f1 | q2+f1+p |  |  |  | 
Phase of s2(2) | q1+f2 | q2+f2 | q1+f1+f2+p | q2+f1+f2 |  |  |  | 
Phase of s1(3) | q1 | q2 | q1+f1 | q2+f1+p | q1+f2 | q2+f2 | q1+f1+f2+p | q2+f1+f2
Phase of s2(3) | q1+f3 | q2+f3 | q1+f1+f3 | q2+f1+f3+p | q1+f2+f3+p | q2+f2+f3+p | q1+f1+f2+f3 | q2+f1+f2+f3+p
Iteration 3
…
…

## Slide 14: For A4 (using iteration 2 as an illustration)
initialization
Iteration 1
Iteration 2
Phase of s1(0) | q1_A4 |  |  |  |  |  |  | 
Phase of s2(0) | q2_A4 |  |  |  |  |  |  | 
Phase of s1(1) | q1_A4 | q2_A4 |  |  |  |  |  | 
Phase of s2(1) | q1_A4+f1_A4 | q2_A4+f1_A4+p |  |  |  |  |  | 
Phase of s1(2) | q1_A4 | q2_A4 | q1_A4+f1_A4 | q2_A4+f1_A4+p |  |  |  | 
Phase of s2(2) | q1_A4+f2_A4 | q2_A4+f2_A4 | q1_A4+f1_A4+ f2_A4+p | q2_A4+f1_A4+ f2_A4 |  |  |  | 
Re-notation
Phase of s1(2) | w11_A4 | w12_A4 | w13_A4 | w14_A4
Phase of s2(2) | w21_A4 | w22_A4 | w23_A4 | w24_A4
Using the rule mentioned earlier, it can be rewritten as
Phase of s1(2) | -w11_A1 +w11_A2 +w11_A3 | -w12_A1 +w12_A2 +w12_A3 | -w13_A1 +w13_A2 +w13_A3 | -w14_A1 +w14_A2 +w14_A3
Phase of s2(2) | -w21_A1 +w21_A2 +w21_A3 | -w22_A1 +w22_A2 +w22_A3 | -w23_A1 +w23_A2 +w23_A3 | -w24_A1 +w24_A2 +w24_A3
This relationship holds for all iterations.  The final sequence A4 = A2 .* A3 ./ A1
Phase addition is equivalent to value multiplication.
Phase subtraction is equivalent to value division.
Apply similar notation for A1, A2 and A3
“.*” and “./” denote point-wise multiplication and division for each element in the array. In our case, it means frequency domain point-wise operation.
We have just proven that the A4=A2.*A3./A1 is constructed with the same structure as A1, A2 and A3, and is therefore a Golay sequence with the same PAPR as others.

## Slide 15: Illustration for Channel Estimation
A1
TX Stream 1
TX Stream 2
- A2
B1
- B2
A3=
A1.*(A3./A1)
A4=
A2.*(A3./A1)
B3= B1.*(B3./B1)
B4= B2.*(B3./B1)
TX stream 1
TX stream 2
RX
.*(A3./A1)
Since this term is a fixed value within one repetition period, it can be viewed as part of the channel response.
[A1, -A2 ]
[A1, A2 ]
“Typical”
Channel Estimation
.*(A1./A3)
.*(A1./A3)
Est{ h11 }
Est{ h12 }
Est{ h21 }
Est{ h22 }
[A1, A2 ]
Since (A3./A1) is known, we can compensate for it after “typical” channel estimation block.
TX
[A3, A4 ]
h11
h12
h21
h22
Since A1 and A3 are 8PSK sequences, “.*(A3./A1)” and “.*(A1./A3)” are just phase rotations.

## Slide 16: Extend to more TX streams, using N_STS=4 as an example
( 2 * NHE_LTF - 1 ) secured sequences required
A1
TX Stream 1
TX Stream 2
- A2
A3
A4
A5
A2.*A5./A1
-A3.*A5./A1
A4.*A5./A1
A6
TX Stream 3
TX Stream 4
A2.*A6./A1
A3.*A6./A1
-A4.*A6./A1
-A7
A2.*A7./A1
A3.*A7./A1
A4.*A7./A1

## Slide 17: Matrix constructed in this manner is always invertible
It is a Hadamard matrix scaled by diagonal matrices.
NHE_LTF = 2
NHE_LTF = 4

## Slide 18: Matrix constructed in this manner is always invertible
NHE_LTF = 6
where

## Slide 19: Matrix constructed in this manner is always invertible
NHE_LTF = 8

## Slide 20: Appendix

## Slide 21: Matrix constructed in this manner is always invertible
NHE_LTF = 4
NHE_LTF = 2

## Slide 22: Matrix constructed in this manner is always invertible
NHE_LTF = 6
where

## Slide 23: Matrix constructed in this manner is always invertible
NHE_LTF = 8

## Slide 24: Math for Channel Estimation (using 2x2 as an example)
Assume the frequency domain value of the kth tone for sequence A1, A2 and A3 are A1k, A2k and A3k respectively. Since A1k and A3k are 8PSK symbols, A1k and A3k can be written as exp( j * qA1k) and exp( j * qA3k) respectively. The k_th tone being send out through the two antennas:
  Symbol: n n+1 n+2 n+3
  TX Ant 0: A1k -A2k B1k -B2k
  TX Ant 1: A3k A2k*exp( j*qA3k)*exp( -j*qA1k) B3k B2k*exp( j*qB3k)*exp( -j*qB1k)
We can rewrite them as (only show symbol n and n+1)
  Symbol: n n+1
  TX Ant 0: A1k -A2k
  TX Ant 1: A1k*exp( j*qA3k)*exp( -j*qA1k) A2k*exp( j*qA3k)*exp( -j*qA1k)

## Slide 25: Math for Channel Estimation (using 2x2 as an example)
If the channel matrix for kth tone is Hk=[ h11_k h12_k ; h21_k h22_k ], then at the receiver for symbol n and n+1, we get (ignoring noise):
  RX Ant 0:
    y1[n] = h11_k* A1k + h12_k* A1k*exp( j*qA3k)*exp( -j*qA1k)
    y1[n+1] = h11_k* (-A2k )+ h12_k* A2k*exp( j*qA3k)*exp( -j*qA1k)
  RX Ant 1:
    y2[n] = h21_k* A1k + h22_k* A1k*exp( j*qA3k)*exp( -j*qA1k)
    y2[n+1] = h21_k* (-A2k )+ h22_k* A2k*exp( j*qA3k)*exp( -j*qA1k)
We can write
  H12_k’ = h12_k*exp( j*qA3k)*exp( -j*qA1k)
  H22_k’ = h22_k*exp( j*qA3k)*exp( -j*qA1k)
Substituting these into the equations, we get
  RX Ant 0:
    y1[n] = h11_k* A1k + h12_k’ * A1k
    y1[n+1] = h11_k* (-A2k )+ h12_k’ * A2k
  RX Ant 1:
    y2[n] = h21_k* A1k + h22_k’ * A1k
    y2[n+1] = h21_k* (-A2k )+ h22_k’ * A2k

## Slide 26: Math for Channel Estimation (using 2x2 as an example)
Now we can solve h11 , h12’ , h21 and h22’ from previous equations
  RX Ant 0:
    y1[n] / A1k = h11_k + h12_k’
    y1[n+1] / A2k = h11_k + h12_k’
  RX Ant 1:
    y2[n] / A1k = h21_k + h22_k’
    y2[n+1] / A2k = h21_k + h22_k’
By adding and subtracting the equations
  RX Ant 0
    h11_k = ( y1[n] / A1k - y1[n+1] / A2k ) /2
    h12_k’ = ( y1[n] / A1k + y1[n+1] / A2k ) /2
  RX Ant 1
    h21_k = ( y2[n] / A2k - y2[n+1] / A2k ) /2
    h22_k’ = ( y2[n] / A2k + y2[n+1] / A2k ) /2
After we solve h12_k’ and h22_k’ , we can then compensate for the phase shift and get h12_k and h22_k
  h12_k = h12_k’ * exp( -j * qA3k) * exp( j * qA1k)
  h22_k = h22_k’ * exp( -j * qA3k) * exp( j * qA1k)