## Slide 1: Multi-Link Auxiliary Link
Date: 2019-09-12
Authors:
Name | Affiliations | Address | Phone | Email
Zhou Lan | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | zhou.lan@broadcom.com
Srinath Puducheri |  |  |  | 
George Kondylis |  |  |  | 
Matthew Fischer |  |  |  | 
Notes: November 2012

## Slide 2: Motivation
Max PHY BW in 11be is envisioned to be 320MHz
Survey of current STAs shows that STA BW is typically smaller than AP:
  E.g, several 11ax/11ac gen2 capable STAs only support up to 80MHz BW, while APs typically support 160MHz BW
Foresee similar trend in 11be, where many STAs in the first generation may only support 160MHz or narrower BW
Asynchronous channels not always available
  Then quasi-asynchronous mode employed, better operation with controlled access
We propose a new mode of multi-link operation (MLO) to address this predicted asymmetry and allow more efficient use of spectrum

## Slide 3: Typical MLO scenario considered so far
  Multi-link on same band or multi-band
  E.g., 2.4G + 5G, 2.4G + 5G + 6G or 5GL+5GH+6G
Key features/assumptions
  Independent/separate radios per link, on both AP and STA
  Single MAC function
  Total aggregated BW can be > 320MHz (max 320MHz per radio)
Possible additional requirements
  Support concurrent and async TX/RX operation across links
    I.e. split the MAC
  There may need to be sufficient frequency separation and filtering protection to allow this mode.
    Otherwise, Quasi-asynchronous mode of operation applies

## Slide 4: Proposed new mode of MLO: “Auxiliary-channel” operation
AP supports higher BW (e.g., 320MHz) than associated STAs. Operational BW is split into two or more neighboring channels. Examples:
  320MHz split into two adjacent channels of 160MHz each,
  320MHz split into two channels 160MHz and 80MHz separated by 80MHz, etc.
Total BW summed across all neighboring channels <= 320MHz
AP establishes a BSS on each of these channels
Some channel combinations might lead to the following restrictions:
  No simultaneous TX/RX, no async RX/RX, no async TX/TX across channels.

## Slide 5: Proposal
Designate one BSS as “Main” and other BSS as “aux”
  Each BSS has its own primary channel
Basic BSS operations
  Each BSS beacons on its own primary channel
  Assoc on main BSS, with AP moving STAs between main and aux BSS
    Partly motivated by the fact that assoc on aux BSS is not guaranteed to succeed due to “virtual collision” with main BSS
      i.e. not a collision on the same channel, but a resource collision for AP receiver functions
      i.e. TX/RX restrictions between channels means that AUX BSS STA would have to be aware of activity on main channel, but it is not
    AP will limit aux BSS membership to 11be clients only
    Allows AP to load-balance and otherwise manage channel use
  AP can offer UORA-based assoc directly on Aux BSS

## Slide 6: Auxiliary BSS Beaconing
AP sends an Aux BSS Beacon on the Aux BSS Primary Channel
  To indicate channel occupancy and provide indication of continued presence for associated STAs, current BSS operational parameters
  Aux Beacon contains “invitation only” BSS Membership selector value, no one can join directly
    Prevents legacy association attempts
    Prevents 11be direct association attempts
      11be STAs only join through “invitation” from main BSS
      STA may refuse invitation
Beacons indicate AP operational mode
  Asynch vs Qsynch vs Synch
  Triggered-only operation

## Slide 7: AUX Association
By invitation only
  STA first joins Main BSS
  AP or STA initiates move to AUX BSS
    Move function/frame exchange TBD
AP or STA can initiate a move from AUX to MAIN
  Move function/frame exchange TBD
  Always have disassociation/reassociation as a backup

## Slide 8: Aux BSS Access Rules
Uplink traffic (control, mgmt, data) from assoc’d STAs in aux BSS: Restricted to Trigger-based
  STAs are assigned AID per-BSS (to be used on respective BSS)
    Natural situation, since BSSs are distinct
    But AP may assign from a single space
  TA, BSSID of all MPDUs except Beacon and Probe Response could be the same for Main and Aux BSS transmissions, same RA, BSSID for all receptions
  STAs may bail out of aux BSS at any time and move to main BSS and notify Aux AP accordingly (details: TBD)
    STAs might move to Main BSS without notifying the Aux AP, since they are not allowed to transmit until triggered, but might have an urge to move quickly. Of course, the STA needs to notify the Main AP of the move
EDCA rules:
  Main BSS: same as 802.11ax for both AP and STAs, wide and narrow operation
    i.e. access based on Main P20
  Aux BSS: AP can access based on Aux P20, STA triggered, STA EDCA next slide

## Slide 9: Optional Untriggered UL on AUX (1)
  Only when AP permits
  STA shall transmit RTS before an un-triggered/un-solicited transmission using EDCA
  AP transmits a wideband CTS covering both main and aux BSS channels if possible (i.e., medium is available on main BSS), else transmits CTS covering only aux BSS, if AP allows UL TX simultaneous with main activity
    I.e. CTS transmitted SIFS after RTS (aux only, or main+aux)
    AP might need to wait for main BSS channel to become available
      At main available, AP may then send CTS, i.e. >> SIFS
      RTS is functional equivalent of UL resource request
      CTS is functional equivalent of an single-user trigger
        AP may send alternative to CTS, e.g. Trigger

## Slide 10: Optional Untriggered UL on AUX (2)
  If transmitting STA receives CTS with non-zero DUR within SIFS, it proceeds with UL PPDU transmission
  If no CTS in SIFS, STA backs off a minimum period of T1 (i.e., T1 + random backoff) before re-trying. If re-try fails, may retry up to N times with increasing back offs of T2, T3, etc.
    AP decides values for T1, T2, etc. (dynamically) and conveys to STAs via 11be operation element, e.g. T1==100 us, T2==400 us, etc.
    If CTS arrives before backoff, then backoff is canceled and UL TX proceeds
    Rationale:
      STA on AUX lacks ED or PHY CRS on main; it compensates with a larger backoff.
      Want AUX STA RTS retries to be sparse, to avoid interferring with AP’s reception on MAIN
    Optional AP response of CTS with DUR==0 to acknowledge the RTS, but TXOP not yet available
  AUX STA may always choose to switch to MAIN

## Slide 11: Semi-asynchronous access
Main and Aux BSS EDCA backoff==0 alignment
  Not likely
But, improved odds because local traffic is triggered only
  I.e. centrally controlled access model
  I.e. fewer MAC instances competing for channel usage
  I.e. more likely idle medium on AUX when only the AP is performing EDCA on AUX

## Slide 12: Example of Wideband STA on Aux
160MHz client is on 80main, and follows normal EDCA access for untriggered UL
  Can use 80 or 160
  Is RTS-CTS with AP required to determine if 80 AUX is available?
    i.e. dynamic bandwidth signaling?
If 80main is busy, 160MHz client may choose to transmit on 80aux, if the AP permits
  BUSY condition due to inter-BSS, not intra-BSS
    As determined by examination of BSS color
  Using 80aux Optional UL Untriggered rules

## Slide 13: Straw poll 1
Do you support that the SFD includes the following statements under the heading Multi-link Operation:
  The amendment shall define:
    A BSS membership selector value that indicates to pre-EHT STA that they cannot joint the BSS and that EHT STA can only join by invitation and labeling this BSS as an AUX BSS*
  YES
  NO
  ABS
  *Or perhaps, RBSS == Restricted BSS

## Slide 14: Straw poll 2
Do you support that the SFD includes the following statements under the heading Multi-link Operation:
  The amendment shall define:
    A mechanism for a negotiated move of an associated STA between a non-AUX and an AUX BSS within the same MLLE AP
  YES
  NO
  ABS

## Slide 15: Straw poll 3
Do you support that the SFD includes the following statements under the heading Multi-link Operation:
  The amendment shall define:
    ​An ability for an MLLE AP to indicate to an EHT STA that UL transmissions in a specific link are restricted to Triggered access
  YES
  NO
  ABS

## Slide 16: Straw poll 4
Do you support that the SFD includes the following statements under the heading Multi-link Operation:
  The amendment shall define:
    CTS rules to support some EDCA-based UL TX by non-AP STA MLLE entities associated to an MLLE AP BSS on a link indicated as UL Triggered access restricted
  YES
  NO
  ABS

## Slide 17: Annex
Would the AP entity hear an RTS on the Aux BSS channel?

## Slide 18: Annex – Aux BSS UL RTS (1)
RX payload on Main
  Maybe the AP can RX RTS on AUX - but if the AP can RX RTS, then the AP could just send CTS DUR > 0 because it can RX payload on AUX as well, right?
      Or is the RTS received because of low MCS and payload would not be decodable at a higher MCS, in which case CTS DUR == 0 is a valid response from the AP
      Or is the correct answer really just "no, the AP cannot receive anything on AUX if it is decoding RX payload on Main"?
TX on main
  TX on main will likely swamp any RX of RTS on AUX, so no response from AP, no chance for CTS of any sort

## Slide 19: Annex – Aux BSS UL RTS (2)
NAV busy on main (and nothing else, e.g. no TX, no RX)
  AP can correctly hear an RTS from the non-AP STA
  If the NAV is for main, then what should the AP do?
      Send CTS DUR == 0 to make the non-AP STA wait, or can it send CTS DUR > 0, to allow the non-AP STA to TX on Aux without disturbing the 3rd party activity on Main?
      If Aux UL TX allowed, then if the NAV on main ends before the Aux UL TX, then some other STA associated to the Main BSS might see medium idle at the end of the NAV and attempt an UL TX on the main that is not observed by the AP because of RX payload decode on Aux
      So CTS DUR == 0 might make sense in this case, to make the AUX non-AP STA wait until NAV end and then send CTS DUR > 0 on both AUX and MAIN to let UL TX proceed while holding off Main UL TX

## Slide 20: Annex – Aux BSS UL RTS (3)
ED busy on main and nothing else
  AP might filter > -62 dBm noise from main to receive RTS on aux
  If RTS RX is possible, then again, CTS DUR == 0 is useful with CTS DUR > 0 at end of ED busy time
PHY SIG Length field decode with 3rd party color
  Discard/Ignore/IDLE medium, SR active
    TX CTS DUR >0 on Aux and Main
  Defer/BUSY, SR not active
    Defer Aux UL TX until the end of Main PPDU RX using CTS DUR == 0
    i.e. no RX of OBSS payload, FE power save condition
    i.e. defer is case of not decoding payload, but not declaring IDLE, no SR
    In this case, presumably, the TX of CTS on Aux is not going to bother the 3rd party receiver of the PPDU on the Main (i.e. SR not needed to TX CTS)
      If TX CTS would interfere, then AP may choose to not TX CTS
      Perhaps the rule is AP does NOT send CTS in this case, as SR condition is not met