## Slide 1: Multi-AP Group Formation
Date: 2019-10-10
Authors:
Name | Affiliations | Address | Phone | Email
Cheng Chen | Intel |  |  | cheng.chen@intel.com
Po-kai Huang |  |  |  | po-kai.huang@intel.com
Laurent Cariou |  |  |  | laurent.cariou@intel.com
Carlos Cordeiro |  |  |  | carlos.cordeiro@intel.com
Notes: September 2012

## Slide 2: Abstract
Most EHT Multi-AP contributions so far have primarily focused on how to leverage the coordination within a Multi-AP group, assuming some APs act as Triggering APs and others serve as Triggered APs.
In this presentation we study the fundamental framework of Multi-AP operations, i.e., the formation of a group of APs for various Multi-AP coordination functions.
We focus on the management/control role of one AP among a group of APs that participate in Multi-AP coordination functions. We do not consider the sequence-trigger roles, i.e., who can send Multi-AP trigger frames etc.
  We will call the set of these APs as an EHT Multi-AP group.
  For simplicity, we use terminologies of the Coordinator AP and Coordinated APs in the management domain to differentiae it from the Master AP and Slave APs used in the domain of specific trigger operations as in most previous presentations.

## Slide 3: Options for EHT Multi-AP group formation
Option 1: The specific Multi-AP group formation procedures are not defined in 11be.
  In 11be, we simply assume there already exists an EHT Multi-AP group with a pre-configured Coordinator AP.
  Leave the formation of the group, and the designation of the Coordinator AP to some methods that are implementation specific (e.g. through User or Service Provider configuration).
Option 2: We define a complete set of Multi-AP group formation procedures in 11be.

## Slide 4: EHT Multi-AP group formation
Generally, an EHT Multi-AP group should be formed in a relatively managed environment, such as enterprise network, factory, or within the same home. Deployment of APs in these scenarios are mostly static.
The selection of the Coordinator AP depends largely on topology, as the key requirement is all Coordinated APs must be able to talk to the Coordinator AP.
Coordinator AP
Coordinated AP1
Coordinated AP2
X

## Slide 5: Coordinator AP selection
Metric-based selection mechanisms may not work in an EHT Multi-AP group because:
  1. The metric-based selection mechanism can be easily complicated if there are multiple APs that want to become the Coordinator AP.
  2. Each pair of APs need to exchange the metric for Coordinator AP selection. The number of exchanges grow exponentially with the number of APs.
Dynamic change of the Coordinator AP has the following challenges:
  1. The topology within an EHT Multi-AP group is generally static and it is not necessarily true that any AP is able to communicate to the other APs.
  2. Once the Coordinator AP changes, how to ensure the Coordinated APs trust the new Coordinator AP?
  3. Once the Coordinator AP changes, all Coordinated APs and STAs within the group need to be notified. This will be a large overhead.

## Slide 6: Option 1 or 2?
In summary, EHT Multi-AP Group formation is more like a long-term configuration and should not change dynamically. As a result, Option 1 is preferred.
  EHT Multi-AP group formation and Coordinator AP selection could then be left to implementation specific mechanisms.
  However, in 11be, we need to define a hook for implementation specific operations, and other management-level group procedures such as the discovery of an EHT Multi-AP group, the discovery of the Coordinator AP, Multi-AP operation rules etc.