## Slide 1: Use Auto Repetition in low latency queue
Date: 2019-09-16
Authors:
Name | Affiliation | Address | Phone | Email
Tony Zeng | Huawei |  |  | tony.zengyan@huawei.com
Eric Wang |  |  |  | 
Yanbo Zhao |  |  |  | 
Xiaoshu Si |  |  |  | 

## Slide 2: Abstract
In this contribution, we introduce Auto Repetition (AR) mode which is designed dedicatedly to low latency flow in the multi-link operation.
In the multi-link operation, for a better QoS, one link can be dedicated for streams which need low latency. For such low latency streams, the link can be operated in an AR mode to guarantee a better reception possibility of the streams.

## Slide 3: Introduction
Recap1: The RTA-TIG recognizes that the worst-cast latency is the major challenge for real-time applications [1]. Some potential technical features are considered: predicable and efficient medium access, TSN extension, coordination between APs/BSS, and multi-link operation.
Recap2: A new low latency queue is recommended for latency critical traffic, especially for the less frequent and small packet [2].
Based on these ideas, the contribution further proposes a mechanism to enable an bounded latency and jitter in the transmission by using auto repetition mode.

## Slide 4: Bounded latency and jitter
Latency+jitter <15ms [1]
Latency+jitter <100ms [1]
Real-time gaming
Cloud gamming
Real-time video
Robotics (Drone control)
Reality: Applications require different QoS for latency and jitter
Requirement:
  Multiple low latency queues may be required
  A bounded latency and jitter may be required
Low latency queue
Entry of Packet #1
Latency budget
Entry of Packet #2
Latency budget
Time

## Slide 5: Current re-transmission
Trigger for re-transmission in many communication systems:
  No ACK
  NACK
Issues:
  ACK frame can be lost due to collision or interference, especially in a high packet loss environment
  Timeout normally exceed the latency boundary requirement
Active transmission mechanism is necessary
  Redundant, active and repeated transmission
  Robustness is enhanced by repetition frequency and spreading over time

## Slide 6: Auto repetition
Definition: Actively transmit a packet repeatedly according to dedicated rules.
Goal:
  To achieve a number of transmission for same packet within a time boundary in order to achieve “zero” packet error rate in 802.11 link
  To transmit a packet in an “exact time stamp” to avoid a low-latency packet stuck in the transmission and RTX queue
Advantages:
  Significantly decrease packet loss in the 802.11 link to avoid packet re-transmission in the upper layer.
  Increase the possibility that the packet will be correctly received.
Slide 6
Tony Zeng, Huawei
PHY
time
Packet enters the TID queue
Expected latency
First sent
Second sent
Third sent
Fourth sent
Assuming 4 repetition is required

## Slide 7: Schematic
MPDU
[(A)-MSDU]
EDCA queue
PHY processing
TID 0-7
Normal Link 1 & 2
Low Latency Link 3
New TID M?
Add new TID M or reuse TID 7 (as am example) for extreme low latency services.
EDCA mechanism is kept while TID M is mapped to low latency link .
In multi-link operation, a dedicated link can be allocated for low latency transmission
Modified EDCA mechanism
Notes: 1 rtx的位置；
2

## Slide 8: Schematic
MPDU/A-MPDU enter the AR Queue in the first transmission.
QoS requirement (i.e. latency budget), repetition number (# N) are configured
How to allocate the sending time is vendor discretionary.
The MPDU packet is sent repeatedly by N times during the latency budget.
MPDU4
MPDU5
MPDU6
MPDU7
MPDUN
…
TID M
Modified EDCA Queue
PHY
MPDU2
MPDU3
AQ queue replace Rtx Queue
First time to send
Enter the queue
Repeated send
Not finished repeated send:
re-enter the queue
MPDU1
time
Packet enters the TID queue
Expected latency
First sent
Second sent
Third sent
Fourth sent
Assuming 4 repetition is required
MUX
Notes: 1 rtx的位置；
2

## Slide 9: How to establish new TID and EDCA queue
How to create a TID queue:
  Method 1: RE-use the current TID: By exchanging a management message to confirm an existed TID is used for AR purpose.
  Method 2: To add new bits in the MAC Frame.
What’re the changes for EDCA queue
  The current access mechanism of EDCA needs to be modified to adapt to the concept of AR: consolidated backoff are required
  Each packet in this new queue needs to have its own countdown counter
  The countdown may be determined by the expected latency boundary and repetition number
  The EDCA queue can be dynamically created or re-use the current EDCA queue.

## Slide 10: Example in multi-band for low latency queues
QoS #1~m are low latency (e.g., <= x ms budget from Tx to Rx) required streams
The x ms latency is longer than the typical value of the round-trip latency (e.g., the mean value of the round-trip latency)
Apply retransmission based on ACK for this Class is meaningless because the first RTX will probably exceed x ms
The streams in this Class MUST be auto repeated by the transmitter at N times in total (where N is configured)
  The transmitter may conduct the “last chance” transmission to increase gain form the time diversity
The receiver should not ACK the packets in this AR path (unless it has special reason to do so).
The transmitter shall not resend the packets that are ACKed.
QoS #m+1~n are normal latency (e.g. > y ms budget from Tx to Rx) required streams
The ACK is expected to be received in less than y ms in statistic aspect (e.g. with respect to the mean value)
Normal RTX based on ACK is applied
  “Last chance” auto repetition MAY also be applied in this path to increase the reception possibility in transmitter discretion
Low latency Queue (modified EDCA Queue)
Link #1
MUX
AR Queue
Normal EDCA Queues
Link #2
MUX
RTX Queue
AR path
RTX path
Low latency band

## Slide 11: Consideration on multiple low latency queues
Low latency streams should be classified into different low latency queues. Each queue should be specified by QoS parameters, such as Tx-to-Rx latency value.
To further improve the robustness, repetition characteristics should be flexible, including repetition frequency, timing for last transmission.
For both the AR path and RTX path, the receiver must preserve the packet order to convey them to the upper layer.
The time stamp for the first transmission shall be kept in the further auto repetition or retransmission for the receiver to decide when to convey the packet to the upper layer.
Buffering and re-ordering of the low latency packet are required in the receiver side.

## Slide 12: Advantages
Low Tx-to-Rx latency queue brings better performance in latency guaranteed for time sensitive service.
By making use multi-link operation, to arrange a link for latency sensitive service further reduce the averaging transmission time and jitter because Low latency packets needn’t compete with other packets which are not latency sensitive.
Auto repetition enable an active and create a latency-jitter boundary for dedicated packet in specific queues.

## Slide 13: Straw Poll #1
Do you support to specify the Auto-Repetition (AR) mode for packet transmission?

## Slide 14: Straw Poll #2
Do you support that the low latency TID should be created for latency sensitive packets?

## Slide 15: Straw Poll #3
Do you support that the number of repetitions in the AR mode can be configured?

## Slide 16: References
[1] Kate Meng, “11-19-0065-06-0rta-rta-tig-summary-and-recommendations”
[2] Kate Meng, “11-19-1175-00-00be-considerations-of-new-queue-mechanisms-for-real-time-applications”,

## Slide 17: Thank you！