## Slide 1: Preamble Design in 11bd
Date: 2019-09-10
      Sept. 2019

## Slide 2: Background
In IEEE July meeting, TGbd passed the following motions:
  The preamble of 11bd PPDU shall include repeated L-SIG (RL-SIG) symbol after L-SIG
  NGV-SIG follows immediately after the RL-SIG in a 11bd PPDU
  11bd PHY shall define only one PPDU format
  802.11 NGV PAR requires that at least one mode that achieves at least 3dB lower sensitivity level (longer range)
  Design considerations in 11ax and 11be preamble format can be reused for 11bd
      Sept. 2019

## Slide 3: Recap: 11ax Extended Range PPDU
HE Extended Range (ER) SU PPDU format is shown below
  L-SIG and RL-SIG have 4 extra subcarriers as training subcarrier allowing more signaling bits in the following SIG field
  HE-SIG-A1 and HE-SIG-A2 have the same encoded bits and HE-SIG-A3 and HE-SIG-A4 have the same encoded bits
  Data bits in HE-SIG-A1(A3) are interleaved and the data bits in HE-SIG-A2(A4) are not interleaved
  HE-SIG-A1(A3, A4) use BPSK modulation while HE-SIG-A2 use QBPSK modulation
  The duplication of data bits in HE-SIG-A1(A2) and HE-SIG-A3(A4) can provide 3dB performance gain
      Sept. 2019
L-STF
HE-SIG
-A1
L-LTF
L-SIG
RL-SIG
HE-SIG
-A2
HE-SIG
-A3
HE-SIG
-A4
HE-STF, HE-LTF, Data, and PE
8us
8us
4us
4us
4us
4us
4us
4us

## Slide 4: Recap: High-level 11be Preamble
In contribution IEEE 802.11/19-1085 the following high-level preamble structure is proposed for 11be
  The EHT SIGs contains static bits (version bits) for differentiation and interoperation between EHT and future generations
  The auto-detection of the EHT and future generation frame formats are simplified through utilizing the version bits
  The definition of static bits (version bits) is for each 20MHz band
L-STF
L-LTF
L-SIG
RLSIG
L-STF
L-LTF
L-SIG
RLSIG
EHT SIGs
L-STF
L-LTF
L-SIG
RLSIG
…
…
;;;
…
      Sept. 2019

## Slide 5: Proposed 11bd Preamble Format
Based on 11ax and 11be preamble design, we propose the following structure of NGV-SIG for 11bd
  Adding 4 extra subcarriers in the L-SIG and RL-SIG which can be used as training subcarriers
    Increases the number of data bits for the NGV-SIG from 24 to 26
    Align with11ax design
  NGV-SIG1 and NGV-SIG2 have the same data bits
    NGV-SIG1 is interleaved and NGV-SIG2 is not interleaved to exploit diversity gain [5]
  NGV-SIG1 and NGV-SIG2 can use ½ BCC + BPSK for coding and modulation
  NGV-SIG can carry information bits for bandwidth, MCS level, number of spatial streams and midamble period, etc.
  NGV-SIG also includes version bits
    For future generation differentiation and simplification of auto detection
L-STF
NGV-SIG1
L-LTF
L-SIG
RL-SIG
Other NGV-Portion
NGV-SIG2
10MHz
16us
16us
8us
8us
8us
8us
      Sept. 2019

## Slide 6: Fields in NGV-SIG
The NGV-SIG may include the following fields
  MCS (including DCM): 4bits BW: 1bit NSTS :1bit
  LDPC extra symbol: 1bit Version: 2bits PPDU type: 1bits
  Midamble period: 2bits CRC: 4bits Tail: 6bits
  Coding: 1bit STBC: 1bit Beamformed: 1bit
  Reserved bit: 1bit
The above design includes 26 data bits in total, which just fits the design with L-SIG and RL-SIG having 4 extra training subcarriers.
      Sept. 2019

## Slide 7: Reference
IEEE 802.11-19/0514 Motion Booklet for IEEE 802.11 TGbd
IEEE 802.11-18/0861 802.11 NGV Proposed PAR
IEEE 802.11ax Draft 4.2
IEEE 802.11-18/1085 High-level EHT Preamble Structure
IEEE 802.11-15/0826r2 HE-SIGA transmission for range extension
      Sept. 2019

## Slide 8: SP#1
Do you support to add the version bits in the NGV-SIG field for future generation differentiation and simplification of auto detection?
Y: N: Abstain:
      Sept. 2019