## Slide 1: MAC layer design for LC
Date: 2019-09-18
Authors:
Name | Affiliation | Address | Phone | Email
Suhwook Kim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | suhwook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Jeongki Kim |  |  |  | jeongki.kim@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Abstract
We have discussed LC PHY layer in several F2F meetings
  Two LC PHYs were proposed and details are described
  We have decided mandatory PHY
So it is time to discuss and decide to MAC layer now

## Slide 3: MAC issues for LC
There is two big problems we have to decide before designing the LC MAC layer
  Channel access
    EDCA vs. HE MAC (OFDMA)
  Supporting mandatory PHY
    MAC operation of mandatory PHY

## Slide 4: Channel Access
There are some options of channel access for LC MAC and we have discussed some of them
  Option 1: EDCA without any change
  Option 2: EDCA with small modification
  Option 3: Simplified HE MAC
  Option 4: HE MAC without any change
Also we may adopt HCCA but it may not be a feasible solution because there is no chipset that implement it

## Slide 5: EDCA MAC (Level 0, 1)
If we decide to use EDCA MAC for LC,
  We can save time to market and reduce chipset price
  We may need small changes to support LC PHY characteristics
    As we have discussed, RTS/CTS would be one of options
  However, the latest technologies(i.e., OFDMA) are excluded in LC
  Performance is relatively poor than HE MAC

## Slide 6: HE MAC (Level 2, 3)
If we adopt HE MAC,
  We can support the new MAC features which are defined by HE MAC
    OFDMA, UL MU-MIMO, TWT, Spatial reuse, etc..
    However, HE MAC is quite complex thus we have to review which features are suitable for LC and how LC will adopt it
  We have better performance and LC can be embedded in 11ax chipset
  But, we may need to adopt HE MAC into LC and chipset price would be expensive

## Slide 7: Supporting mandatory PHY
Even though we have decide to define mandatory PHY, we may need to discuss how the mandatory PHY operates in MAC layer
  If a STA is implemented by mandatory PHY and optional PHY, the STA has to switch operating PHY from mandatory PHY to optional PHY
  If there are STAs that implement mandatory PHY only and STAs that implement optional PHY in single BSS, the AP has to support both type of STAs in same time

## Slide 8: Mandatory PHY
Management frames are define to support key functions so they shall be transmitted by mandatory PHY
  Probe request/response frame
  Authentication request/response frame
  (Re)Association request/response frame
  Beacon frame
  Action frame
  ETC…

## Slide 9: Mandatory PHY
If all management frames are transmitted by mandatory PHY, a STA implemented by mandatory PHY and optional PHY will operate as follows
  Scanning, authentication and association procedure is performed in mandatory PHY
  After association, the STA can transmit/receive data frame by operational PHY
  The STA may receive beacon frame at every TBTTs by mandatory PHY

## Slide 10: Mandatory PHY
The AP can altogether support the STA of two types at same time even though the AP cannot transmit to two PHYs at same time
  The AP can assign the section for the specific PHY using beacon frame

## Slide 11: Summary
We addressed and reviewed key MAC features for designing LC MAC
  Channel access
  Supporting mandatory PHY

## Slide 12: References
[1] 11-19-0757-02-00bb-lc-mac-submission.pptx

## Slide 13: Straw poll 1
Which option do you prefer for LC MAC?
  Option 1: LC MAC mandates EDCA and exclude HE MAC
  Option 2: LC MAC mandates EDCA and support HE MAC optionally
  Option 3: LC MAC mandates HE MAC
Note: EDCA and HE MAC can be slightly modified when applied to LC
Y
N
A

## Slide 14: Straw poll 2
Do you agree that all management frames shall be transmitted by mandatory PHY?
Y
N
A