## Slide 1: Discussion on TESLA Based Frame Authentication
Date: 2019-09-18
Authors:

## Slide 2: Abstract
TESLA based frame authentication has been proposed as a scheme for authenticating eBCS frames [1][2].
This presentation highlights a few shortcomings of the TESLA algorithm for TGbc members to consider.

## Slide 3: Recap: TESLA algorithm [2]
TESLA is an algorithm that enables all receivers check integrity and authenticate the source of each frame in multicast or broadcast data stream.
TESLA uses One-way key chain.
One-way key chain is based on the nature of one-way hash function.
  In case of Vi+1 = Hash(Vi)
    Calculating Vi+1 from Vi is easy.
    Calculating Vi from Vi+1 is difficult. (practically impossible)
Vi
Vi+1
easy
difficult

## Slide 4: Recap: Frame Sequence [2]
eBCS Info frame
Transmitted in TI interval
TK
TI
eBCS Data frames
  eBCS Info frame includes
  Ks,N (where s is the seq num of eBCS Info)
  Ks-1,L (where L is the last used key index)
  Ks-1,L+1 (if d = 2)
  Timestamp
  TI
  TK
  d
  eBCS Info sequence number
  Public key with CA signature
  Signature by the sender’s private key
Sender generates one-way key chain before
generating each eBCS Info frame
(Ks,N, Ks,N-1, Ks,N-2, …, Ks,0)
  eBCS Data frame includes
  Ks,i+2 (where s is the seq num of eBCS Info, d=2)
  As,i (Authenticator generated by the key K’s,i)
  Key index: i
  eBCS Info seq num: s

## Slide 5: Can it address all use cases?
The TESLA design intended for streaming services where continuous stream of traffic is broadcast.
  The scheme is not suitable if the frame transmissions are intermittent.
    For example event triggered aperiodic DL or UL
  Potential solution to aperiodic traffic: Transmitter sends dummy frames to keep a constant stream of frames carrying keys
    However, this will introduce unnecessary overhead
    Without such dummy broadcast, the receiver will be stuck waiting for the next set of frames to authenticate what was received so far (latency and memory requirements).

## Slide 6: Loss of a single Info frames = loss of a set Data of frames
If an info frame is lost, the set of frames sent during an interval TI cannot be verified.
  Channel conditions can frequently change, and there is no guarantee that all the receivers correctly receive the eBCS Info frame
eBCS Info frame
Transmitted in TI interval
TK
TI
eBCS Data frames
X

## Slide 7: Attack scenario: Injection of fake Data frames
Injection of false eBCS Data frames (i.e., frames carrying false authenticator information) can easily exhaust the receiver buffer
  For example:
    an attacker injects many eBCS Data frames that have the same sequence # and Key (both of which are not confidential info) but different data and authenticator
    By nature of the protocol, the receiver is required to store all frames as it doesn’t know which one is the correct one until the corresponding verification key disclosed later.
    In other words, there would be one correct data frame out of 100 frames, but the STA can only tell which one is correct after getting the key.

## Slide 8: Other considerations
The periodicity and timing of eBCS Info frame is not known a priori
  As a result, if the periodicity of the eBCS Info frame is large, a client device may burn power in monitoring the medium to receive the Info frame carrying the configuration information before it can join the eBCS service
    Note, the configuration or periodicity information can’t be carried in Beacon frames since beacons are not protected
Memory considerations: The algorithm will have an impact on memory requirement
  i.e., the receiver needs to buffer several frames before it can decrypt a frame that was received in the past.
  This may make it unsuitable for certain category of devices (e.g., cheap low power/low memory)
Latency – due to the key-chaining nature of the algorithm, it introduces inherent latencies
  i.e., receiver needs to wait for future frames before it can authenticate past frames
  May make it unsuitable for certain use cases that focus on real-time or ultra low-latency applications
Hardware impact?
  For use cases that need high speed data, the frame authentication may need to be done in hardware.
  This is a new algorithm that is not commonly seen in today’s systems
  There may be implementations that won’t be able to use existing hardware to work with this algorithm.
  This may go against BCS charter – i.e., to not require any hardware changes

## Slide 9: Summary
The document provides a few limitations of the TESLA that the TGbc members need to consider before deciding on whether to use it as a protocol for eBCS frame authentication.
The presenter requests that TGbc share the Tesla-based frame authentication proposal (e.g., [2]) with a wider group (e.g., 802.11 membership) to solicit feedback from experts in security domain.
  The objective is to help TGbc come-up with an authentication framework that works for all use cases and scenarios.

## Slide 10: Reference
[1]:11-19/0451: eBCS Frame Authentication Proposal
[2]: 11-19/1645: TESLA Based Frame Authentication