## Slide 1: 3GPP RAN1 status on NR-Unlicensed
Date: 2019-09-19
Authors:
Name | Affiliations | Address | Phone | email
Sindhu Verma | Broadcom |  |  | sindhu.verma@broadcom.com
Shubhodeep Adhikari | Broadcom |  |  | shubhodeep.adhikari@broadcom.com
David Boldy | Broadcom |  |  | david.boldy@broadcom.com

## Slide 2: Outline
This presentation provides a short high level update from the 3GPP RAN1 meeting RAN1#98 between 26/Aug – 30/Aug on the standardization of NR-Unlicensed, with a focus on fair coexistence with 802.11.
The presentation discusses status of the following topics:
Contention Window adaptation mechanisms in NR-U
LBT for a 16us gap after a DL transmission and before a UL transmission in a gNB-acquired COT in NR-U.
Short 25us LBT for NR-U control messages.
Common preamble between NR-U and Wi-Fi in 5 GHz and 6 GHz.
Multi-carrier LBT

## Slide 3: Contention Window adaptation mechanisms in NR-U
CW adaptation mechanisms have been partially agreed for the following cases:
COT initiated by an NR-U gNB and which has unicast DL data transmissions.
COT initiated by an NR-U gNB which doesn’t have any unicast DL data transmissions but only UL data transmissions.
COT initiated by an NR-U UE and which has UL data transmissions.
Note:
The principle of the CW being adapted based on errors at the start of the transmission/COT has been approximately adhered to.
However, for case 2 above, where the UL transmissions cannot occur at the start of the COT and where there can even be gaps/pauses between the DL transmission (similar to that of an 11ax trigger), the combined % error over all UL transmissions in the COT will be considered.
For all of the above 3 cases, there has been no decision yet on the % of errors among data transmissions that will lead to doubling the CW.
The agreement text in RAN1#98 on CW adaptation is put in the Appendix.

## Slide 4: LBT in the 16us gap after DL transmission and before UL transmission in a gNB-acquired COT in NR-U
In 11ax, UL transmissions after a trigger and within 16us of the trigger, need mandatory channel sensing (via both energy detection as well as preamble detection) in case the transmissions are longer than a specified duration. Such sensing is a good practice as it avoids collisions from nodes that are visible to the UL/client but not to the DL/AP.
The goal has been to put a similar principle for NR-U. However, as there has been no consensus on a common preamble, NR-U at least for now will restrict itself to energy detection only in the gap between the DL and UL transmission.
Note:
Energy detection involves sensing the channel for not less than 4us.
For NR-U, there has been no agreement so far on the number of such 4us sensing intervals within the 16us gap.
Many companies in 3GPP want only one such sensing interval in 16us.
However, 11ax has to do such sensing twice in order to meet the standards requirements.
Sensing twice is a more robust procedure to detect hidden nodes, in light of slot misalignment between NR-U and Wi-Fi and the absence of an additional layer of preamble detection. Note that absence of preamble detection also leads to sensing misalignment between NR-U and Wi-Fi which reduces the effectiveness of energy detection

## Slide 5: Other important unresolved topics
There have been no agreements on the following topics that are important for better coexistence between NR-U and Wi-Fi.
% of transmissions with fixed 25us LBT.
Multi-carrier LBT.
Common preamble.

## Slide 6: Agreements made in RAN1#98 on CW adaptation (1)
Agreement:
For a gNB initiated channel occupancy the reference duration for CWS adjustment is defined as follows.
For a CO with unicast PDSCH(s) and for each set of LBT bandwidths for which a single contention window is maintained, the reference duration for CWS adjustment is from the beginning of the CO until the end of the first slot where at least one unicast PDSCH is transmitted over all the resources allocated for the PDSCH, or until the end of the first transmission burst by the gNB that contains unicast PDSCH(s) transmitted over all the resources allocated for the PDSCH, whichever occurs earlier.
  If the CO has a unicast PDSCH, but doesn’t have any unicast PDSCH transmitted over all the resources allocated for that PDSCH, then, the duration of the first transmission burst by the gNB within the CO that contains unicast PDSCH(s) is the reference duration for CWS adjustment.
Agreement:
For a UE initiated channel occupancy the reference duration for CWS adjustment is defined as follows.
For a CO with PUSCH(s) and for each set of LBT bandwidths for which a single contention window is maintained, the reference duration for CWS adjustment is from the beginning of the CO until the end of the first slot where at least one PUSCH is transmitted over all the resources allocated for the PUSCH, or until the end of the first transmission burst by the UE that contains PUSCH(s) transmitted over all the resources allocated for the PUSCH, whichever occurs earlier.
  If the CO has a PUSCH, but doesn’t have any PUSCH transmitted over all the resources allocated for that PUSCH, then, the duration of the first transmission burst by the UE within the CO that contains PUSCH(s) is the reference duration for CWS adjustment.

## Slide 7: Agreements made in RAN1#98 on CW adaptation (2)
Agreement:
For a gNB initiated channel occupancy, for a DL burst without unicast PDSCH and with one or multiple UL grants, and for each set of LBT bandwidths for which a single contention window is maintained, CWS adjustment is based on the success or failure (FFS: CB, CBG, or TB) of reception of PUSCH transmissions in the granted resources
FFS: Details of CWS adjustment based on the reception of a successful transmission
FFS: Handling of PUCCH/PRACH/SRS and PUSCH without UL-SCH