## Slide 1: Compendium of motions related to the contents of the TGbe specification framework document
Date: 2020-06-17
Authors:

## Slide 2: September 2019 interim

## Slide 3: Motion 1
Move to add the followings to the 11be SFD:
For EHT PPDU, L-STF, L-LTF and L-SIG shall be transmitted at the beginning of the EHT PPDU.
For EHT PPDU, the first symbol after L-SIG shall be BPSK modulated.
Move: Ross Jian Yu Second: Bin Tian
Discussion: None.
Result:
Passes with unanimous consent
---------------------------------------------------------------------------------------------------------------
SP Result:
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1099-02-00be-preamble-structure-in-11be.pptx

## Slide 4: Motion 1a
Move to table Motion 2
Move: Osama Aboul Magd Second: Jarkko Knekt
Result: 43Y, 29N, 17A
Passes

## Slide 5: Motion 2
Move to add to the specification framework document:
  Define a TID-to-link mapping mechanism among the enabled links of a multi-link logical entity.
  Note: For each TID, TID-to-link mapping can be 1-to-1 or 1-to-many.
Move: Yongho Seok Second: Po-Kai Huang
Discussion: Yes.
Result:
Tabled
---------------------------------------------------------------------------------------------------------------
SP result: 56Y/9N/55A
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0979-02-00be-multi-link-operation-follow-up.pptx

## Slide 6: Motion 3a
Move to table Motion 3
Move: Osama Aboul Magd Second: Yunbo Li
Result: 26Y, 40N, 31A
Fails

## Slide 7: Motion 3
Move to add the followings to the 11be SFD:
  Multi-link logical entity: A logical entity that has one or more affiliated STAs. The logical entity has one MAC data service interface and primitives to the LLC and a single address associated with the interface, which can be used to communicate on the DSM.
  NOTE –A Multi-link logical entity allows STAs affiliated with the multi-link logical entity to have the same MAC address
  NOTE – The exact name can be changed
Move: Po-Kai Huang Second: Liwen Chu
Discussion: Yes.
Result: 51Y, 29N, 27A.
Fails
---------------------------------------------------------------------------------------------------------------
SP result:
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0822-04-00be-extremely-efficient-multi-band-operation.pptx

## Slide 8: Motion 4
Move to add the followings to the 11be SFD:
  Multi-link AP logical entity: A multi-link logical entity, where each STA affiliated with the multi-link logical entity is an AP.
  Multi-link non-AP logical entity: A multi-link logical entity, where each STA affiliated with the multi-link logical entity is a non-AP STA.
  NOTE – The MAC addresses setting of STAs affiliated with the Multi-link AP logical entity or Multi-link non-AP logical entity is TBD
Move: Po Kai Huang Second:
Discussion: Yes.
Result:
Deferred
--------------------------------------------------------------------------------------------------------------------------------
SP result:
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0822-04-00be-extremely-efficient-multi-band-operation.pptx

## Slide 9: Motion 5
Move to add the followings to the 11be SFD:
  Define a multi-link setup signaling exchange executed over one link initiated by a multi-link non-AP logical entity with a multi-link AP logical entity as follows:
  Capability for one or more links can be exchanged during the multi-link setup
  The multi-link AP logical entity serves as the interface to the distribution system (DS) for the multi-link non-AP logical entity after successful multi-link setup
  NOTE – The link identification is TBD
  NOTE – Details for non-infrastructure mode of operation TBD
Move: Po-Kai Huang Second:
Discussion: Yes
Result:
Deferred
---------------------------------------------------------------------------------------------------------------
SP result:
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0773-07-00be-multi-link-operation-framework.pptx

## Slide 10: Motion 6
Move to add the following text into 11be SFD:
  11be shall allow more than one Resource Units (RUs) to be assigned to a single STA
    Coding and interleaving schemes for multiple RUs assigned to a single STA are TBD.
    Maximum number of RUs (>1) assigned to a single STA is also TBD.
Move: Jianhan Liu Second: Bin Tian
Discussion: None.
Result:
Passes with unanimous consent
---------------------------------------------------------------------------------------------------------------
SP result:
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1126-01-00be-enhanced-resource-unit-allocation-schemes-for-11be.pptx

## Slide 11: Motion 7
Move to add the following text to the 11be SFD:
  The links between multi-link AP entity and multi-link STA entity may be disabled or enabled.
Move: Liwen Chu Second:
Discussion: Yes.
Result:
Deferred
---------------------------------------------------------------------------------------------------
SP result:
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0821-03-00be-multiple-band-discussion.pptx

## Slide 12: Motion 8
Move to add the following text into the 11be SFD
11be PPDU shall include the repeated L-SIG after L-SIG
Move: Dongguk Lim Second: Jianhan Liu
Discussion: Yes
Result: 37Y, 21N, 26A
Fails
---------------------------------------------------------------------------------------------------
SP result:
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1486-01-00be-further-discussion-for-11be-preamble.pptx

## Slide 13: Motion 9a
Move to table Motion 9
Move: Huizhao Wang Second: Srinivas Kandala
Result:13Y, 45N, 26A
Fails

## Slide 14: Motion 9
Move to add the following to the 802.11be SFD:
  Define mechanism(s) for multi-link operation that enables the following:
  An operational mode for concurrently exchanging frames on more than one link for one or more TID(s)
  An operational mode for restricting exchanging frames of one or more TID(s) to be on one link at a time
Move: Abhishek Patil Second: Po-Kai Huang
Discussion: Yes
Result: 63Y, 11N, 19A
Passes
---------------------------------------------------------------------------------------------------------------
SP result:
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1082-03-00be-multi-link-operation-dynamic-tid-transfer.pptx

## Slide 15: Motion 10
Move to add the following to the 11be spec framework document
  11be supports 320MHz and 160+160MHz PPDU.
Move: Bin Tian Second: Jianhan Liu
Discussion: None
Result:
Passes with unanimous consent
---------------------------------------------------------------------------------------------------------------
SP result: 61Y, 0N, 13A
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0797-01-00be-11be-320mhz-channelization-and-tone-plan.pptx

## Slide 16: Motion 11
Move to add the following to the 11be spec framework document
  11be uses the same subcarrier spacing for the data portion of EHT PPDU as 11ax data portion
Move: Bin Tian Second: Jianhan Liu
Discussion: None.
Result:
Passes with unanimous consent
---------------------------------------------------------------------------------------------------
SP result: 70Y, 0N, 10A
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0797-01-00be-11be-320mhz-channelization-and-tone-plan.pptx

## Slide 17: Motion 12
Move to add the following to the 11be spec framework document
For 11be
  Reuse 11ax tone plan for 20/40/80/160/80+80MHz PPDU
  320MHz and 160+160MHz use duplicated HE160 for OFDMA tone plan
Note: puncturing design TBD. Non-OFDMA 320MHz/160+160MHz tone plan TBD
Move: Bin Tian Second: Xiaogang Chen
Discussion: Yes.
Result:
Deferred
---------------------------------------------------------------------------------------------------------------
SP result: 42Y, 0N, 37A
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0797-01-00be-11be-320mhz-channelization-and-tone-plan.pptx

## Slide 18: Motion 13
Move to add the followings to the 11be SFD:
  Define the following multi-link operation
    Frames are transmitted independently over multiple links by STAs belonging to a multi-link capable device regardless of downlink or uplink
Move: Insun Jang Second: Jeongki Kim
Discussion: Yes.
Result:
Deferred
---------------------------------------------------------------------------------------------------------------
SP result:
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1144-04-00be-channel-access-for-multi-link-operation.pptx

## Slide 19: NOVEMBER 2019 PLENARY

## Slide 20: Motion 14
Move to add the following text into IEEE 802.11be SFD:
11be shall provide a joint NDP sounding scheme as optional mode for multiple-AP systems.
  Sequential sounding scheme that each AP transmits NDP independently and sequentially without overlapped sounding period of each AP can also be used in multi-AP systems.
Move: Jianhan Liu Second: Junghoon Suh
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1593-03-00be-joint-sounding-for-multi-ap-systems.pptx

## Slide 21: Motion 15
Move to add the following text into IEEE 802.11be SFD:
Joint NDP sounding scheme for multi-AP system with less or equal to total 8 antennas at AP has all antennas active on all LTF tones and uses 802.11ax P matrix across OFDM symbols.
Move: Jianhan Liu Second: Wook Bong Lee
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1593-03-00be-joint-sounding-for-multi-ap-systems.pptx

## Slide 22: Motion 16
Move to add the following text to the TGbe SFD
11be supports 240 MHz and 160+80 MHz transmission
  Whether 240/160+80 MHz is formed by 80MHz channel puncturing of 320/160+160 MHz is TBD
Move: Eunsung Park Second: Wook Bong Lee
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1066-03-00be-tone-plan-discussion.pptx

## Slide 23: Motion 17
Move to add the following text to the TGbe SFD
240/160+80 MHz bandwidth is constructed from three 80MHz channels which include primary 80MHz
Move: Eunsung Park Second: Wook Bong lee
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1889-02-00be-discussion-on-240mhz-bandwidth.pptx

## Slide 24: Motion 18
Move to add the following to the TGbe SFD
A 160MHz tone plan is duplicated for the Non-OFDMA tone plan of 320/160+160 MHz PPDU
  The 160 MHz tone plan is TBD
Move: Eunsung Park Second: Wook Bong Lee
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1492-03-00be-non-ofdma-tone-plan-for-320mhz.pptx

## Slide 25: Motion 19
Move to add the following to the TGbe SFD
12 and 11 null tones are placed at the left and right edges in each 160MHz segment for the Non-OFDMA tone plan of 320/160+160 MHz PPDU
Move: Eunsung Park Second: Wook Bong Lee
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1492-03-00be-non-ofdma-tone-plan-for-320mhz.pptx

## Slide 26: Motion 20
Move to add the following to the 11be SFD:
Shall allow the following asynchronous multi-link channel access
  Each of STAs belonging to a multi-link device performs a channel access over their links independently in order to transmit frames
  Downlink and uplink frames can be transmitted simultaneously over the multiple links
Move: Jeongki Kim Second: Eunsung Park
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1144-06-00be-channel-access-for-multi-link-operation.pptx

## Slide 27: Motion 21
Move to add the following to the 11be SFD:
Support a mechanism for multi-link operation
  An AP affiliated with an AP multi-link device can indicate the capabilities and operational parameters for one or more STAs of the multi-link device
  A non-AP STA affiliated with a non-AP multi-link device can indicate the capabilities for one or more non-AP STAs of the non-AP multi-link device
  Specific information of capabilities and operational parameters of multi-link device is TBD
Move: Jeongki Kim Second: Eunsung Park
Discussion: None
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1509-05-00be-discussion-on-multi-link-setup.pptx

## Slide 28: Motion 22
Move to add the followings to the 11be SFD:
The 802.11be amendment shall define mechanism(s) for an AP to assist a STA that communicates with another STA.
Move: Patrice NEZOU Second: Pascal VIGER
Discussion: Yes.
Result: 46Y, 1N, 44A (Passes).
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1117-02-00be-direct-link-mu-transmissions.pptx

## Slide 29: Motion 23
Move to add the followings to the 11be SFD:
Multi-link device (MLD): A device that has more than one affiliated STA and has one MAC SAP to LLC, which includes one MAC data service.
  NOTE–The device can be logical
  NOTE–It is TBD for a MLD to have only one STA.
  NOTE–Whether the WM MAC address of each STA affiliated with the MLD is the same or different is TBD
Move: Po-Kai Huang Second: Laurent Cariou
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0822-09-00be-extremely-efficient-multi-band-operation.pptx

## Slide 30: Motion 24
Move to add the followings to the 11be SFD:
AP multi-link device (AP MLD): A multi-link device, where each STA affiliated with the multi-link device is an AP.
Non-AP multi-link device (non-AP MLD): A multi-link device, where each STA affiliated with the multi-link device is a non-AP STA.
Move: Po-Kai Huang Second: Jeongki Kim
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0822-09-00be-extremely-efficient-multi-band-operation.pptx

## Slide 31: Motion 25
Move to add the followings to the 11be SFD:
Define a multi-link setup signaling exchange executed over one link initiated by a non-AP MLD with a AP MLD as follows:
  Capability for one or more links can be exchanged during the multi-link setup
  The AP MLD serves as the interface to the distribution system (DS) for the non-AP MLD after successful multi-link setup
NOTE–The link identification is TBD
NOTE–Details for non-infrastructure mode of operation TBD
Move: Po-Kai Huang Second: Jeongki Kim
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0773-08-00be-multi-link-operation-framework.pptx

## Slide 32: Motion 26
Move to add the followings to the 11be SFD:
A multi-link device can indicate capability to support exchanging frames simultaneously on a set of affiliated STAs to another multi-link device
Move: Po-Kai Huang Second: Laurent Cariou
Discussion: Yes.
Result: 66Y, 9N, 22A (Passes).
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0773-08-00be-multi-link-operation-framework.pptx

## Slide 33: Motion 27
Move to add the following to the spec-framework document
There shall be a 2 OFDM symbol long, jointly encoded Universal-SIG(U-SIG) field in the EHT preamble immediately after the RL-SIG
  The U-SIG will contain version independent fields. The intent of the version independent content is to achieve better co-existence among future 802.11 generations.
  In addition, the U-SIG can have some version dependent fields
  The size of the U-SIG for the case of an Extended Range Mode (if such a mode were to be adopted) is TBD
  The U-SIG will be sent using 52 data tones and 4 pilot tones per-20MHz
Move: Sameer Vermani Second: Xiaogang Chen
Discussion: None
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1519-05-00be-forward-compatibility-for-wifi-preamble-design.pptx

## Slide 34: Motion 28
Move to add the following to the spec-framework document
PHY version identifier field shall be one of the version independent fields in the U-SIG
  Purpose is to simplify auto-detection for future 802.11 generations, i.e, value of this field is used to identify the exact PHY version starting with 802.11be
  Exact location of this field is TBD
Move: Dongguk Lim Second: Eunsung Park
Discussion: None
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1486-08-00be-further-discussion-for-11be-preamble.pptx

## Slide 35: Motion 29
Move to add the following to the spec-framework document
The LENGTH field in L-SIG set to a value N such that mod(N,3) = 0
Move: Dongguk Lim Second: Rui Cao
Discussion: Yes.
Result: 68Y, 12N, 19A (Passes).
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1486-09-00be-further-discussion-for-11be-preamble.pptx

## Slide 36: Motion 29a
Move to table Motion 29
Move: Joseph Levy Second: Harry Bims
Result: 21Y, 42N, 22A (Fails).

## Slide 37: Motion 30
Move to add the following text to the TGbe SFD
The 802.11be amendment shall support a preamble puncture mechanism for an EHT PPDU transmitted to multiple STAs
Move: Oded Redlich Second: Ross Jian Yu
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1190-03-00be-improved-preamble-puncturing-in-802-11be.pptx

## Slide 38: Motion 31
Move to add the following text to the TGbe SFD
The 802.11be amendment shall support a preamble puncture mechanism for an EHT PPDU transmitted to a single STA
Move: Oded Redlich Second: Ross Jian Yu
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1190-03-00be-improved-preamble-puncturing-in-802-11be.pptx

## Slide 39: Motion 32
Move to add the followings to the 11be SFD:
Define mechanism(s) for multi-link operation that enables the following:
  Indication of capabilities and operating parameters for multiple links of an AP multi-link device (AP MLD)
  Negotiation of capabilities and operating parameters for multiple links during a single setup signaling exchange.
Move: Abhishek Patil Second: Jeongki Kim
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1525-02-00be-multi-link-association.pptx

## Slide 40: Motion 33
Move to add the following to the 11be spec framework document
11be reuses 11ax tone plan for 20/40/80/160/80+80MHz PPDU
For 320MHz and 160+160MHz PPDU, 11be uses duplicated HE160 for OFDMA tone plan
Move: Bin Tian Second: Tianyu Wu
Discussion: Yes.
Result: 78Y, 3N 29A (Passes)
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1521-02-00be-further-thoughts-on-11be-tone-plan.pptx

## Slide 41: Motion 34
Move to add the following to the 11be spec framework document
The 11be 320/160+160 MHz non-OFDMA tone plan uses duplicated tone plan of HE160
Note: puncturing design TBD
Move: Bin Tian Second: Sameer Vermani
Discussion: Yes.
Result: 51Y, 5N, 43A (Passes).
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1521-02-00be-further-thoughts-on-11be-tone-plan.pptx

## Slide 42: Motion 35
Move to add the following to the 11be spec framework document
11be 240/160+80 transmission consists of 3x80MHz segments while the tone plan of each 80MHz segment is the same as HE80 in 11ax
Move: Bin Tian Second: Tianyu Wu
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1521-02-00be-further-thoughts-on-11be-tone-plan.pptx

## Slide 43: Motion 36
Move to add the following text into IEEE 802.11be SFD:
A single block ack agreement is negotiated between two Multi-link devices (MLDs) for a TID that may be transmitted over one or more links.
Note: The format of the setup frames is TBD.
Move: Rojan Chitrakar Second: Jeongki Kim
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1512-06-00be-multi-link-acknowledgment.pptx

## Slide 44: Motion 37
Move to add the following text into IEEE 802.11be SFD:
Sequence numbers are assigned from a common sequence number space shared across multiple links of a Multi-link device (MLD), for a TID that may be transmitted to a peer Multi-link device over one or more links.
Move: Rojan Chitrakar Second: Abhishek Patil
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1512-06-00be-multi-link-acknowledgment.pptx

## Slide 45: Motion 38
Move to add the followings to the 11be SFD:
A MLD that supports multiple links can announce whether it can support transmission on one link concurrent with reception on the other link for each pair of links.
Note - The 2 links are on different channels
Note - Whether to define a capability of announcing the support transmission on one link concurrent with transmission on the other link is TBD.
Move: Liwen Chu Second: Tomoko Adachi
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1159-05-00be-multilink-operation-capability-announcement.pptx

## Slide 46: Motion 39
Move to add the following text to the 11be SFD:
An AP/non-AP multi-link device (MLD) can disable or enable one or more its links.
NOTE- An AP/non-AP multi-link device (MLD) can’t disable all its links.
Move: Liwen Chu Second: Jeongki Kim
Discussion:
Result:
RAN OUT OF TIME.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0821-04-00be-multiple-band-discussion.pptx

## Slide 47: Motion 39a
Move to bring from the table Motion 39
Move: Liwen Chu Second: Srinivas Kandala
Result: 57Y, 3N, 19A (Passes)

## Slide 48: Motion 39b
Move to amend Motion 39 by replacing with the following:
An AP/non-AP multi-link device (MLD) can negotiate to disable or enable one or more of its links. Exact signaling TBD.
Move: Liwen Chu Second: Manish Kumar
Discussion:
Result:
RAN OUT OF TIME.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0821-04-00be-multiple-band-discussion.pptx

## Slide 49: Motion 40
Move to add the followings to the 11be SFD:
A MLD has a MAC address that identifies the MLD management entity
For example, the MAC address can be used in multi-link setup between a non-AP MLD and an AP MLD
Move: Po-Kai Huang Second: Zhou Lan
Discussion: Yes.
Result: 62Y, 9N, 36A (Passes).
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-0822-09-00be-extremely-efficient-multi-band-operation.pptx

## Slide 50: Motion 41
Move to add the following to the TGbe SFD
Phase rotation is applied to the legacy preamble part of EHT PPDU
Coefficients applied to each 20MHz channel are TBD
Application to the other fields is TBD
Move: Eunsung Park Second: Wook Bong Lee
Discussion: Yes.
Result: 69Y, 5N, 22A (Passes).
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1493-01-00be-phase-rotation-for-320mhz.pptx

## Slide 51: Motion 42
Move to add the following to the spec-framework document:
The U-SIG shall contain the following version independent fields
  PHY version identifier: 3 bits
  UL/DL flag: 1 bit
Move: Sameer Vermani Second: Bin Tian
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1870-04-00be-further-ideas-on-eht-preamble-design.pptx

## Slide 52: Motion 43
Move to add the following to the spec-framework document:
There shall be a variable MCS and variable length EHT-SIG, immediately after the U-SIG, in an EHT PPDU sent to multiple users.
Move: Sameer Vermani Second: Steve Shellhammer
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1870-04-00be-further-ideas-on-eht-preamble-design.pptx

## Slide 53: Motion 44
Move to add the following to the spec-framework document:
The EHT-SIG (immediately after the U-SIG) in an EHT PPDU sent to multiple users shall have a common field and user-specific field(s).
  Special case compressed modes (e.g., full BW MU-MIMO) are TBD
Move: Sameer Vermani Second: Bin Tian
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1870-04-00be-further-ideas-on-eht-preamble-design.pptx

## Slide 54: Motion 45
Move to add the following to the spec-framework document:
The U-SIG is modulated in the same way as the HE-SIG-A field of 11ax.
  Extended range SU mode is TBD
Move: Sameer Vermani Second: Bin Tian
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1870-04-00be-further-ideas-on-eht-preamble-design.pptx

## Slide 55: Motion 46
Move to add the following to the 11be SFD:
Shall allow a multi-link device that has constraints to simultaneously transmit and receive on a pair of links to operate over this pair of links?
  Signaling of this constraints is TBD
Move: Sharan Naribole Second: Jeongki Kim
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1405-07-00be-multi-link-operation-channel-access-discussion.pptx

## Slide 56: Motion 47
Move to add the following text to 11be SFD:
The U-SIG includes Version-independent bits followed by Version-dependent bits.
  Version-independent bits have static location and bit definition across different generations/PHY versions.
  Version-dependent bits may have variable bit definition in each PHY version.
Move: Rui Cao Second: Sameer Vermani
Discussion: None.
Result: 66 Y, 6N, 27A (Passes).
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1540-07-00be-eht-preamble-design.pptx
Version-independent Bits
Version-dependent Bits

## Slide 57: Motion 48
Move to add the following text to 11be SFD?
The U-SIG field includes the following bits in Version-independent bits portion:
  BSS color, number of bits TBD
  TXOP duration, number of bits TBD
Move: Rui Cao Second: Xiaogang Chen
Discussion: Yes.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1540-07-00be-eht-preamble-design.pptx

## Slide 58: Motion 49
Move to add the following to the 11be SFD:
EHT PPDU shall have a RL-SIG field, which is a repeat of the L-SIG field, immediately following the L-SIG field.
Move: Xiaogang Chen Second: Sameer Vermani
Discussion: None.
Result: Approved unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1516-04-00be-11be-preamble-structure.pptx

## Slide 59: JANUARY 2020 INTERIM

## Slide 60: Motion 50
Move to add to the TGbe SFD:
the 802.11be amendment shall define mechanism(s) in support of priority access to a non-AP STA for national security (NS)/emergency preparedness (EP) Priority Service
Note: Non-AP STA for NS/EP Priority Service is a regular non-AP STA authorized to NS/EP Service
Move: Subir Das Second: Srinivas
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1901-04-00be-priority-access-support-in-ieee-802-11be-what-and-why.pptx

## Slide 61: Motion 51
Move to add the following text to 11be SFD:
For each of the enabled links, frame exchanges are possible when the corresponding non-AP STA of the enabled link is in the awake state.
  NOTE-A link is enabled when that link can be used to exchange frames subject to STA power states.
  NOTE-When a link is disabled (i.e. not enabled) by an MLD the frame exchanges are not possible.
Move: Minyoung Park Second: Po-Kai Huang
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1544-05-00be-multi-link-power-save-operation.pptx

## Slide 62: Motion 52
Move to add the following text to 11be SFD:
An AP of an AP MLD may transmit on a link a frame that carries an indication of buffered data for transmission on other enabled link(s)
Move: Minyoung Park Second: Po-Kai Huang
Discussion: Yes.
Result: 45Y, 7N, 23A (Passes)
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1544-05-00be-multi-link-power-save-operation.pptx

## Slide 63: Motion 53
Move to add the following to 11be SFD:
An AP that intends to use the resource (i.e., frequency or time) shared by another AP shall be able to indicate its resource needs to the AP that shared the resource.
Move: Yongho Seok Second: James Yee
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1788-01-00be-coordinated-ofdma-operation.pptx

## Slide 64: Motion 54
Move to add the following to 11be SFD:
802.11be defines a directional-based TID-to-link mapping mechanism among the setup links of a multi-link logical device (MLD)
  By default, after the multi-link setup, all TIDs are mapped to all setup links.
  The multi-link setup may include the TID-to-link mapping negotiation.
    TID-to-link mapping can have the same or different link-set for each TID unless a non-AP MLD indicates that it requires to use the same link-set for all TIDs during the multi-link setup phase.
      NOTE: Such indication method by the non-AP MLD is TBD (implicit or explicit).
  The TID-to-link mapping can be updated after multi-link setup through a negotiation, which can be initiated by any MLD
    Format TBD
      NOTE: When the responding MLD can not accept the update, it can reject the TID-to-link mapping update
Move: Yongho Seok Second: James Yee
Discussion: None.
Result: Passes unanimously.
-----------------------------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1358-04-00be-multi-link-operation-management.pptx

## Slide 65: Motion 55
Move to add the following to 11be SFD:
11be shall define a mechanism to determine whether an AP is part of an AP candidate set and can participate as a shared AP in Coordinated AP transmission initiated by a sharing AP.
Move: Cheng Chen Second: Po-Kai Huang
Discussion: Yes.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1931-02-00be-multi-ap-group-formation-follow-up.pptx

## Slide 66: Motion 56
Move to add the following to 11be SFD:
Define a procedure for an AP to share its frequency/time resources of an obtained TXOP with a set of APs
  Set of APs is TBD
Move: George Cherian Second: Duncan Ho
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1582-02-00be-coordinated-ap-time-and-frequency-sharing-in-a-transmit-opportunity-in-11be.pptx

## Slide 67: Motion 57
Move to add the following to 11be SFD:
An RU Allocation subfield is present in the Common field of the EHT-SIG field of an EHT PPDU sent to multiple users.
  Compressed modes are TBD
  Contents of RU allocation subfield are TBD
Move: Ross Jian Yu Second: Ming Gan
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0029-02-00be-preamble-structure-and-sig-contents.pptx

## Slide 68: Motion 58
Move to add the following to 11be SFD:
There exists at least one compressed mode in which RU Allocation subfield doesn’t exist in the Common field of the EHT-SIG field of an EHT PPDU sent to multiple users.
  Signaling method is TBD
Move: Ross Jian Yu Second: Ming Gan
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0029-02-00be-preamble-structure-and-sig-contents.pptx

## Slide 69: Motion 59
Move to add the following to 11be SFD:
The following subfields exist in U-SIG of an EHT PPDU sent to multiple users.
  EHT-SIG MCS
  Number of EHT-SIG Symbols
Move: Ross Jian Yu Second: Ming Gan
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0029-02-00be-preamble-structure-and-sig-contents.pptx

## Slide 70: Motion 60
Move to add the following to 11be SFD:
Coordinated OFDMA is supported in 11be, and in a coordinated OFDMA, both DL OFDMA and its corresponding UL OFDMA acknowledgement are allowed
Move: Liwen Chu Second: Ming Gan
Discussion: Yes.
Result: 25Y 3N 31A (Passes).
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1919-03-00be-coordinated-ofdma.pptx

## Slide 71: Motion 61
Move to add the following to 11be SFD:
The established block Ack agreement allows the QoS Data frames of the TID, aggregated within the A-MPDUs, to be exchanged between the two MLDs on any available link.
Move: Liwen Chu Second: Zhou Lan
Discussion: None.
Result: 47Y, 1N, 13A (Passes).
-----------------------------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1856-03-00be-a-mpdu-and-ba.pptx

## Slide 72: Motion 62
Move to add the following to 11be SFD:
For each block ack agreement, there exists one receive reordering buffer based on MPDUs in the MLD which is the recipient of the QoS Data frames for that block ack agreement.
The receive reordering buffer operation is based on the Sequence Number space that is shared between the two MLDs.
Move: Liwen Chu Second: Po-Kai Huang
Discussion: None.
Result: Passes unanimously.
-----------------------------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1856-03-00be-a-mpdu-and-ba.pptx

## Slide 73: Motion 63
Move to add the following to 11be SFD:
The receive status of QoS Data frames of a TID received on a link shall be signaled on the same link and may be signaled on other available link(s)
Move: Liwen Chu Second: Po-Kai Huang
Discussion: None.
Result: Passes unanimously.
-----------------------------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1856-03-00be-a-mpdu-and-ba.pptx

## Slide 74: Motion 64
Move to add the following to 11be SFD:
An AP of an AP MLD may transmit on a link a frame that carries an indication of individually addressed frames buffered for transmission on other enabled link(s)
  An non-AP MLD needs to be aware on which link(s) the AP MLD provides the indication
  The mechanism to determine on which link(s) the AP MLD provides the indication is TBD
An AP of an AP MLD may transmit on a link a frame that carries an indication of individually addressed frames buffered for transmission on any enabled links
  An non-AP MLD needs to be aware on which link(s) the AP MLD provides the indication
  The mechanism to determine on which link(s) the AP MLD provides the indication is TBD
Move: Liwen Chu Second: Laurent Cariou
Discussion: Yes.
Result:18Y 15N 15A (Fails)
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1617-02-00be-multi-link-power-save.pptx

## Slide 75: Motion 65
Move to add the following to 11be SFD:
11be supports a maximum of 16 spatial streams (total across all the scheduled STAs) for MU-MIMO
Move: Wook Bong Lee Second: Youhan Kim
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1877-01-00be-16-spatial-stream-support.pptx

## Slide 76: Motion 66
Move to add the following to 11be SFD:
11be defines a maximum of 16 spatial streams for SU-MIMO
Move: Wook Bong Lee Second: Youhan Kim
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1877-01-00be-16-spatial-stream-support.pptx

## Slide 77: Motion 67
Move to add the following to 11be SFD:
Setup a BA agreement for multi-link operation by using ADDBA request and ADDBA response frames.
Move: Yunbo Li Second: Ross Jian Yu
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1591-05-00be-ba-setup-for-multi-link-aggregation.pptx

## Slide 78: Motion 68
Move to add the following to 11be SFD:
A new element will be defined as a container to advertise and exchange capability information for multi-link setup.
Move: Yunbo Li Second: Ross Jian Yu
Discussion: None.
Result: 41Y 3N 18A (Passes)
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1549-05-00be-multi-link-association.pptx

## Slide 79: Motion 70
Move to add the following to 11be SFD:
11be shall define a mechanism to teardown an existing multi-link setup agreement
Move: Po-Kai Huang Second: Ming Gan
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1823-03-00be-multi-link-setup-follow-up.pptx

## Slide 80: Motion 71
Move to add the following to 11be SFD:
After multi-link setup between two MLDs, different GTK/IGTK/BIGTK in different links with different PN spaces are used
  GTK/IGTK/BIGTK in different links can be delivered in one 4-way handshake
Move: Po-Kai Huang Second: Ming Gan
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1822-04-00be-multi-link-security-consideration.pptx

## Slide 81: Motion 72
Move to add the following to 11be SFD:
An EHT AP supporting the Multi-AP coordination can send a frame (e.g., Beacon or other management frame) including capabilities of Multi-AP transmission schemes.
Note: Multi-AP transmission schemes are TBD (e.g., Coordinated OFDMA)
Move: Jeongki Kim Second: Ming Gan
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1895-02-00be-setup-for-multi-ap-coordination.pptx

## Slide 82: Motion 73
Move to add the following to 11be SFD:
An EHT AP which obtains a TXOP and initiates the Multi-AP coordination is the Sharing AP*
An EHT AP which is coordinated for the Multi-AP transmission by the Sharing AP is the Shared AP*
*Note: The name can be modified.
Move: Jeongki Kim Second: Ming Gan
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1895-02-00be-setup-for-multi-ap-coordination.pptx

## Slide 83: Motion 74
Move to add the following to 11be SFD:
802.11be shall include 1x EHT-LTF and 2x EHT-LTF
Move: Dandan Liang Second: Jung Hoon Suh
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1980-02-00be-eht-p-matrices-discussion.pptx

## Slide 84: Motion 75
Move to add the following to 11be SFD:
802.11be shall include 4x EHT-LTF
Move: Dandan Liang Second: Jung Hoon Suh
Discussion: None.
Result:Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0117-01-00be-eht-ltfs-design-for-wideband.pptx

## Slide 85: Motion 76
Move to add the following to 11be SFD:
Small-size RUs can only be combined with small-size RUs and large-size RUs can only be combined with large-size RUs.
RUs with equal to or more than 242 tones are defined as large-size RUs
RUs with less than 242 tones are defined as small-size RUs
Move: James Yee Second: Bin Tian
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1907-02-00be-multiple-ru-combinations-for-eht.pptx

## Slide 86: Motion 77
Move to add the following to 11be SFD:
Combination of small-size RUs shall not cross 20MHz channel boundary.
Move: James Yee Second: Youhan Kim
Discussion: None.
Result: 45Y, 17N , 20A (Fails)
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1907-02-00be-multiple-ru-combinations-for-eht.pptx

## Slide 87: Motion 69
Move to add the following to 11be SFD:
Combination of small-size RUs shall not cross 20MHz channel boundary.
  The combination that includes RU 106 plus center 26-tone RU case is TBD.
Move: Bin Tian Second: Ross Jian Yu
Discussion: None.
Result: 58Y, 8N, 10A (Passes)
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1907-02-00be-multiple-ru-combinations-for-eht.pptx

## Slide 88: Motion 78
Move to add the following to 11be SFD:
Only allowed small-RU combinations are RU106+RU26 and RU52+RU26.
Move: James Yee Second: Yongho Seok
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1907-02-00be-multiple-ru-combinations-for-eht.pptx

## Slide 89: Motion 79
Move to add the following to 11be SFD:
For 20 and 40 MHz PPDU, within 20MHz boundary, any contiguous RU26 and RU106 can be combined.
Move: James Yee Second: Yongho Seok
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1907-02-00be-multiple-ru-combinations-for-eht.pptx

## Slide 90: Motion 80
Move to add the following to 11be SFD:
For 20 and 40 MHz PPDU, the blue colored combination of RU52 and RU26 are allowed.
Move: James Yee Second: Yongho Seok
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1907-02-00be-multiple-ru-combinations-for-eht.pptx

## Slide 91: Motion 81
Move to add the following to 11be SFD:
For 80MHz PPDU, the blue colored combination of RU52 and RU26 are allowed.
Move: James Yee Second: Yongho Seok
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1907-02-00be-multiple-ru-combinations-for-eht.pptx

## Slide 92: Motion 82
Move to add the following to 11be SFD:
For LDPC coding, for combined RUs sent to a user with RU size less than 242-tone, a single tone mapper shall be used.
Move: Ross Jian Yu Second: Wook Bong Lee
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1914-04-00be-multiple-ru-discussion.pptx

## Slide 93: Motion 83
Move to add the following to 11be SFD:
11be supports EHT-LTF for 16 spatial streams.
Move: Jinsoo Choi Second: Wook Bong Lee
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1925-02-00be-consideration-of-eht-ltf.pptx

## Slide 94: Motion 84
Move to add the following to 11be SFD:
For a link setup between an AP MLD and a non-AP MLD, a non-AP STA operating on that link can send to an AP operating on that link an indication that (an)other non-AP STA(s) within the same non-AP MLD that has(have) transition to doze state is(are) in awake state
Move: Jeongki Kim Second: Abhishek Patil
Discussion: None.
Result: passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1510-06-00be-eht-power-saving-considering-multi-link.pptx

## Slide 95: Motion 85
Move to add the following to 11be SFD:
For the PPDU transmitted to MU, the User field having TBD bits is contained in the user specific field of EHT-SIG
  The User field indicates user information assigned to each RU similar to that used in HE MU PPDU
  Detailed descriptions are TBD
Move: Eunsung Park Second: Ross Jian Yu
Discussion: None.
Result: passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0022-01-00be-consideration-on-240-160-80-mhz-and-preamble-puncturing.pptx

## Slide 96: Motion 86
Move to add the following to 11be SFD:
For the OFDMA transmission in contiguous 240MHz, for one STA large size RU aggregation is allowed only within 160MHz which is composed of two adjacent 80MHz channels
For the OFDMA transmission in non-contiguous 160+80MHz, for one STA large size RU aggregation is allowed only within contiguous 160MHz or the other 80MHz, respectively
2x996+484 RU combinations is TBD
Move: Eunsung Park Second: Bin Tian
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0023-02-00be-multiple-ru-aggregation.pptx

## Slide 97: Motion 87
Move to add the following to 11be SFD:
For the OFDMA transmission in 320/160+160 MHz, for one STA large size RU aggregation is allowed only within primary 160 or secondary 160, respectively
  Note that primary 160 is composed of primary 80 and secondary 80 and secondary 160 is 160MHz channel other than primary 160 in 320/160+160 MHz
Exception: 3x996 is supported
3x996+484 RU combinations is TBD
Move: Eunsung Park Second: Bin Tian
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0023-02-00be-multiple-ru-aggregation.pptx

## Slide 98: Motion 88
Move to add the following to 11be SFD:
The U-SIG shall contain Bandwidth Information, carried as a version independent field.
  This field may also convey some puncturing information.
  Number of bits for this field is TBD.
Move: Sameer Vermani Second: Bin Tian
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0049-02-00be-ppdu-types-and-u-sig-content.pptx

## Slide 99: Motion 89
Move to add the following to 11be SFD:
The U-SIG shall contain a PPDU type field, carried as a version dependent field.
  Number of bits for this field is TBD.
Move: Sameer Vermani Second: Bin Tian
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0049-02-00be-ppdu-types-and-u-sig-content.pptx

## Slide 100: Motion 90
Move to add the following to 11be SFD:
CCA minimum BW resolution is 20MHz
Preamble puncturing resolution is 20MHz
Move: Bin Tian Second: Ross Jian Yu
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1869-02-00be-preamble-puncturing-and-ru-aggregation.pptx

## Slide 101: Motion 91
Move to add the following to 11be SFD:
In 11be, there is only one PSDU per STA for each link
Move: Bin Tian Second: Sameer Vermani
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1869-02-00be-preamble-puncturing-and-ru-aggregation.pptx

## Slide 102: Motion 92
Move to add the following to 11be SFD:
In 11be, for LDPC encoding each PSDU only uses one encoder
Move: Bin Tian Second: Sameer Vermani
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1869-02-00be-preamble-puncturing-and-ru-aggregation.pptx

## Slide 103: Motion 93
Move to add the following to 11be SFD:
In 80MHz non-OFDMA the following conditional mandatory (conditional on supporting puncturing) large RU combinations are supported
  Any one of four 242RU can be punctured
Move: Ron Porat Second: Youhan Kim
Discussion: Done.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1908-04-00be-multi-ru-support.pptx
RU size | Agg. BW | Notes
484+242 | 60 MHz | 4 options

## Slide 104: Motion 94
Move to add the following to 11be SFD:
In 160MHz non-OFDMA the following conditional mandatory (conditional on supporting puncturing) large RU combinations are supported
  Any one of eight 242RUs can be punctured
  Any one of four 484RUs can be punctured
Move: Ron Porat Second: Youhan Kim
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1908-04-00be-multi-ru-support.pptx
80MHz RU size | 80MHz RU size | Agg. BW | Notes
484 | 996 | 120 MHz | 4 options
484+242 | 996 | 140 MHz | 8 options

## Slide 105: Motion 95
Move to add the following to 11be SFD:
In 240MHz non-OFDMA the following conditional mandatory (conditional on supporting puncturing) large RU combinations are supported
  Any one of six 484RUs can be punctured
  Any one of three 996RUs can be punctured
Move: Ron Porat Second: Youhan Kim
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1908-04-00be-multi-ru-support.pptx
80MHz RU size | 80MHz RU size | 80MHz RU size | Agg. BW | Notes
484 | 996 | 996 | 200 MHz | 6 options
- | 996 | 996 | 160 MHz | 3 options

## Slide 106: Motion 96
Move to add the following to 11be SFD:
In 320MHz non-OFDMA the following conditional mandatory (conditional on supporting puncturing) large RU combinations are supported
  Any one of eight 484RUs can be punctured
  Any one of four 996RUs can be punctured
Move: Ron Porat Second: Youhan Kim
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1908-04-00be-multi-ru-support.pptx
80MHz RU size | 80MHz RU size | 80MHz RU size | 80MHz RU size | Agg. BW | Notes
484 | 996 | 996 | 996 | 280 MHz | 8 options
- | 996 | 996 | 996 | 240 MHz | 4 options

## Slide 107: Motion 97
Move to add the following to 11be SFD:
In 80MHz OFDMA the following large RU combinations are supported
Move: Ron Porat Second: Youhan Kim
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1908-04-00be-multi-ru-support.pptx
RU size | Agg. BW | Notes
484+242 | 60 MHz | 4 options

## Slide 108: Motion 98
Move to add the following to 11be SFD:
In 160MHz OFDMA the following large RU combinations are supported
Move: Ron Porat Second: Youhan Kim
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1908-04-00be-multi-ru-support.pptx
RU size | Agg. BW | Notes
484+996 | 120 MHz | 4 options

## Slide 109: Motion 99
Move to add the following to 11be SFD:
The following subfields exist in U-SIG and/or EHT-SIG of an EHT PPDU sent to single user:
  MCS
  NSTS
  GI+EHT-LTF Size
  Coding
Move: Ross Jian Yu Second: Youhan Kim
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0029-03-00be-preamble-structure-and-sig-contents.pptx

## Slide 110: Motion 100
Move to add the following to 11be SFD:
The following subfield exists in U-SIG or EHT-SIG of an EHT PPDU sent to multiple users:
  GI+EHT-LTF Size
Move: Ross Jian Yu Second: Youhan Kim
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0029-03-00be-preamble-structure-and-sig-contents.pptx

## Slide 111: Motion 101
Move to add the following to 11be SFD:
At any point in time, a TID shall always be mapped to at least one link that is set up, unless admission control is used
Move: Laurent Cariou Second: Po-Kai Huang
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1924-01-00be-multilink-steps-for-using-a-link.pptx

## Slide 112: Motion 102
Move to add the following to 11be SFD:
Management frames are allowed on all enabled links, following baseline
Move: Laurent Cariou Second: Po-Kai Huang
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1924-01-00be-multilink-steps-for-using-a-link.pptx

## Slide 113: Motion 103
Move to add the following to 11be SFD:
If a TID is mapped in UL to a set of enabled links for a non-AP MLD, then the non-AP MLD can use any link within this set of enabled links to transmit data frames from that TID
If a TID is mapped in DL to a set of enabled links for a non-AP MLD, then:
  the non-AP MLD can retrieve buffered BUs corresponding to that TID on any links within this set of enabled links
  The AP MLD can use any link within this set of enabled links to transmit data frames from that TID, subject to existing restrictions for transmissions of frames that apply to those enabled links
  An example of restriction is if the STA is in doze state
Move: Laurent Cariou Second: Minyoung Park
Discussion: Yes.
Result: 25Y, 3N, 21A (Passes)
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1924-01-00be-multilink-steps-for-using-a-link.pptx

## Slide 114: Motion 104
Move to add the following to 11be SFD:
A non-AP MLD monitors and performs basic operations (such as traffic indication, BSS parameter updates, etc.) on one or more link(s)
Move: Abhishek Patil Second: Youhan Kim
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1526-03-00be-multi-link-power-save.pptx

## Slide 115: Motion 105
Move to add the following to 11be SFD:
A link, that is setup as part of a multi-link setup, is defined as Enabled if that link can be used for frame exchange and at least one TID is mapped to that link
  Note: frame exchange on a link is subject to the power state of the corresponding non-AP STA
Move: Abhishek Patil Second: Yongho Seok
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1528-05-00be-multi-link-operation-link-management.pptx

## Slide 116: Motion 106
Move to add the following to 11be SFD:
An AP MLD can recommend a non-AP MLD to use one or more enabled links
  The AP’s indication could be carried in a broadcast or a unicast frame
Move: Abhishek Patil Second: George Cherian
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1904-03-00be-mlo-link-management-follow-up.pptx

## Slide 117: Motion 107
Move to add the following to 11be SFD:
The extra 4 subcarriers are applied to L-SIG and RL-SIG.
  The indices for extra subcarriers are [-28, -27, 27, 28]
  The extra subcarriers are BPSK modulated
  The coefficients [-1 -1 -1 1 ] as in 11ax are mapped to the extra subcarriers
Move: Dongguk Lim Second: Ross Jian Yu
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/20/11-20-0019-01-00be-11be-ppdu-format.pptx

## Slide 118: Motion 108
Move to add the following to 11be SFD:
The value of the RA/TA fields sent over-the-air in the MAC header of a frame is the MAC address of the STA affiliated with the MLD corresponding to that link
Move: Duncan Ho Second: Po-Kai Huang
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1899-07-00be-mla-mac-addresses-considerations.pptx

## Slide 119: Motion 109
Move to add the following to 11be SFD:
The MAC address of each affiliated AP within an AP MLD shall be different from each other unless the affiliated APs cannot perform simultaneous Tx/Rx operation (e.g., due to near band in-device interference), in which case the MAC address properties are TBD
  Note: it is TBD whether we allow the operation of an AP MLD without simultaneous Tx/Rx operation
Move: Duncan Ho Second: Yongho Seok
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1899-07-00be-mla-mac-addresses-considerations.pptx

## Slide 120: Motion 110
Move to add the following to 11be SFD:
Each non-AP STA affiliated with a non-AP MLD that is operating on an enabled link maintains its own power state/mode
Move: Abhishek Patil Second: Rojan Chitrakar
Discussion: None.
Result: Passes unanimously.
---------------------------------------------------------------------------------------------------------------------------------
Ref: https://mentor.ieee.org/802.11/dcn/19/11-19-1528-05-00be-multi-link-operation-link-management.pptx

## Slide 121: JUNE 11, 2020, TELECONFERENCE

## Slide 122: Motion 111
Move to add to the 11be SFD candidate specification text in 11-20/566r28 that is identified with the following tags:
  SP0611-01, SP0611-02, SP0611-03, SP0611-04, SP0611-05, SP0611-06, SP0611-07, SP0611-08, SP0611-09, SP0611-10, SP0611-11, SP0611-12, SP0611-13, SP0611-14, SP0611-15, SP0611-16, SP0611-17, SP0611-18, SP0611-19, SP0611-20, SP0611-21, SP0611-22, SP0611-23, SP0611-24, SP0611-25, SP0611-26, SP0611-27, SP0611-28, SP0611-29, SP0611-30, SP0611-31, SP0611-32, SP0611-33, SP0611-34, SP0611-35, SP0611-36
Move: Bin Tian Second: Edward Au
Discussion: None.
Result: Approved by unanimous consent.
Note: These are all candidate SFD texts highlighted in green

## Slide 123: Motion 112
Move to add to the 11be SFD candidate specification text in 11-20/566r28 that is identified with the following tags:
  SP1, SP2, SP3, SP4, SP5, SP6, SP7, SP8, SP9, SP10, SP11, SP12, SP13, SP14, SP15, SP16, SP17, SP18, SP19, SP20, SP21, SP22, SP23, SP24, SP25, SP26, SP27, SP28, SP29, SP30, SP31, SP32, SP33, SP34, SP35, SP36, SP37, SP38, SP39, SP40, SP41, SP42, SP43, SP44, SP45, SP46, SP47, SP48, SP49, SP50, SP51, SP52, SP53, SP54, SP55
Move: Laurent Cariou Second: Bin Tian
Discussion: Clarificatory discussion.
Result: Approved by unanimous consent.
Note: These are all candidate SFD texts highlighted in yellow that have not received a request for further discussion

## Slide 124: Motion 113
Move to add to the 11be SFD candidate specification text in 11-20/566r28 that is identified with the following tags:
  SP28
Move: Wook Bong Lee Second: Bin Tian
Discussion: Yes, discussion.
Preliminary Result: Motion Passes (69Y, 20N, 38A)
Amended Result*: Motion Passes (66Y, 19N, 35A)
Note: These are all candidate SFD texts highlighted in yellow that have received a request for further discussion
* Amended result accounts for removal of 7 votes of non-voting members.

## Slide 125: Motion 114
Move to add to the 11be SFD candidate specification text in 11-20/566r28 that is identified with the following tags:
  SP5
Move: Abhishek Patil Second: George Cherian
Discussion: No further discussion.
Preliminary Result: Motion Passes (71Y, 23N, 27A)
Result*: Motion Passes (70Y, 21N, 25A)
Note: These are all candidate SFD texts highlighted in yellow that have received a request for further discussion
* Amended result accounts for removal of 5 votes of non-voting members.