## Slide 1: Agenda for IEEE 802.11 Coexistence SC meeting in Hawaii in November 2019
12 November2019
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: Welcome to the 15th F2F meeting of the Coex SC in Hawaii in November 2019
  The IEEE 802.11 PDED ad hoc was formed in September 2016 at the Warsaw interim meeting
  The IEEE 802.11 PDED ad hoc met in San Antonio (Nov 2016), Atlanta (Jan 2017), Vancouver (Mar 2017) and Daejeon (May 2017)
  In Daejeon in May 2017 it was decided to convert the IEEE 802.11 PDED ad hoc into the IEEE 802.11 Coexistence SC
  The IEEE 802.11 Coexistence SC met in Berlin (July 2017), Hawaii (Sept 2017), Orlando (Nov 2017), Irvine (Jan 2018), Chicago (Mar 2018), Warsaw (May 2018), San Diego (July 2018), Hawaii (Sept 2018), Bangkok (Nov 2018), St Louis (Jan 2019), Vancouver (Mar 2019), Atlanta (May 2019), Vienna (Jul 2019) & Hanoi (Nov 2019) and will meet twice this week
    Wed PM1
    Thu PM1 (any motions)

## Slide 3: The first task for the Coex SC today is not to appoint a secretary
  It is important to keep proper minutes of all Coexistence SC meetings
  Fortunately, Guido Hiertz (Ericsson) agreed in Berlin (in July 2017) to be appointed the IEEE 802.11 Coexistence SC’s permanent Secretary …

## Slide 4: The Coex SC will review the official IEEE-SA patent material for pre-PAR groups

## Slide 5: Participant behavior in IEEE-SA activities is guided by the IEEE Codes of Ethics & Conduct
  All participants in IEEE-SA activities are expected to adhere to the core principles underlying the:
    IEEE Code of Ethics
    IEEE Code of Conduct
  The core principles of the IEEE Codes of Ethics & Conduct are to:
    Uphold the highest standards of integrity, responsible behavior, and ethical and professional conduct
    Treat people fairly and with respect, to not engage in harassment, discrimination, or retaliation, and to protect people's privacy.
    Avoid injuring others, their property, reputation, or employment by false or malicious action
  The most recent versions of these Codes are available at
    http://www.ieee.org/about/corporate/governance
Approved slide

## Slide 6: Participants in the IEEE-SA “individual process” shall act independently of others, including employers
  The IEEE-SA Standards Board Bylaws require that “participants in the IEEE standards development individual process shall act based on their qualifications and experience”
  This means participants:
    Shall act & vote based on their personal & independent opinions derived from their expertise, knowledge, and qualifications
    Shall not act or vote based on any obligation to or any direction from any other person or organization, including an employer or client, regardless of any external commitments, agreements, contracts, or orders
    Shall not direct the actions or votes of other participants or retaliate against other participants for fulfilling their responsibility to act & vote based on their personal & independently developed opinions
  By participating in standards activities using the “individual process”, you are deemed to accept these requirements; if you are unable to satisfy these requirements then you shall immediately cease any participation
Approved slide

## Slide 7: IEEE-SA standards activities shall allow the fair & equitable consideration of all viewpoints
  The IEEE-SA Standards Board Bylaws (clause 5.2.1.3) specifies that “the standards development process shall not be dominated by any single interest category, individual, or organization”
    This means no participant may exercise “authority, leadership, or influence by reason of superior leverage, strength, or representation to the exclusion of fair and equitable consideration of other viewpoints” or “to hinder the progress of the standards development activity”
  This rule applies equally to those participating in a standards development project and to that project’s leadership group
  Any person who reasonably suspects that dominance is occurring in a standards development project is encouraged to bring the issue to the attention of the Standards Committee or the project’s IEEE-SA Program Manager
Approved slide

## Slide 8: IEEE SA Copyright Policy
  By participating in this activity, you agree to comply with the IEEE Code of Ethics, all applicable laws, and all IEEE policies and procedures including, but not limited to, the IEEE SA Copyright Policy.
    Previously Published material (copyright assertion indicated) shall not be presented/submitted to the Working Group nor incorporated into a Working Group draft unless permission is granted.
    Prior to presentation or submission, you shall notify the Working Group Chair of previously Published material and should assist the Chair in obtaining copyright permission acceptable to IEEE SA.
    For material that is not previously Published, IEEE is automatically granted a license to use any material that is presented or submitted.
Approved slide

## Slide 9: IEEE SA Copyright Policy
  The IEEE SA Copyright Policy is described in the IEEE SA Standards Board Bylaws and IEEE SA Standards Board Operations Manual
    IEEE SA Copyright Policy, see:
      Clause 7 of the IEEE SA Standards Board Bylaws
      Clause 6.1 of the IEEE SA Standards Board Operations Manual
  IEEE SA Copyright Permission
  IEEE SA Copyright FAQs
  IEEE SA Best Practices for IEEE Standards Development
  Distribution of Draft Standards (see Clause 6.1.3 of the SASB Operations Manual)
Approved slide

## Slide 10: Do we even need to worry about coexistence with 5G?
  For many years, it has been observed that having an odd numbered WG is an apparent pre-condition for success in IEEE 802
    ie 802.1, 802.3, 802.11, 802.15 (?)
  It has now apparently been claimed that “even” the cellular world is afflicted with an “odd” problem
    And then again some of it is weirdly occult, with a number of people feeling obliged to note that only even number radio iterations (i.e. 2G, 4G) turn out to be successful, source: realwireless
  So maybe we don’t need to worry about coexistence between IEEE 802.11 and 5G based NR-U … 

## Slide 11: The Coex SC will consider a proposed agenda for Hawaii in November 2019
Proposed Agenda
  Bureaucratic stuff,
    Scope of IEEE 802.11 Coexistence SC (a reminder)
    Approve minutes
  What is happening this week? (in no particular order)
    Update of unlicensed LTE deployment
    Review of “important issues”
    Review of inbound/outbound LSs
      Update on outbound LS related to Coexistence Workshop
      Review of inbound LS on CW update from ETSI BRAN
    …

## Slide 12: The Coex SC will consider a proposed agenda for Hawaii in November 2019
Proposed Agenda
    Review of recent ETSI BRAN activities
      Chair election
      EN 301 893 issues (5 GHz)
        Paused COT
        Use of no/short LBT for control signalling
        CW adjustment mechanisms with delayed acks (including inbound LS)
        Blocking energy/reservation signals
        Spectral mask (will be discussed on Thursday PM1, based on a request)
        Floating thresholds & preamble detection
      EN 303 687 issues (6 GHz)
        Alternative WI
        6GHz ED threshold in 6GHz Review of recent 3GPP RAN/RAN1 activities
    Review of recent 3GPP RAN/RAN1 activities (Thursday, by request)
    Review of recent WBA activities
    Discussion of extension of Coex SC charter
    Motions (Thursday PM1)
  Other business

## Slide 13
  Scope of IEEE 802.11 Coexistence SC

## Slide 14: The agreed Coex SC scope focuses on ensuring 802.11ax has fair access to global unlicensed spectrum
Discuss the use of PD, ED or other 802.11 coexistence mechanisms with the goal of promoting “fair” use of unlicensed spectrum
Promote an environment that allow IEEE 802.11ax “fair access” to global unlicensed spectrum
Will initially focus on liaising with 3GPP RAN/RAN1/RAN4 but may also lead to interactions with regulators and other stakeholders
Will probably not conclude at least until RAN4’s 802.11/LAA coexistence testing is defined and successfully executed
May require the SC to consider other simulations and results of tests of potential LAA/802.11 coexistence mechanisms
Will initially focus on encouraging a “technology neutral” solution in the next revision of EN 301 893 that allows IEEE 802.11ax fair access to unlicensed spectrum in Europe (noting the European approach is likely to have global impact)
The effort will also focus on allowing 802.11ax to use innovative mechanisms for frequency reuse without compromising the goal of fair access

## Slide 15: Coex SC will close when determined by the 802.11 WG or 802.11ax is ratified
IEEE 802.11 Coexistence SC close down criteria
  The SC is closed by the IEEE 802.11 WG
    … after it is determined that the SC is unlikely to make further progress towards its goals
  IEEE 802.11ax completes Sponsor Ballot
    … noting that the Coexistence SC ad hoc is unlikely to be relevant at that point anyway

## Slide 16: The Coex SC may discuss and consider a new scope to extend its life beyond 802.11ax on Thu
  The question of coexistence between Wi-Fi and various LTE based technologies has been “hot” for the last 4+ years
  The Coex SC is scheduled to close when 802.11ax completes Sponsor Ballot (now called Standards Committee Ballot) in early 2020
  However, here is no reason to think that coexistence will not remain a vitally important issue beyond the completion of IEEE 802.11ax as:
    IEEE 802.11be is developed
    ETSI BRAN develops a Harmonised standard for 6 GHz operation
  As the ratification of IEEE 802.11ax get closer the Coex SC may want to consider a scope extension
  It is proposed the SC continue this discussion at the end of the agenda (on Thu), when participants will have a better idea of the potential ongoing work for the SC … but think about it in the meantime

## Slide 17
  Minutes

## Slide 18: The Coex SC will consider approval of its meeting minutes from Hanoi in Sept 2019
  The minutes for the Coex SC at the Hanoi meeting in Sept 2019 are available on Mentor:
    See 11-19-1776-00
  Motion:
    The IEEE 802 Coex SC approves 11-19-1776-00 as minutes of its meeting in Hanoi in Sept 2019
    Moved:
    Seconded:
    Result:

## Slide 19
  Agenda items
  Unlicensed LTE deployment

## Slide 20: Latest stats conform that there is growing interest in LAA, suggesting good coexistence will be important
Technology | Stage | GSMA1 (July 2018) | GSA2 (Oct 2018) | GSA3 (Jan 2019) | GSA4 (Jul 2019) | GSA4 (Nov 2019)
LAA | Planned | 23 | 22 | 26 | 29 | 30
 | Deployed | 4 | 6 | 6 | 8 | 8
eLAA | Planned | ? | 1 | 1 | 1 | 1
 | Deployed | ? | 0 | 0 | 0 | 0
LWA | Planned | ? | 2 | 2 | 2 | 2
 | Deployed | ? | 1 | 1 | 1 | 1
LTE-U | Planned | ? | 8 | 8 | 8 | 8
 | Deployed | ? | 3 | 3 | 3 | 3
1 GSMA (July 2018)
2 GSA: Evolution from LTE to 5G: Global Market Status (Nov 2018)
3 GSA: LTE in unlicensed and shared spectrum (Jan 2019)
4 GSA: Evolution from LTE to 5G: Global Market Status (Aug 2019)
5 LTE Unlicensed - LTE in Unlicensed and Shared Spectrum (Nov 2019)

## Slide 21: The number planned/testing and deployed LAA networks is slowly increasing
Chart: Globally planned/testing & deployed LAA networks
| 43282 | 43374 | 43466 | 43647 | 43770
Planned, testing | 23 | 22 | 26 | 29 | 30
Deployed | 4 | 6 | 6 | 8 | 8

## Slide 22
  Agenda items
  Outbound LS

## Slide 23: A LS was sent to multiple organisations notifying them of the Coex Workshop results/documents
  In Hanoi, the Coex SC agreed to send LSs to 3GPP RAN, 3GPP RAN1, ETSI BRAN, WFA, WBA & GSMA notifying them of the availability of:
    Documents from the IEEE 802.11 Workshop (agenda, minutes, papers)
    Results from the post workshop surveys (along with a caveat on their use)
  The 802.11 WG sent the LS to these organisations and 5G-ACIA
    Sample LS is embedded to right
  Acknowledgements were received from 4 out of 6:
    WFA
    5G ACIA
    ETSI BRAN
    3GPP RAN1
    3GPP RAN
    GSMA

## Slide 24
  Agenda items
  Inbound LS

## Slide 25: The 802.11 WG received a LS from ETSI BRAN related to CW update requirements
  ETSI BRAN has been discussing requirements for the CW updates in LBT and appear to be converging on a consensus position
  ETSI BRAN has sent the IEEE 802.11 Coex SC a LS notifying the WG of the proposed revised requirements., which
    Explicitly enable broadcasts, as used in 802.11
    Enable delayed ack/nacks, as mostly used in LAA/NR-U
  The LS encourages the WG to analyze the requirements on the CW update procedure, particularly the aspect related to no bias in providing transmission feedback
    See 11-19-1777-00
  The Coex SC will discuss the material later in the agenda, including if and how we want to respond to the LS from ETSI BRAN

## Slide 26
  Agenda items
  Important issues?

## Slide 27: WBA & post workshop surveys will guide the SC on the importance of various coexistence issues
Chart: 
| Use of 802.11 preambles or common preambles for coexistence | Energy Detection only vs. Preamble or Energy Detection vs. both | Multi-channel sharing mechanisms | Use of no/short LBT for control signaling | Blocking energy/reservation signals | Synchronous access proposals in U-NII-7 | Contention Window adjustment mechanisms with delayed acknowledgements | Something else | Don't know | None of these | Prefer not to say
Post workshop survey | 0.57143 | 0.55556 | 0.31746 | 0.38095 | 0.30159 | 0.1746 | 0.2381 | 0.063492 | 0.063492 | 0.031746 | 0.095238
WBA survey | 0.5 | 0.36 | 0.36 | 0.22 | 0.1 | 0.08 | 0.04

## Slide 28
  Relationship topics
  ETSI BRAN activities

## Slide 29: BRAN#103 elected a new Chair and discussed various 5 & 6 GHz related issues
  ETSI BRAN #103 was held 7-10 Oct 2019 in Sophia Antipolis
  BRAN#103 discussed various issues of interest to the Coex SC
    Chair election
    EN 301 893 issues (5 GHz)
      Paused COT
      Use of no/short LBT for control signalling
      CW adjustment mechanisms with delayed acks (including inbound LS)
      Blocking energy/reservation signals
      Spectral mask
      Floating thresholds & preamble detection
    EN 303 687 issues (6 GHz)
      Alternative WI
      6GHz ED threshold in 6GHz
    Next meetings

## Slide 30
  Relationship topics
  ETSI BRAN activities
  Chair election

## Slide 31: ETSI BRAN elected a new Chair … congratulations to Guido Hiertz
  ETSI BRAN elected a new Chair … congratulations to Guido Hiertz!
  The election was very close … and a little controversial
    R1 was 52%/48% (threshold is 71%) and R2 was 55%/45% (threshold is 50%)
    It was observed that there were many late registrations (60 out of 189), many voters had never attended an ETSI BRAN meeting, and probably never will
    However, it is important to note that this behaviour is completely within the rules
  The election result suggests a deep concern from the cellular industry about the perceived influence of the Wi-Fi industry in ETSI BRAN
    One of the candidates was generally perceived to be aligned with the Wi-Fi industry, and the other with the cellular industry; the latter won!
    Note: the Chair is required to be neutral and so it actually does not matter who won the election, as long as they run the ETSI BRAN professsionally
  The message to the Wi-Fi industry from this election result should be that the work of ETSI BRAN is important; the cellular folk certainly think so!

## Slide 32
  Relationship topics
  ETSI BRAN activities
  EN 301 893 issues
  Paused COT

## Slide 33: There was no consensus on whether to re-establish status quo with paused COT using EDT of -72 dBm
Submissions
  BRAN(19)103006r1: Paused COT update (Cisco)
  BRAN(19)000036: 25 us LBT (Ericsson)
Summary of paused COT issue
  EN 301 893 v2.1.1 contains a paused COT feature with EDT of -72 dBm
    Paused COT was included for LAA, but could be used by other technologies
    It restarts a COT after a >100µs gap using a short LBT with an EDT of -72 dBm
  Latest EN 301 893 allows EDT of -62 dBm for paused COT as an unintended result of allowing any technology to use ED-only or PD/ED
    An LAA UE can use EDT of -62 dBm (with an expansion of its access) by asserting it can do PD, knowing PD is not possible in a short LBT
  Some (Cisco et al) want to return paused COT access to the status quo in v2.1.1, with an EDT of -72dBm, while others (Ericsson et al) do not!

## Slide 34: There was no consensus on whether to re-establish status quo with paused COT using EDT of -72 dBm
Discussion of paused COT issue
  There were multiple (counter) arguments put forward in relation to the Cisco proposal in BRAN(19)103006r1 that a restart of a paused COT always use an ED of -72 dBm
    It was asserted an LAA UE would never do this … and yet it was also argued they should have the right to do so, making it important to deal with the issue
    It was argued that PD does not work anyway … which will be addressed later in the agenda and is not true!
    It was argued that the UE has the right to use the same method (ie PD/ED) as used to obtain the COT … although the UE has no way of knowing what method was used to obtain the COT because there is no signalling
    It was argued that less exceptions are better … which is a reasonable argument, assuming there are no other factors to consider

## Slide 35: There was no consensus on whether to re-establish status quo with paused COT using EDT of -72 dBm
  A compromise was proposed by Cisco whereby any UE using PD/ED for paused COT should be awake at least a max COT time before the restart of the COT to allow PD to operate
    This was rejected by Ericsson on the basis that Wi-Fi does not do that in multi-channel, which is this is true, but multi-channel is a independent issue from paused COT, with its own status quo
    The discussion highlights the difficulty of consistency in an inconsistent situation caused by the introduction of an “exception” for LAA
Result of discussion
  BRAN ended in impasse, with no agreement, and further discussion put off until the December meeting
  It is expected that Cisco will make a refined proposal at BRAN #104 that includes the compromise above

## Slide 36
  Relationship topics
  ETSI BRAN activities
  EN 301 893 issues
  Use of no/short LBT for control signalling

## Slide 37: Use of no/short LBT for control signalling has been controversial in ETSI BRAN since late 2018
Submissions related to no/short LBT issue
  BRAN(19)103005r1: Update of short LBT issue (Cisco)
Summary of no/short LBT issue
  EN 301 893 v2.1.1 allows the use of no LBT for (roughly) up to 5% of the time for Short Control Signalling (with max length of 2.5ms)
  It has been observed that overuse of this mechanism (or short LBT) could cause the channel to enable unfair access and possibly collapse
  Cisco et al proposed in ETSI BRAN in late 2018 to resolve this issue by restricting the use of short LBT for Short Control Signalling to about 1%
    The proposal was later modified restrict the use of no LBT to about 1% to avoid complex drafting issues (noting no LBT is not known to be used, and the 1% would also apply to short LBT)
  A decision in ETSI BRAN on the topic was delayed in BRAN#102 to allow discussion at the Coex Workshop in July 2019

## Slide 38: Submissions to the Coex Workshop suggested a compromise restricting no LBT had no downside
Summary of no/short LBT issue
  At the Coex Workshop in July 2019, three submissions were made
    3-12: The use of no LBT for DRS is not justified by history (Cisco)
      Explains how the historical basis of the no LBT rule in EN 301 893 justifies its removal or at least further restriction
    3-13: LBT for Short Control Messages (Huawei)
      Asserts the use of short LBT for DRS (like a Beacon) has no significant impact on coexistence between Wi-Fi & LAA/NR-U
      Explains that simulation shows restricting the use of short LBT for DRS by NR-U has relatively small impact on the DRS transmission rate
    3-14: On standalone transmissions with short fixed LBT (Broadcom)
      Explains that simulation shows the use of short LBT for DRS for NR-U significantly degrades the performance of Wi-Fi using normal LBT access
  It was observed at the Workshop & in the Coex SC in Sept 2019 that restricting no LBT could represent a logical compromise because:
    3-13 showed there was no harm to NR-U
    3-14 showed there was a benefit to Wi-Fi
Conclusion: No downside in restricting no LBT!

## Slide 39: Discussion at Coex SC in Hanoi suggested it might not be in Wi-Fi’s interest to restrict the use of short LBT
Summary of no/short LBT issue
  At Coex SC meeting in Hanoi in Sept 2019, there were strong objections to 802.11 WG supporting any proposal to restrict the use of short LBT
    … and particularly to the proposed LS to ETSI BRAN and/or 3GPP RAN1 on the topic
  There was some suggestion that many Wi-Fi devices use short LBT (or PIFS) for Beacons, contrary to the IEEE 802.11 standard
    No one was willing to go on the record that they used PIFS for Beacons
    The limited responses to a request (by e-mail before the Hanoi meeting) by the Coex SC Chair for information about the use of PIFS for Beacons were ambiguous
  As a result, Cisco asked at BRAN#103 that discussion and a decision be delayed until BRAN#104 in December 2019

## Slide 40: It now appears restricting the use of no/short LBT in EN 301 893 is not in the interest of Wi-Fi industry
Summary of no/short LBT issue
  Since BRAN#103, the Coex SC Chair has been digging into the use of PIFS for Beacons by deployed Wi-Fi gear
  He has established that the use of PIFS for Beacons is probably widespread in the industry, at least among major chip vendors
    Chip vendor A: often uses PIFS for Beacons, with APs usually grouping Beacons for multi-BSSID
    Chip vendor B: often uses PIFS for Beacons, with APs usually spreading Beacons over time for multi-BSSID
    Chip vendor C: confirmed it often uses PIFS for Beacons
    Chip vendor D: hinted (but did not confirm) it often uses PIFS for Beacons
    Chip vendor E: confirmed it does NOT use PIFS for Beacons
  On this basis, any restriction of the use of no LBT in EN 301 893 would probably not be in the best interest of the Wi-Fi industry

## Slide 41: It is now proposed that the 802.11 standards be refined to allow PIFS with Beacons
Summary of no/short LBT issue
  Cisco will no longer be proposing a restriction on the use of no/short LBT in EN 301 893, given it would cause many Wi-Fi implementations to be unusable in Europe
  However, we now have a (known) situation where many Wi-Fi implementations are violating the 802.11 standard
    A group of 802.11 experts previously concluded that the correct mechanim for Beacon transmission in 802.11-2016 is EDCA using AC-VO
  It therefore probably makes sense to modify the IEEE 802.11 standard to better reflect industry practice
    So everyone knows what is possible and allowed
  Andrew Myles has submitted a comment in the LB on 802.11md that proposes explicitly allowing the use of PIFS for Beacons
    It is likely that the resolution of this comment will not occur until SA ballot phase

## Slide 42
  Relationship topics
  ETSI BRAN activities
  EN 301 893 issues
  CW adjustment mechanisms with delayed acks

## Slide 43: There was substantive progress at BRAN#103 on defining CW adjustment requirements
Submissions related to CW adjustment
  BRAN(19)103017r1: Delayed CW updating procedure (Qualcomm, Nokia, Ericsson)
  BRAN(19)103022: CW update response to BRAN(19)103017 (Cisco)
  BRAN(19)103033: Draft LS to 3GPP and IEEE on CW updates (Cablelabs)
Summary related to CW adjustment
  There was agreement at BRAN#102 that EN 301 893’s CW adjustment requirements needed refinement
  At BRAN#103, a proposal to resolve all of the issues related to CW adjustment was accepted in principle
  ETSI BRAN has asked both IEEE 802.11 WG & 3GPP RAN1 to evaluate the proposed CW adjustment requirements

## Slide 44: There was agreement at BRAN#102 that EN 301 893’s CW adjustment requirements needed refinement
  It was agreed at BRAN#102 that the current CW adjustment requirements in EN 301 893 v2.1.1 are unsatisfactory:
    They do not explicitly (but may implicitly) define CW adjustment with broadcasts, as used by 802.11/LAA/NR-U
    They do not define the requirement with delayed ack/nacks, as used by LAA (and NR-U)
  Fortunately, there was also some agreement during BRAN#102 on principles to remedy these problems
    It agreed that it was OK to rely on delayed feedback to drive CW adjustment
    It agreed that it is necessary to use a random selection of the delayed feedback
    There was not consensus on whether success at the start of the COT drove the CW updates
  It was agreed that these principles should became the basis of a future solution

## Slide 45: At BRAN#103, a proposal to resolve all of the issues related to CW adjustment was accepted in principle
  At BRAN#103, Qualcomm, Ericsson & Nokia submitted BRAN(19)103017 as a proposal to resolve all of the issues related to CW adjustment
    It explicitly provides for broadcast (like 802.11)
    It focuses the evaluation of success/failure on the start of the COT (like 802.11)
    It allows only a selection of feedback to be used to double or reset CW (otherwise CW remains the same), but requires the selection of feedback to be random/unbiased
  It was agreed that the text should be included in the draft (in square brackets)
  Menzo Wentink may present accepted proposal
  SC will address LS from BRAN, particularly
  submitted BRAN(19)103017 based on the agreement as a proposal to resolve all of the issues related to CW adjustemnt
  Menzo Wentink may present accepted proposal
  SC will address LS from BRAN, particularly in relation to no bias
  When CW is updated:
  if new feedback is available relative to the prior CW update, the feedback for the latest COT for which new feedback is received shall be used
    if the feedback indicates success, CW shall be set to CWmin
    if the feedback indicates failure, CW shall be set to min( CW×2 + 1, CWmax )
  otherwise, CW shall remain the same
  During normal operation, there shall be no bias towards success in the selection of the feedback used to update CW.
  Proposed CW update/no bias text in BRAN(19)103017

## Slide 46: Key elements of the CW proposal are that the feedback selection is based on the start of the COT & is unbiased
  A key elements of BRAN(19)103017 are that:
    The selection of feedback used to drive CW adjustment is random/unbiased
    The feedback is based on the success of the start of the COT
  The issue of bias is addressed because there is at least one trivial example of a biased feedback selection that causes an obvious problem
    Suppose a protocol provided feedback only when the last COT was successful
    This would mean that the CW would never increase from CWmin

## Slide 47: It is believed 802.11 can satisfy the CW adjustment requirements but the status of NR-U/LAA is unknown
  802.11 generally use immediate feedback based on the success (or otherwise) of the start of all TXOPs, and so it inherently satisfies the proposed requirements
    One known possible exception where there is not immediate feedback of success at the start of a TXOP is for a (delayed) block ack
    However, the 802.11 standard recommends that RTS/CTS or PKT/ACK is used at the start of a sequence of MPDU’s that are not immediately acked (10.24.3)
    This means there is a commonly used mechanism in the 802,11 standards that can be used to satisfy the proposed CW adjustment rules in the CW adjustment proposal
  It is not known if NR-U and LAA satisfy the proposed requirements
    The bias properties of NR-U and LAA have not been evaluated, as far as is known
    It appears that LAA/NR-U may not always focus on success at the start of a COT, although there are assertions to contrary

## Slide 48: ETSI BRAN asked 802.11 WG & 3GPP RAN1 to evaluate the proposed CW adjustment requirements
  BRAN#103 recognised the importance of key elements of proposed CW adjustment requirements, and decided to ask IEEE 802.11 WG and 3GPP RAN1 to evaluate them
  In particular a LS from ETSI BRAN encourages both organisations to analyze the requirements on the CW update procedure, particularly the aspect related to no bias in providing transmission feedback
    See 11-19-1777-00

## Slide 49: The SC will discuss issues related to the LS from ETSI BRAN
  The Coex SC will discuss issues related to the LS from ETSI BRAN
  Possible topics for discussion include:
    Does the SC have any objections to the CW adjustment requirements?
      Noting they seem to be aligned with the 802.11 standard
    Is the SC aware of any cases where the CW adjustment process is not driven by the success (or otherwise) at the start of the COT?
      Beyond the one case related to Block Acks already noted
    Is the SC aware of any bias in 802.11 in its selection of feedback?
      Should not be any given feedback is generally immediate
    …

## Slide 50: The SC will discuss a discuss a possible reply to the LS from ETSI BRAN
  Would anyone like to volunteer to draft a reply to ETSI BRAN for consideration on Thursday?
  A possible outline follows:
    Thank you for the LS
    802.11 generally satisfies the proposed CW adjustment requirements, including the no bias requirement, defined in the LS because it almost always uses immediate feedback based on the success (or otherwise) of the start of all TXOPs to drive CW adjustments
    We are aware of one case (related to the use of Block Acks) in the IEEE 802.11 standard where it is possible to not satisfy the proposed CW adjustment requirements
    However, the standard recommends that Block Acks always be used in a particular way that does satisfy the proposed CW adjustment requirements and it is our understanding that this recommendation is widely followed in implementations
    IEEE 802.11 WG supports the proposed CW adjustment requirements
Superseded by next slide

## Slide 51: The Coex SC will discuss a discuss a possible reply to the LS from ETSI BRAN
  Originally, the Chair was going to ask for volunteers to wrote a reply LS to ETSI BRAN
  However, it seemed more efficient to just draft a starting point for discussion …
    See 11-19-2066-00
  The Coex SC will discuss …

## Slide 52: The Coex SC may consider approving a LS reply to the LS from ETSI BRAN
Possible motion (for consideration on Thu PM1)
  The IEEE 802.11 Coex SC recommends to the IEEE 802.11 WG that the material in 11-19-2066-00 be sent to ETSI BRAN as a response to its Liaison Statement to the IEEE 802.11 WG in 11-19-1777-00
  Moved:
  Seconded:
  Result:

## Slide 53
  Relationship topics
  ETSI BRAN activities
  EN 301 893 issues
  Blocking energy/reservation signals

## Slide 54: The Coex SC stopped discussing blocking energy some months ago due to a lack of consensus
  The Coex SC has previously discussed the use of blocking energy or reservation signals by LAA (and possibly NR-U)
    It is suspected that some LAA implementation transmit up to 1ms of blocking energy to maintain control of the channel before it is ready to send data
    It has previously been the 802.11 WG position in LSs to 3GPP RAN1 that the use of blocking energy for long periods is inappropriate for shared channels
    It has also been the position of the 802.11 WG that the use of a short period of blocking energy is acceptable; this is enabled by more starting positions in LAA, which were promised by 3GPP RAN1 but apparently never implemented
  The Coex SC stopped discussing blocking energy issues some months ago, mainly because it was clear that there was no consensus on pushing the issue further
    There was also clearly no consensus in ETSI BRAN discussions …
    … and 3GPP RAN1 refused to even discuss blocking energy because reservation signals are not defined in either the LAA or NR-U specs (although they are apparently used in at least one LAA implementation)

## Slide 55: A paper at the Coexistence Workshop identified and solved a new problem relating to blocking energy
  There was only one paper dealing with blocking energy during the Coexistence Workshop
    3-10: Collision Detection for Fair LAA/Wi-Fi Coexistence (IITP RAS)
  This paper observed that the use of blocking energy by an LAA eNB breaks underlying LBT sharing principles
    The use of blocking energy allows an LAA eNB to ignore a collision with a Wi-Fi system, when the Wi-Fi transmission is short or an RTS
    Whereas the Wi-Fi system will have to double its CW, the LAA system will be able to continue with no impact
  While banning blocking energy would solve this problem, the paper provides an alternative solution
    It requires the eNB to execute a short LBT towards the beginning of the blocking energy; if a energy is detected a collision is assumed and the transmission stops with CW doubled.

## Slide 56: The Coex Workshop discussion seemed to inspire new interest in the blocking energy issue
Chart: 
| Use of 802.11 preambles or common preambles for coexistence | Energy Detection only vs. Preamble or Energy Detection vs. both | Multi-channel sharing mechanisms | Use of no/short LBT for control signaling | Blocking energy/reservation signals | Synchronous access proposals in U-NII-7 | Contention Window adjustment mechanisms with delayed acknowledgements | Something else | Don't know | None of these | Prefer not to say
Post workshop survey | 0.57143 | 0.55556 | 0.31746 | 0.38095 | 0.30159 | 0.1746 | 0.2381 | 0.063492 | 0.063492 | 0.031746 | 0.095238
WBA survey | 0.5 | 0.36 | 0.36 | 0.22 | 0.1 | 0.08 | 0.04

## Slide 57: A proposal to BRAN#103 on CW updates had a side effect of disallowing the use of blocking energy
  At BRAN#103, Qualcomm, Nokia and Ericsson made a proposal for refining EN 301 893 in relation to CW updates
    See BRAN(19)103017 (we will address the CW update aspects later)
  Part of the proposal focused on defining “success” and “failure”, which drive the CW update process
  At BRAN#103, Cisco observed that one implication of these definitions is that blocking energy is clearly not allowed
    See BRAN(19)103022
  This claim was contentious, at least partially because the proposers of the CW update requirements apparently had not intended to disable the use of blocking energy so obviously
  There was no consensus on this topic at BRAN#103, particularly on a proposal to notify 3GPP RAN1, and the next steps in BRAN are unclear

## Slide 58: The CW update proposal at BRAN#103 essentially bans the use of blocking energy
  Updating CW is based on feedback about the success or failure of Channel Occupancies.
  a Channel Occupancy is a success
    when it has been confirmed that at least one transmission that started at the beginning of the Channel Occupancy was successful, or
    when there is no intention to retransmit any part of the information transmitted during the Channel Occupancy
  otherwise, the Channel Occupancy is a failure
  Proposed success/failure text in BRAN(19)103017
A COT consisting of data prepended with blocking energy is never a success by this clause because blocking energy at the start of the COT is not ack’ed/confirmed
A COT consisting of any unicast data prepended with blocking energy is never a success by this clause because there is an intention to retransmit the data if it fails
Therefore the use of blocking energy with any unicast data means the COT is always a failure … which would mean that CW would always be max’ed out, contrary to the needs of LAA/NR-U

## Slide 59: It is proposed that the Coex SC not re-address the blocking energy issue at this time
  ETSI BRAN needs to conclude their discussion of the CW update requirements before anyone gets too excited about requirements in EN 301 893 related to blocking energy
  Any effort by the Coex SC put into addressing any blocking energy/reservation signal issue also depends on whether it is used in practice
    Does anyone know if real implementations of NR-U/LAA (or Wi-Fi) use reservation signals?
    How often are reservation signals used by these systems?
    How long are the reservation signals used by these systems?
    What is the nature of the reservation signals? Noise or data?
  It is proposed that the Coex SC wait until ETSI BRAN resolves the CW update issue before re-addressing the issue of blocking energy
    Maybe a note in EN 301 893 that blocking energy is not allowed (or is limited in length) will be sufficient?

## Slide 60
  Relationship topics
  ETSI BRAN activities
  EN 301 893 issues
  Spectral mask
  (Thursday PM1)

## Slide 61: ETSI BRAN continues to discuss the issue of spectral masks
Executive summary
  In June 2019, ETSI BRAN could not achieve consensus on some spectral mask questions from 3GPP RAN4
    They have an effect on the mask during puncturing, and are of potential interest to the IEEE 802.11 WG
  in August 2019, ETSI BRAN did not achieve consensus at a spectral mask ad hoc
    … beyond agreeing to send a LS to 3GPP RAN4 stating there was no consensus
    See 11-19-1672-00
  The Coex SC will hear a summary of the recent discussions on the spectral mask issue in ETSI BRAN

## Slide 62: In June 2019, ETSI BRAN could not achieve consensus on some spectral mask questions from 3GPP RAN4
Submissions in June 2019
  BRAN(19)102009r1: LS from 3GPP RAN4 on Interpretations of EN 301 893 for NR-U (spectrum mask) (introduced by Ericsson)
  BRAN(19)102021r1: Proposed answers to questions on the ETSI spectrum mask asked by 3GPP RAN4 (Ericsson)
Summary of discussion in June 2019
  RAN4 had two questions about the spectral mask
    How the roll off region of the spectrum mask is dependent upon Tx BW?
    How to interpret the spectrum mask during puncturing?
  There was not consensus on how to respond but it was agreed to have an ad hoc meeting
Already discussed

## Slide 63: Q1: Should 802.11 WG have a position on the mask during puncturing?
IEEE 802.11ax seems to assume -20dBr. Is this something for which the WG should express a view?
Already discussed

## Slide 64: Q2: Should 802.11 WG have a position on the mask roll of being related to the BW?
Roll off is a function of the BW (20/40/80/160MHz). Does IEEE 802.11 WG have a position on this issue?
Already discussed

## Slide 65: The Coex SC will hear a summary of the recent spectral mask discussions in ETSI BRAN
  ETSI BRAN has continued to discuss the spectrum mask issue at
    BRAN#103
    A teleconference on 31 Oct
  David Boldy (Broadcom) will provide an update on the discussions …
    Early reports are that a compromise was agreed
    See 11-19-xxxx-00
  Dorin Viorel (Cablelabs) will also lead a discussion on this topic (requested for Thursday)
    A submission regarding the impact of the SEM on punctured channels on legacy 802.11 and provide recommendations
    See 11-19-2035-00

## Slide 66
  Relationship topics
  ETSI BRAN activities
  EN 301 893 issues
  Preamble detection

## Slide 67: BRAN#103 started a contentious discussion about PD testing …
Submissions related to PD testing at BRAN#103
  BRAN(19)103009: Measurement Results for Preamble Detection Floating Thresholds (R&S)
  BRAN(19)103018: R&S Plugfest Results and Discussion (Ericsson, Nokia)
  BRAN(19)103035: PD test results (Qualcomm & Broadcom)
Summary of PD testing
  Ericsson & Nokia expressed a concern that many Wi-Fi devices do not do undertake PD as expected, based on testing with two test signals at R&S
    802.11a frame that was 4000+ bytes long
    802.11a preamble (with 1.5ms length indicated) followed by no energy
  …

## Slide 68: … with the discussion about PD testing not coming to any agreed conclusion
Summary of PD testing
  Qualcomm & Cisco both observed that it was reasonable for an implementation to ignore both signals as illegal or impractical
    The 802.11a frame was too long
    A preamble followed by no energy will never occur in practice
  Qualcomm & Broadcom shared their own testing that showed PD does work (at least in the scenario they tested)
    Although their signals included at least 2 BPSK symbols after the preamble
  Qualcomm asserted that PD testing is not necessary because only Wi-Fi uses PD
    The counter was that PD testing is required, just in case other technologies want to use PD
  It was agreed at BRAN#103 that further testing was required to understand why the R&S testing was giving the indicated results

## Slide 69: There was further discussion of PD at an ad hoc teleconference in late Oct 2019
Submissions related to PD testing during ad hoc teleconference
  BRAN(19)000037r1: Test Signals for Preamble Detection (Ericsson)
  BRAN(19)000038: Issues with Preamble Detection (Ericsson)
  BRAN(19)103035r1: PD test results (Qualcomm & Broadcom)

## Slide 70: There was disagreement on whether test signals should be based on legalistic or pragmatic interpretations
  Legalistic vs pragmatic?
  BRAN(19)000038 from Ericsson made a case that various signals were legal in 802.11 and should result in PD
    4us truncated preamble
    802.11a frame >2304 bytes
    A preamble followed by nothing (or something)
  BRAN(19)000037 from Ericsson then proposed PD test signals based on these legal signals
  Qualcomm & Cisco agreed these signals might be technically allowed by 802.11 (noting the 802.11 standard is not perfect) but asserted it is widely understood such a legalistic approach is not pragmatic/practical
  There seemed to be consensus that whatever was agreed/understood about PD, it needs to be written down to be accessible to all

## Slide 71: Qualcomm & Broadcom showed that an alternative test signal can be used to test PD
PD does work with at least one reasonable test signal
  BRAN(19)103035r1 from Qualcomm & Broadcom reported on some testing with APs
  The test method started by removing the UDP load on the APUT in the Ericsson/R&S/Nokia test, to mitigate an issue that the test signal was starting illegally without a backoff
    The Ericsson/R&S/Nokia test signal is also illegal in that it is too long
  The Qualcomm/Broadcom test signal consisted of a preamble, followed by 2 BPSK symbols, followed by 1ms of AWGN
  This test signal, when used to block the channel, gave the expected result; that Wi-Fi gear does actually defer when seeing a preamble
    In the case of the APUT, it stopped sending Beacons

## Slide 72: The Qualcomm/Broadcom test signal is more than just the preamble
The appropriate test signal is more than a preamble
  A key observation from the Qualcomm and Broadcom testing is that just the 802.11a preamble is insufficient for most Wi-Fi implementations to defer
    Two additional BPSK symbols are required, presumably to give the implementation additional confidence it is a real preamble
  This is contrary to expectations of most people that an 802.11a preamble was enough, but is also not surprising given the constraints of practical implementation
    Does anyone have a different expectation/understanding of PD operation?
    Could everyone with Wi-Fi products (esp chip vendors) do some testing to ensure the Qualcomm/Broadcom test signal is sufficient?

## Slide 73: The Qualcomm & Broadcom results suggest that EN 301 893 needs to be refine
EN 301 893 needs refinement
  The next likely step is a tweak to the definition of PD in EN 301 893 to require more than just a preamble
    It appears at least two BPSK symbols need to sent to ensure PD by Wi-Fi devices
  This change would be a significant problem if any other technology (eg NR-U) had adopted the version of PD in EN 301 893 v2.1.1 based on a preamble only… but they haven’t
    3GPP RAN even banned further discussion of proposals
  There are claims by Ericsson and Nokia that such a change is not “technology neutral” …
    … but it is not any less “technology neutral” that the status quo
    … which itself was shown to be more technology neutral than just relying on ED

## Slide 74: The Coex SC will discuss PD testing
  It is hoped that Menzo Wentink (Qualcomm) or David Boldy (Broadcom) will provide an update of the PD testing issue
    See <link>

## Slide 75
  Relationship topics
  ETSI BRAN activities
  EN 303 687 issues
  Alternative WI

## Slide 76: The potential issue of multiple WI’s for a 6 GHz WI has now been resolved
  It was previously reported that there were two WI proposals for a 6 GHz Harmonised Standard (EN 303 687)
  One of the WI proposals (BRAN(19)102016r2) was eventually approved by consensus after BRAN#102
    Proposed by: HPE, Cisco, Microsoft, Broadcom, Intel & Ruckus
    Rapporteur: David Boldy (Broadcom)
    Adopted scope:
      This Harmonised standard will specify technical characteristics and methods of measurements for Wireless access systems including radio local area networks (WAS/RLANs) operating in the band 5 925 MHz to 6 425 MHz and as further described in ETSI TR 103 524 and ECC Report 302.
  …

## Slide 77: The potential issue of multiple WI’s for a 6 GHz WI has now been resolved
  …
  The alternative WI proposal (BRAN(19)102041) was withdrawn at BRAN#103
    Proposed by: Nokia, Qualcomm, Ericsson, DT
    Rapporteur: Narendar Madhava (Ericsson)
    Adopted scope:
      This new Harmonised standard will cover Wireless Access Systems including Radio LANs (WAS/RLANs) operating in the frequency band 5 925 MHz - 6 425 MHz as described by ETSI TR 103 524 and ECC Report 302. The standard shall align with the (draft) ECC decision on 6 GHz RLAN being developed by FM57. The standard will be developed according to the EC mandate to CEPT (Ares(2017)6222764 - 19/12/2017), for supporting the principles of service and technological neutrality, non-discrimination and proportionality insofar as technically possible.
  The withdrawal of the alternative WI means a focus on the one output
    Although the issues defined by differences in the two WI’s scopes will probably resurface during the development of EN 303 687

## Slide 78
  Relationship topics
  ETSI BRAN activities
  EN 303 687 issues
  6GHz ED threshold in 6GHz

## Slide 79: The 6GHz WI has started with the rapporteur developing an initial EN 303 687 draft
  Work started at BRAN#103 on the HS for 6 GHz operation (EN 303 687)
  The rapporteur (David Boldy) has started work on a draft
    Clause 5 text for power, power density, rx spurious emissions, rx blocking (with 5GHz levels in brackets) and ACS requirements will be based on EN 301 893
    Clause 5.4. text for product information will be developed based on EN 301 893
    Spectrum mask requirements will be postponed until 5GHz mask discussions are concluded
  A call was made for contributions for:
    Channel access mechanisms (aka adaptivity)
    Channelization/guard-bands
    Receiver blocking levels
  In addition, there will be future consideration of removing occupied channel bandwidth clause

## Slide 80: The adaptivity clause in EN 303 687 is proving to be a point of disagreement, just like EN 301 893
Submissions related to adaptivity in 6 GHz
  BRAN(19)103016: 6 GHz channel access simulation results (Nokia)
  BRAN(19)103023: Response to BRAN(19)103016 (Cisco)
Summary of adaptivity in 6 GHz
  Nokia argued that the EDT should be uniformly set to -72 dBm for all technologies in 6GHz
  Cisco argued that the EDT for 6 GHz operation should maintain the status quo for 5 GHz operation
  There was no consensus on the issue of an EDT for 6 GHz in EN 303 687

## Slide 81: Nokia argued that the EDT should be uniformly set to -72 dBm for all technologies in 6GHz
Summary of Nokia case on adaptivity in 6 GHz
  BRAN(19)103016 from Nokia concluded that the EDT in 6GHz should be set to -72 dBm for all technologies
    Under this proposal, 802.11 will not be able to use an EDT of -62 dBm if it also does PD at -82 dBm
  The Nokia conclusion was based on simulation of an “indoor office” scenario, previously specified by 3GPP RAN1
    An NR-U and a Wi-Fi operator, each with 1 AP or 3 APs, in a grid layout
  The Nokia simulations showed that all technologies were better off with a uniform EDT of -72 dBm (with Wi-Fi still using a PD of -82 dBm)

## Slide 82: Cisco argued that the EDT for 6 GHz operation should maintain the status quo for 5 GHz operation
Summary of Cisco case on adaptivity in 6 GHz
  BRAN(19)103023 from Cisco argued that EN 303 687 for 6 GHz operation should adopt the status quo in the adaptivity clauses from EN 301 893 for 5 GHz operation
  Cisco noted there is currently insufficient evidence to change the 5 GHz status quo for 6 GHz operation
  Cisco finally noted that even acceptance that an ED threshold of -72 dBm is better for all doesn’t justify changing the status quo

## Slide 83: Cisco claimed here is currently insufficient evidence to change the 5 GHz status quo for 6 GHz operation
  It is generally accepted that compelling evidence is required to change the long established status quo
    ie the ability to chose between ED-only & PD/ED
  However, there is currently insufficient evidence to change the status quo to only allow the ED-only mechanism at -72 dBm for 6 Ghz
    No/limited deployment experience for ED-only, either by itself or with PD/ED (in contrast to 20 years of good deployment experience with ED/PD)
    Most simulations inappropriately extrapolate very limited use cases to conclusions covering all use cases
      Note: see BRAN(18)100008r1 for previous evaluations of simulation evidence
    Some simulations from Ericsson suggest use of PD/ED by LAA/NR-U provides better performance than ED-only in some circumstances
    Some simulations from Ericsson suggest an ED-only threshold of -77 dBm provides even better performance for all technologies in some circumstances

## Slide 84: Cisco noted acceptance that an ED threshold of -72 dBm is better for all doesn’t justify changing the status quo
  Consider the Nokia (and Ericsson) simulations asserting an ED threshold of -72 dBm is better for both NR-U & 802.11ax
    BRAN(19)103016 (Nokia) & 3GPP R1-1813947 (Ericsson)
  Assume these simulations are correctly run and presented
    Probably true, but would need careful review to confirm
  Assume it is valid to extrapolate the results based on a limited use case to the general case
    Not true, but let’s assume it anyway 
  Nokia’s (& Ericsson’s) simulation results & assumptions then suggest that 802.11ax (and 802.11be) should be constrained by an ED threshold of -72 dBm in EN 303 687
    Note: 802.11ax/be can then use any ED or PD threshold up to -72 dBm
  Or do they … ?

## Slide 85: Cisco noted acceptance that an ED threshold of -72 dBm is better for all doesn’t justify changing the status quo
  … no, they don’t!
  The simulation results indicate that 802.11ax will be better off using an ED threshold of -72 dBm (rather than -62 dBm)
  If the conclusion is correct … then there is no need for ETSI BRAN to constrain the ED threshold to -72 dBm because 802.11ax vendors will do it anyway based on their best interest
    Note that this is exactly same argument used by Ericsson in 3GPP R1-1813882 to justify not reducing the ED threshold for NR-U to -77 dBm
  If the conclusion is incorrect … then there is no justification for ETSI BRAN to change the status quo by constraining the ED threshold to -72 dBm

## Slide 86: There was no consensus on the issue of an EDT in EN 303 687
  The minutes of the discussion related to the EDT in EN 303 687 stated
    No agreements were reached on channel access mechanism during BRAN#103
    It was agreed that for future channel access mechanism discussions face to face meetings were the best option.
    No GoToMeetings were scheduled for 6GHz
  Which probably means a long discussion process …

## Slide 87: It is likely that TGax will consider & probably reject any proposal to limit the EDT to -72 dBm in 6 GHz
  Andrew Myles inserted a comment into the 802.11ax Letter Ballot in relation to limiting the EDT to -72 dBm
  The comment requests that 802.11ax be modified to introduce this restriction for operation in the 6 GHz band on the basis of assertions it will improve performance
  It is expected that TGax will reject this comment, which will provide good guidance on the position of the 802.11 community

## Slide 88: What does this mean for the Wi-Fi industry?
Some discussion points
  While the full and proper discussion of adaptivity in 6 GHz is important, the Wi-Fi industry probably wants a timely conclusion to allow selling of 6GHz equipment in late 2020
  The Wi-Fi industry should have an open mind about the 6 GHz adaptivity parameters because 6 GHz is different
    No legacy systems, eg 11a/n/ac
    Less contention, and more scheduling
  What does the Wi-Fi industry want?
    Status quo
    EDT of -72 dBm
    Something else?

## Slide 89
  Relationship topics
  ETSI BRAN activities
  Next meetings

## Slide 90: ETSI BRAN will next meet at BRAN#104 in December 2019
ETSI BRAN plans
  BRAN #104
    2-6 December 2019 – Sophia Antipolis
  BRAN #105
    23-27 March 2019 – Sophia Antipolis

## Slide 91
  3GPP NR-U
  WBA review

## Slide 92: WBA may consider coexistence in 6GHz are a priority focus area in 2020
  The WBA has a process whereby they define high priority focus for the following year
  “Fair Coexistence Wi-Fi and Unlicensed 5G (5G-NRU)” has been proposed as a priority topic for 2020
    Define the requirements on fair Coexistence of Wi-Fi and Unlicensed 5G on 6 GHz
    Address opportunity to converge operator requirements to IEEE and subsequently 3GPP
    Define the architecture, QoS and policy interfaces for RAN Convergence Experience
    Nominate 1 expert from each operator member to contribute to this effort
  It is hoped the WBA will provide more information to the Coex SC before the Hawaii meeting

## Slide 93: The WBA is likely to explore coexistence within an umbrella project focusing Wi-Fi/5G Convergence
Latest update (from Bruno Tomas)
  The WBA yearly roadmap will include an umbrella project focusing Wi-Fi/5G Convergence
    This was the #1 priority project voted by WB members.
  Within this overarching project there are some references to fair coexistence between Wi-Fi and 5G-NRU
  The WBA Board supports exploration of coexistence issues in fast-track mode, but need to find the right persons/contacts within the WBA membership (potentially in parallel to the above master project)
  …

## Slide 94: The WBA are looking for participation in the coexistence activity
Latest update (from Bruno Tomas)
  The current planned scope of the coexistence activity is:
    Define the requirements on fair Coexistence of Wi-Fi and Unlicensed 5G on 6 GHz
    Address opportunity to converge operator requirements to IEEE and subsequently 3GPP
    Define the architecture, QoS and policy interfaces for RAN Convergence Experience
  Bruno Tomas will be running an initiative to collect expression of interest to form a project team
    With 1 expert from each operator member to contribute to this effort
  Bruno Tomas’ expectation is to have the group formed and running before year-end with a formal kick-off at the Q1 F2F Working Sessions in Singapore on Feb-6.

## Slide 95
  3GPP NR-U
  3GPP RAN/RAN1 review
  (Thursday PM1)

## Slide 96: The Coex SC may hear a status update from the most recent 3GPP RAN/RAN1 meetings
  Sindhu Verma (Broadcom) will provide a RAN1 update
    See 11-19-2044-00-coex

## Slide 97
  Agenda items
  Extension of SC charter

## Slide 98: The Coex SC may discuss and consider a new scope to extend its life beyond 802.11ax on Thu
  The question of coexistence between Wi-Fi and various LTE based technologies has been “hot” for the last 4+ years
  The Coex SC is scheduled to close when 802.11ax completes Sponsor Ballot (now called Standards Committee Ballot) in early 2020
  However, here is no reason to think that coexistence will not remain a vitally important issue beyond the completion of IEEE 802.11ax as:
    IEEE 802.11be is developed
    ETSI BRAN develops a Harmonised standard for 6 GHz operation
  As the ratification of IEEE 802.11ax get closer the Coex SC may want to consider a scope extension
  It is proposed the SC continue this discussion at the end of the agenda (on Thu), when participants will have a better idea of the potential ongoing work for the SC … but think about it in the meantime
From Hanoi session

## Slide 99: The agreed Coex SC scope focuses on ensuring 802.11ax has fair access to global unlicensed spectrum
Discuss the use of PD, ED or other 802.11 coexistence mechanisms with the goal of promoting “fair” use of unlicensed spectrum
Promote an environment that allow IEEE 802.11ax “fair access” to global unlicensed spectrum
Will initially focus on liaising with 3GPP RAN/RAN1/RAN4 but may also lead to interactions with regulators and other stakeholders
Will probably not conclude at least until RAN4’s 802.11/LAA coexistence testing is defined and successfully executed
May require the SC to consider other simulations and results of tests of potential LAA/802.11 coexistence mechanisms
Will initially focus on encouraging a “technology neutral” solution in the next revision of EN 301 893 that allows IEEE 802.11ax fair access to unlicensed spectrum in Europe (noting the European approach is likely to have global impact)
The effort will also focus on allowing 802.11ax to use innovative mechanisms for frequency reuse without compromising the goal of fair access
From Hanoi session

## Slide 100: The Coex SC has potential coexistence work related to 802.11be and 6 GHz
Why should the Coex SC charter be extended?
  The existing Coex SC charter is mostly constrained to 802.11ax and 5 GHz coexistence, despite potential coexistence issues in 802.11be & 6GHz
    It does not cover coexistence with 802.11be (the next big thing )
    It did not explicitly cover coexistence in 6 GHz (the other next big thing )
      It could be argued that is does implicitly cover 6 GHz with the 802.11ax PAR extension to cover 6 GHz
  There is likely to be relevant material to review from other organisations related to coexistence
    3GPP RAN1 will probably not provide as much to review as in the past because the NR-U spec is scheduled for completion in early 2020 (although thye are talking about revisions)
    ETSI BRAN will continue providing material as the 5 GHz HS (EN 301 893) is completed and the 6 GHz HS (EN 303 687) is developed

## Slide 101: The SC may discuss a possible new scope for a rechartered Coex SC
Possible new scope for Coexistence SC charter extension
  The Coex SC shall promote the establishment of an environment and the use of mechanisms that enable IEEE 802.11 technologies to have “fair access” to global unlicensed spectrum
  The Coex SC should focus particularly on coexistence of 802.11ax & 802.11be with LAA & NR-U in the 5 GHz and 6 GHz bands
  The Coex SC may consider coexistence with other technologies and in other bands as directed by the Chair of the 802.11 WG
Possible close down criteria for Coexistence SC
  The Coex SC will close when it is determined by the 802.11 WG that the SC is unlikely to make further progress towards its goals

## Slide 102: The Coex SC may consider approving the extension of its charter
Possible motion
  The IEEE 802.11 Coex SC recommends to the IEEE 802.11 WG that its charter is revised to <see previous slide>
  Moved:
  Seconded:
  Result:

## Slide 103
  Agenda items
  Plans for next meeting

## Slide 104: The Coex SC will continue its normal business in Jan 2020 in Irvine
Possible agenda items
  Review results of ETSI BRAN meeting in Dec 2019
  Review recent 3GPP RAN/RAN1 activities
  Prepare for ETSI BRAN meeting in Mar 2020
  …

## Slide 105: The IEEE 802.11 Coexistence SC meeting in Hawaii in Nov 2019 is adjourned!