## Slide 1: India Channels 167 169 173
Date: 2019-10-20
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com
Jun Zheng |  |  |  | 
Jason Tseng |  |  |  | 
Ron Porat |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 2: Abstract
India has “recently” added some channels for indoor/outdoor unlicensed use
These newly available channels should be included in the global channels listing in Annex E
  Table E-4—Global operating classes
CID 4157

## Slide 3: CID 4157
CID 4157
CID | Commenter | Page | Clause | Comment | Proposed Change | Proposed Resolution
4157 | Matthew Fischer | 4380.00 | E | India has "recently" added some channels for indoor/outdoor unlicensed use These newly available channels should be included in the global channels listing in Annex E | Within Annex E at Table E-4 Add 173 to op class 125 Add 165 to op class 126 Add 169 to op class 127 See 11-19-1778 | Revise – TGmd editor to make changes shown in 11-19-1778r1 which add channels 165, 169, 173 to Annex E in appropriate locations within the global class table.

## Slide 4: Missing Channels
The following channels are recently* available in India, but are not included in the Global operating classes table in Annex E
Ch 167 BW40
  CH 165 Primary Lower BW40
  CH 169 Primary Upper BW40
Ch 169 BW20
Ch 173 BW20
*See [2] Gazette of India, OCTOBER 22, 2018

## Slide 5: Proposed Changes
Table E-4—Global operating classes
Note the additions in underlined text
Operating class | Nonglobal operating class(es) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel set | Channel center frequency index | Behavior limits set
125 | E-1-5, E-2-17, E-5-3 | 5 | 20 | 149, 153, 157, 161, 165, 169, 173 | _ | LicenseExemptBehavior, UseEirpForVHTTxPowEnv
126 | E-1-25,26, E-5-6 | 5 | 40 | 149, 157, 165 | _ | PrimaryChannelLowerBehavior, UseEirpForVHTTxPowEnv
127 | E-1-30,31 | 5 | 40 | 153, 161, 169 | _ | PrimaryChannelUpperBehavior, UseEirpForVHTTxPowEnv

## Slide 6: Straw poll #1
Do you support the proposed changes to Draft P802.11REVmd_D3.0 Annex E Table E-4 – Global operating classes as described in 11-19-1778-00-000m-India-ch-167-169-173?
  YES
  NO
  ABS

## Slide 7: References
[1] Draft P802.11REVmd_D3.0
[2] Gazette of India, Extraordinary, PART II—Section 3—Sub-section (i), OCTOBER 22, 2018, G.S.R. 1048(E)