## Slide 1: India Channels 167 169 173
Date: 2019-10-20
Authors:
Name | Affiliations | Address | Phone | Email
Matthew Fischer | Broadcom | 250 Innovation Dr, San Jose, CA 95134 |  | Matthew.fischer@broadcom.com
Jun Zheng |  |  |  | 
Jason Tseng |  |  |  | 
Ron Porat |  |  |  | 
Vinko Erceg |  |  |  | 

## Slide 2: Abstract
India has “recently” added some channels for indoor/outdoor unlicensed use
These newly available channels should be included in the global channels listing in Annex E
  Table E-4—Global operating classes
There is a question of exactly how to include the new channels, which is actually a general question
CID 4157

## Slide 3: CID 4157
CID 4157
CID | Commenter | Page | Clause | Comment | Proposed Change | Proposed Resolution
4157 | Matthew Fischer | 4380.00 | E | India has "recently" added some channels for indoor/outdoor unlicensed use These newly available channels should be included in the global channels listing in Annex E | Within Annex E at Table E-4 Add 173 to op class 125 Add 165 to op class 126 Add 169 to op class 127 See 11-19-1778 | Revise – TGmd editor to make changes shown in 11-19-1778r4 which add channels 165, 169, 173 to Annex E in appropriate locations within the global class table and add an indication of support for the new channels.

## Slide 4: Missing Channels
The following channels are recently* available in India, but are not included in the Global operating classes table in Annex E
Ch 167 BW40
  CH 165 Primary Lower BW40
  CH 169 Primary Upper BW40
Ch 169 BW20
Ch 173 BW20
*See [2] Gazette of India, OCTOBER 22, 2018

## Slide 5: Proposed Changes (1)
Table E-4—Global operating classes
Note the additions in underlined text
Operating class | Nonglobal operating class(es) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel set | Channel center frequency index | Behavior limits set
125 | E-1-5, E-2-17, E-5-3 | 5 | 20 | 149, 153, 157, 161, 165, 169, 173 | _ | LicenseExemptBehavior, UseEirpForVHTTxPowEnv
126 | E-1-25,26, E-5-6 | 5 | 40 | 149, 157, 165 | _ | PrimaryChannelLowerBehavior, UseEirpForVHTTxPowEnv
127 | E-1-30,31 | 5 | 40 | 153, 161, 169 | _ | PrimaryChannelUpperBehavior, UseEirpForVHTTxPowEnv
TGmd editor to make the following changes:

## Slide 6: Should There Be More Changes?
Compatibility issue
  It is possible that regulations change and channels appear and disappear
    Should these changes simply be made within the Annex E tables every time that they occur?
  If this is done, then how can two STAs agree on an operating channel?
    Two STAs can be aware of each other’s OpClass understanding, but not the channel set within any given OpClass

## Slide 7: Add A Capability Bit
Add a capability bit for each set of changes to the channels
  E.g. EX CAP IE bits to indicate support for:
    Channel lists that existed as of 2020-01-01
      No bit needed, implied support
    Support for 165, 169, 173
    Future capability bits each time that there is any additional change in the complete set of Annex E channels

## Slide 8: Proposed Changes (2a)
Table 9-153—Extended Capabilities field
  Add a new row to Table 9-153 – Extended Capabilities field as shown (note that the top row is for orientation purposes only)
Bit | Information | Notes
<ANA> | Extension Channel Set 1 | The STA sets the Extension Channel Set 1 field to 1 when dot11ExtChSet1 is true, and sets it to 0 otherwise.

## Slide 9: Proposed Changes (2b)
  Add a new MIB variable as shown:
C.3 MIB Detail
dot11ExtChSet1OptionActivated OBJECT-TYPE
  SYNTAX TruthValue
  MAX-ACCESS read-only
  STATUS current
  DESCRIPTION
  "This is a capability variable. Its value is determined by device capabilities.
  This attribute, when true, indicates that the STA implementation supports operating class 126 channel 165, operating class 127 channel 169, and operating class 125 channel 173 as found in Table E-4 – Global Operating classes. The capability is disabled, otherwise."
  DEFVAL { false }
  ::= { dot11StationConfigEntry <XX>}

## Slide 10: Alternative Solution
Create new operating classes for each new set of channels
  I.e. instead of adding to an existing operating class and providing a capability bit for the set of new channels
This allows existing elements to be used to indicate support for the new channels
  See 9.4.2.53 Supported Operating Classes element
  No new capability bit required
  Limited reserved operating class values remain
    New amendment will need some – e.g. new BW, new spectrum
    Op class == 255 available for further extension
    Or just define Extended Supported Operating Classes element when needed, plus Ext Cap IE to indicate support of the new element

## Slide 11: Proposed Changes (3)
In TGmd draft D3.2
  TGmd editor to add the following rows to Table E-4—Global operating classes
Operating class | Nonglobal operating class(es) | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel set | Channel center frequency index | Behavior limits set
136 | _ | 5 | 20 | 173 | _ | LicenseExemptBehavior, UseEirpForVHTTxPowEnv
137 | _ | 5 | 40 | 165 | _ | PrimaryChannelLowerBehavior, UseEirpForVHTTxPowEnv
138 | _ | 5 | 40 | 169 | _ | PrimaryChannelUpperBehavior, UseEirpForVHTTxPowEnv

## Slide 12: Straw poll #1
Do you support the proposed changes to Draft P802.11REVmd_D3.2 Annex E Table E-4 – Global operating classes as described in 11-19-1778-05-000m-India-ch-167-169-173 Proposed Changes (1)?
  YES
  NO
  ABS

## Slide 13: Straw poll #2
Do you support the proposed changes to Draft P802.11REVmd_D3.2 Table 9-153—Extended Capabilities field and the addition of a new MIB variable as described in 11-19-1778-05-000m-India-ch-167-169-173 Proposed Changes (2a) and Proposed Changes (2b)
  YES
  NO
  ABS

## Slide 14: Straw poll #3
Do you support the proposed changes to Draft P802.11REVmd_D3.2 Annex E Table E-4 – Global operating classes as described in 11-19-1778-05-000m-India-ch-167-169-173 Proposed Changes (3)?
  YES
  NO
  ABS

## Slide 15: References
[1] Draft P802.11REVmd_D3.2
[2] Gazette of India, Extraordinary, PART II—Section 3—Sub-section (i), OCTOBER 22, 2018, G.S.R. 1048(E)