## Slide 1: Downlink spatial reuse parameter framework with coordinated beamforming/null steering for 802.11be
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
David Lopez-Perez | Nokia |  |  | david.lopez-perez@nokia-bell-labs.com
Adrian Garcia-Rodriguez |  |  |  | 
Lorenzo Galati Giordano |  |  |  | 
Olli Alanen |  |  |  | 
Mika Kasslin |  |  |  | 
Enrico Rantala |  |  |  | 
November 2019

## Slide 2: Introduction
The 802.11ax spatial reuse parameter (SRP) framework is uplink-centric
  SRP allows APs to altruistically—but coordinately—‘share’ an uplink transmission opportunity (TXOP) with other inter-BSS devices
  As shown in [1594r2], SRP also provides a good basis for coordinated beamforming/null steering
In this contribution, we
  review the SRP framework with coordinated beamforming/null steering of [1594r2],
  propose an extension of the uplink-centric SRP framework of 802.11ax to the downlink, and
  sketch how coordinated beamforming/null steering can take advantage of it
November 2019

## Slide 3: Uplink 802.11ax SRP Framework Enables spatial reuse during uplink transmissions
Standard version
ACK
TF
UL data
UL data (constrained TX power)
ACK
Contention
UL data
UL data reception
UL data reception
STA21 measures power, and identifies a spatial reuse opportunity
TF advertises SRO
AP1 advertises the spatial reuse opportunity (SRO) in a trigger frame (TF), and provides information about
  AP1 transmit power
  AP1 acceptable uplink interference level
STA21 measures AP1 received power level, and determines whether using the SRO
  STA21 derives, e.g. its maximum transmit power, based on the above information
If STA21 finds an SRO, it contends while AP1 is receiving uplink data
  STA21 TXOP has to accommodate all transmissions within AP1 data reception
Data transmission
STA21
donor AP1
AP2
STA11
STA12
November 2019
t
BSS1
BSS2

## Slide 4: Uplink 802.11ax SRP framework Good basis for coordinated beamforming/null steering
Standard version + coordinated null steering support (see [1594r2])
ACK
TF
UL data
UL data
ACK
Contention
STA21
donor AP1
AP2
STA11
UL data
STA12
UL data reception
UL data reception
STA21 measures power, and identifies a spatial reuse opportunity
TF advertises spatial reuse opportunity
NDP
TF
TF
NDP
NDP
NDP
NDPA
Transfer and return frames may be needed to coordinate AP1 and AP2 actions
NDP
NDP
NDP
NDP
Phase 1 – Coord.
Phase 2 – Implicit CSI acquisition
Phase 3 – Coordinated inter-AP DATA TX & ACK with nulls
CRequest
CResponse
Data transmission
Null steering
AP2 nulls
STAs 11 and 12
AP1 nulls
STA21
*Similar to 802.11ax, an alternative implementation could be based on AP2 sending the ACK while AP1 is still performing UL data reception
November 2019
t
BSS1
BSS2

## Slide 5: Uplink 802.11ax SRP framework Need for extending this framework to the downlink
802.11ax SRP does not extend its operation to the downlink
Two major missed opportunities:
  In contrast to the uplink, APs cannot altruistically—but coordinately—‘share’ a downlink TXOP with other inter-BSS devices
    This results in wasted spatial reuse opportunities
  More importantly, we cannot provide a straightforward extension for downlink coordinated beamforming/null steering
  In the following, we propose a downlink SRP framework to address both shortcomings, with the core objective of enabling downlink coordinated beamforming/null steering operations in 802.11be
November 2019

## Slide 6: Downlink 802.11be SRP framework Enabling spatial reuse during downlink transmissions
The proposed protocol builds on—is protected by—an enhanced MU-RTS/CTS frame exchange, and consists of two phases:
Phase 1: Improved MU-RTS to flag a downlink spatial reuse opportunity (SRO)
  Enhanced MU-RTS informs inter-BSS devices about
    the upcoming downlink SRO, and
    the acceptable interference level towards data-receiving STAs addressed by the MU-RTS
Phase 2: New channel access rules for inter-BSS devices
  Upon reception of the enhanced MU-RTS frame, announcing a potential downlink SRO, inter-BSS devices do not immediately update their NAV
  Instead, inter-BSS devices identify channel access opportunities, where they need to adjust their transmission power based on
    the maximum tolerable level of interference specified by the MU-RTS frame, and
    the aggregate received power level (RPL) measured during the CTS response/s
November 2019

## Slide 7: Downlink 802.11be SRP framework Example
Coverage region of AP2 [BSS2]
AP1
…
AP2
Coverage region of AP1 [BSS1]
STA 11
STA 22
Donor AP1
MU-RTS
Phase 1
Transmission Phase
STA 11
STA 22
CTS
Downlink transmission
Downlink reception (from AP1)
NAV set upon evaluating new channel access conditions. No channel access allowed
AP2
STA 21
Downlink spatial reuse opportunity advertised
t
AP2 and STA 21 start contention
Downlink transmission (constrained TX power)
Downlink reception (from AP2)
ACK
ACK
Received power level (RPL) measurements over CTS allow inter-BSS devices to
  obtain up-to-date estimates of the potential interference towards downlink data-recipient STAs, and
  identify channel access opportunities
To identify channel access opportunities, inter-BSS devices must constrain their maximum TX power according to such RPL measurements
  Max TX power [dBm] SRPDL – RPL [dBm], where SRPDL was provided in the MU-RTS
  In this example, 1) AP2 and STA 21 identify a spatial reuse opportunity, and 2) AP2 gains channel access first
AP2 gains channel access
…
RPL measurements to estimate the strength of the potential interference link
STA 21
November 2019
Phase 2
BSS1
BSS2

## Slide 8: Downlink 802.11be SRP framework Benefits
As a result of implementing the above protocol, a safe downlink spatial reuse is enabled, and simultaneously,
  The AP that sent the MU-RTS (AP1 in previous example) performs a successful downlink transmission with a controlled acceptable interference level
  The inter-BSS APs/STAs that identified a spatial reuse opportunity (AP2 and STA 21 in the previous example) continue the countdown of an existing back-off procedure, and
  The inter-BSS device that gains channel access first (AP2 in the previous example) performs a concurrent transmission
    as long as it satisfies the power constraint set by the donor AP (AP1 in the previous example)
November 2019

## Slide 9: Coordinated null steering enhancement
Downlink coordinated beamforming/null steering, as evaluated in e.g. [0772r1] and [1212r2], may be efficiently realized by combining the proposed downlink 802.11be SRP framework with
  the enhanced spatial reuse opportunity coordination, and
  the CSI acquisition phases
  presented in [1594r2]
MU-RTS
Data transmission phase
STA 11
STA 22
CTS
Downlink transmission
Downlink reception (from AP1)
AP2
STA 21
Downlink spatial reuse opportunity advertised
t
Downlink transmission
Downlink reception (from AP2)
ACK
ACK
RPL measurements to estimate the strength of the potential interference link
Phase 1
Downlink reception (from AP2)
ACK
Coverage region of AP2 [BSS2]
AP1
…
AP2
Coverage region of AP1 [BSS1]
STA 11
STA 21
…
Multi-AP coordination phase
Enhanced spatial reuse coordination and
CSI acquisition phases
See [1594r2]
November 2019
Donor AP1
Phase 2
Data transmission
Null steering
AP2 start contention and gains channel access
TX nulls to STAs 21 and 22
TX null to STA 11
RX null to STA 11
RX nulls to STAs 21 and 22
STA 22
BSS1
BSS2

## Slide 10: Summary
In this contribution, we have generalized the coordinated beamforming/null steering protocol of [1594r2] to the downlink
  To achieve that objective, we have proposed a downlink extension of the uplink-centric SRP of 802.11ax
    This extension relies on the utilization of MU-RTS/CTS and modified channel access conditions to guarantee safe downlink spatial reuse operations
  The proposed downlink SRP framework can be readily enhanced to enable an efficient implementation of coordinated beamforming/null steering operations in 802.11be
November 2019

## Slide 11: Straw poll
Do you believe that coordinated beamforming is an appealing concept and should be further explored within the 802.11be task group?
  82 Yes
  2 No
  31 Abstain
November 2019

## Slide 12: References
[0772r1] Roya Doostnejad (Intel), “Multi-AP Collaborative BF in IEEE 802.11”, 19/0772.
[1212r2] David Lopez-Perez (Nokia), “Performance of Coordinated Null Steering in 802.11be”, 19/1212.
[1594r2] David Lopez-Perez (Nokia), “Coordinated Beamforming/Null Steering in 802.11be”, 19/1594.
November 2019