## Slide 1: Context-based V2X Reliability
Date: 2019-11-14
Authors:
Onn Haran, Autotalks

## Slide 2: Recap
  V2X Broadcast ACK was proposed during the last 3 meetings [1,2]
  Motivation: Assuring message delivery for vehicle control
  Consecutive messages failure delays awareness of potentially important changes in vehicle trajectory
    Maximal allowed gap between packets depends on safety scenario
  Previous suggested scheme: unsolicited periodic BroadcastAck messages
  A vehicle periodically sends BroadcastAck containing source addresses of valid received messages
  Another vehicle may retransmit if its address is not included in the BroadcastAck message
  A new scheme is presented
  Simplified and aligned with BlockAck operation

## Slide 3: Absolute vs. Context-Based Reliability
  Absolute reliability is unneeded and unfeasible
  Most V2X messages don’t have any impact on vehicle
  Impractical to receive feedback from all vehicles
  High channel load increase
  Context-based reliability is essential and practical
  The few V2X messages controlling vehicle require high-reliability
  Possible to receive feedback from some relevant vehicles only during relevant time
  Suggestion: allow selective acknowledgement request from selected vehicles
  Activation and vehicle selection are up to upper layer

## Slide 4: Context-Based Reliability – Examples
  Upper layer identifies dangerous situations demanding high-reliability, and the vehicles that should provide acknowledgement
  For example:
  Vehicle is driving in a platoon: all other platoon members
  Vehicle is entering an intersection: vehicles approaching intersection from other directions
  Vehicle is negotiating a lane merge: other vehicles in negotiation group
  Upper layer should consider event criticality and channel load

## Slide 5: Reliable Group Communication
  C-V2X Rel. 16 adds group concept for reliable communication between group members
  Upper layers may be enhanced to leverage this new functionality
  Adding context-based reliability to 802.11 will match this functionality
  A group member requests acknowledgments from all other members after each transmission
  No formal group definition: other vehicles may not reciprocally request acknowledgements

## Slide 6: Acknowledgement Sequence
  Operation follows BlockAck scheme and frame format
  Few minimal BlockAck modifications are needed
  Skipping session negotiation phase
  Capabilities should be pre-agreed
    Should be mandated in all 11bd devices
  Retransmission is decided based on responses from multiple vehicles
Broadcast / Multicast
AckReq
Ack
OK
AckReq
AckReq
Ack
Fail
Originator
Solicited #1
Solicited #2
Solicited #3
Retransmitting when one of the responding STAs have failed to receive (#3) or haven’t answered (#2)
Broadcast / Multicast

## Slide 7: Sequential Acknowledgement Request
  Each single handshake “wastes” MAC header and SIFS
  Channel load increase should be minimized
  Achieved by combining all BlockAckReq into a single message
  A sequence of up to 8 (TBD) STAs can Ack using a single BlockAckSeqReq
  STAs are responding sequentially at pre-determined time offsets following the order in BlockAckSeqReq
Broadcast / Multicast
AckSeqReq
Originator
Solicited #1
Solicited #2
Solicited #3
Ack
OK
Ack
Fail
Broadcast / Multicast
Retransmitting when one of the responding STAs have failed to receive (#3) or haven’t answered (#2)

## Slide 8: BlockAckSeqReq for Lower Channel Load
Block Ack Starting sequence control
Number of recipients
Address recipient #1
Address recipient #N
16
3
48
48

## Slide 9: Potential Marking of BlockAckSeqReq Extension Type
  Reserved values can be utilized

## Slide 10: Straw Poll #1
Do you agree to add the following text into Section 3 of SFD?
  “NGV shall allow Broadcast and Mulitcast reception feedback using BlockAck. Upper layer initiates BlockAckReq and selects the recipients.”
Y:
N:
A:
November 2019
Onn Haran, Autotalks

## Slide 11: Straw Poll #2
Do you agree to add the following text into Section 3 of SFD?
  “NGV shall include BlockAckSeqReq requesting sequential Ack responses from multiple recipients.”
Y:
N:
A:
November 2019
Onn Haran, Autotalks

## Slide 12: References
  [1] Reliable V2X operation, Onn Haran 802.11-19-0717/r1
  [2] Mechanisms fo reliable V2X operation, Onn Haran 802.11-19-1158/r2
November 2019
Onn Haran, Autotalks