## Slide 1: Coordinated OFDMA Operation
Date: 2020-01-14
Authors:

## Slide 2: Motivation
This contribution discusses a general coordinated OFDMA operation.

## Slide 3: Coordinated OFDMA Architecture
A first AP that obtains a TXOP may grant to use a partial bandwidth (one ore more 20 MHz channels) to one or more second APs under the control of the first AP.
  The first AP and the second AP are called as a coordinator AP and a coordinated AP, respectively.
STA1
STA2
AP2
(Coordinated AP)
AP1
(Coordinator AP)
STA3
AP3
(Coordinated AP)

## Slide 4: Coordinated OFDMA Architecture
Each AP (a coordinator AP and a coordinated AP) may create its own BSS.
  The coordinated AP may work as a relay. In such case, it has two functionalities, the first is a non-AP STA for associating with the coordinator AP and the second is an AP STA for serving its own BSS.
STA1
STA3
STA2/AP2
(Coordinated AP)
AP1
(Coordinator AP)
BSS1
BSS2

## Slide 5: Coordinated OFDMA Operation
Coordinated OFDMA setup
  An AP that wants to participate in the coordinated OFDMA operation as the coordinator AP should announce to neighbor APs the coordinator AP role in the Beacon or Probe Response frames.
  An AP that wants to participate in the coordinated OFDMA operation as the coordinated AP should negotiate the coordinated OFDMA operation with the AP that announced the coordinator AP role.

## Slide 6: Coordinated OFDMA Operation
Coordinated AP resource needs report
  The coordinated AP should indicate resource needs to the coordinator AP, to intend to use the resource (i.e.,. frequency or time) shared by the coordinator AP.
    The resource needs indication should be sent on an SU PPDU. Or, it can be sent an HE TB PPDU if the coordinated AP supports an UL MU transmission.

## Slide 7: Coordinated OFDMA Operation
Coordinated OFDMA transmission schedule
  The coordinator AP allocates the bandwidths, lengths, and additional TXVECTOR parameters for DL and UL transmission. Such allocation may be announced by the Coordinated OFDMA Announcement (COA) control frame to one or more coordinated APs.
    The DL TXVECTOR parameter may have Format, GI, LTF size, number of HE-SIG-B symbols, and number of HE-LTF symbols.
    The UL TXVECTOR parameter may have GI, LTF type and number of HE-LTF symbols, etc.

## Slide 8: Coordinated OFDMA Operation
Coordinated OFDMA transmission schedule
  The coordinator AP does not allocate the RUs for the STAs associated with the coordinated APs. Instead, the coordinated AP schedules the DL and UL transmission to its associated STAs subject to the constrained parameters from the received COA frame.
    For example, when the coordinated AP schedules the RU for the DL and UL transmission, the allocated RU shall be within the allocated bandwidth from the coordinator AP.

## Slide 9: Coordinated OFDMA Operation
Coordinated OFDMA transmission schedule
  In the below figure, the COA frame indicates the allocated bandwidths for the coordinated AP1 and the coordinated AP2 to the lower 20 MHz and the upper 20 MHz respectively.
    The coordinated AP1 schedules the RU for STA1 within the lower 20 MHz.
    The coordinated AP2 schedules the RU for STA2 within the upper 20 MHz.
Coordinator AP
Coordinated AP1
Coordinated AP2
STA1
(associated with AP1)
STA2 (associated with AP2)
COA frame
COA frame
Data and Trigger frames to STA1
Data and Trigger frames to STA2
UL frame to AP1
UL frame to AP2
20MHz
20MHz
20MHz
20MHz
20MHz
20MHz
COA frame
COA frame
Data and Trigger frames to STA1
Data and Trigger frames to STA2

## Slide 10: Coordinated OFDMA Operation
Primary CH (AP2)
Coordinated OFDMA primary channel selection
  The APs that wants to participate in the coordinated OFDM operation as either the coordinator AP or the coordinated AP should select the different primary channels.
    In such case, the COA frame should be sent in a non-HT duplicated PPDU or an HE MU PPDU.
Coordinator AP
Coordinated AP1
Coordinated AP2
STA1
(associated with AP1)
STA2 (associated with AP2)
COA frame
COA frame
Data and Trigger frames to STA1
Data and Trigger frames to STA2
UL frame to AP1
UL frame to AP2
20MHz
20MHz
20MHz
Primary CH (STA2)
20MHz
20MHz
Primary CH (STA1)
COA frame
COA frame
Data and Trigger frames to STA1
Data and Trigger frames to STA2
Primary CH (AP1)

## Slide 11: Coordinated OFDMA Operation
Primary CH (STA2)
Primary CH (AP2)
Coordinated OFDMA primary channel selection
  When the APs participated in the coordinated OFDM operation select the same primary channel,
    The coordinated AP (its associated STAs also) whose allocated bandwidth does not cover its own primary channel needs to switch its primary channel to another channel which is within the allocated bandwidth.
Coordinator AP
Coordinated AP1
Coordinated AP2
STA1
(associated with AP1)
STA2 (associated with AP2)
Primary CH (AP1)
Primary CH (STA1)
Primary channel switch
Primary channel switch
COA frame
COA frame
Data and Trigger frames to STA1
Data and Trigger frames to STA2
COA frame
COA frame
20MHz
20MHz
Data and Trigger frames to STA1
Data and Trigger frames to STA2
UL frame to AP1
UL frame to AP2
20MHz
20MHz
20MHz

## Slide 12: Coordinated OFDMA Operation
Primary CH (STA2)
Primary CH (AP1)
Primary CH (STA1)
Primary channel switch
Coordinated OFDMA primary channel selection
  Because the STAs associated with the coordinated APs can be the hidden nodes from the coordinator AP, they may not listen the COA frame. In such case, the coordinator AP and the coordinated AP may exchange the primary channel switch (PCS) request and the primary channel switch (PCS) response frames before the coordinated OFDAM transmissions.
Coordinator AP
Coordinated AP1
Coordinated AP2
STA1
(associated with AP1)
STA2 (associated with AP2)
PCS Request frame
PCS Request frame
Data and Trigger frames to STA1
Data and Trigger frames to STA2
UL frame to AP1
UL frame to AP2
20MHz
20MHz
20MHz
20MHz
20MHz
20MHz
PCS Response frame
PCS Response frame
PCS Response frame
PCS Response frame
……
COA frame
COA frame
Primary CH (AP2)

## Slide 13: Coordinated OFDMA Operation
Coordinated OFDMA primary channel selection
  After transmitting the primary channel switch (PCS) response frame or receiving the primary channel switch (PCS) response frame, the coordinated AP and its associated STAs switch its primary channel to the temporary primary channel indicated in the PCS response frame for the coordinated OFDMA duration which is also indicated in the PCS response frame.
  After the coordinated OFDMA duration, the coordinated AP and its associated STAs switch back to their original primary channel.

## Slide 14: Conclusion
In this contribution, we present the coordinated OFDMA architecture and the basic coordinated OFDMA operation mechanisms.
In a follow-up contribution, we will evaluate and propose the details (e.g., power control and protection) of the coordinated OFDMA operation.

## Slide 15: SP1
Do you support to add the following in SFD
  An AP that intends to use the resource (i.e.,. frequency or time) shared by another AP shall be able to indicate its resource needs to the AP that shared the resource.