## Slide 1: TESLA Based Frame Authentication
Date: 2019-10-29
Authors:

## Slide 2: Abstract
This presentation describes an improvement of TESLA based frame authentication that is proposed in 11-19/451r5.

## Slide 3: Key Disclosure
The transmitter discloses the keys after d * Tk (d >= 2)
time
TK
K’N-1
TK
K’N-2
TK
K’N-3
TK
K’N-4
TK
K’N-5
TK
K’0
KN-1
KN-2
KN-3
Disclosed Key
(d = 2)
K2
Authenticator Key
Data
Auth (K’N-1)
Data
Auth (K’N-2)
Data
Auth (K’N-3)
KN-1
Data
Auth (K’N-4)
KN-2
Data
Auth (K’N-4)
KN-3
Data
Auth (K’0)
K2

## Slide 4: 11-19/1675r0: Attack scenario: Injection of fake Data frames
Injection of false eBCS Data frames (i.e., frames carrying false authenticator information) can easily exhaust the receiver buffer
  For example:
    an attacker injects many eBCS Data frames that have the same sequence # and Key (both of which are not confidential info) but different data and authenticator
    By nature of the protocol, the receiver is required to store all frames as it doesn’t know which one is the correct one until the corresponding verification key disclosed later.
    In other words, there would be one correct data frame out of 100 frames, but the STA can only tell which one is correct after getting the key.

## Slide 5: Buffering on Transmitter
The issue is caused by receiver side buffering.
To solve the issue, buffer packets in transmitter side.
Data frames include additional hash value of the data in the data frame that will be sent later.
Data
(D1)
Hash
(D3)
Data2
(D2)
Data3
(D3)
Data4
(D4)
Data5
(D5)
K0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Data6
(D6)
K0
Frame 6
Data7
(D7)
K1
Frame 7
Data8
(D8)
K1
Frame 8
HMAC
(M1, K’0)
Hash
(D4)
HMAC
(M2, K’0)
Hash
(D5)
HMAC
(M3, K’1)
Hash
(D6)
HMAC
(M4, K’1)
Hash
(D7)
HMAC
(M5, K’2)
Hash
(D8)
HMAC
(M6, K’2)
Hash
(D9)
HMAC
(M7, K’3)
Hash
(D10)
HMAC
(M8, K’2)
Use K’0, Disclose none
Use K’1, Disclose none
Use K’2, Disclose K0
Use K’3, Disclose K1
M1
M5

## Slide 6: Improve Packet Loss Tolerance
A Data frame can contain multiple hashes.
Data
(D1)
Hash
(D3)
Data2
(D2)
Data3
(D3)
Data4
(D4)
Data5
(D5)
K0
Frame 1
Frame 2
Frame 3
Frame 4
Frame 5
Data6
(D6)
K0
Frame 6
Data7
(D7)
K1
Frame 7
Data8
(D8)
K1
Frame 8
HMAC
(M1, K’0)
Hash
(D4)
HMAC
(M2, K’0)
Hash
(D5)
HMAC
(M3, K’1)
Hash
(D6)
HMAC
(M4, K’1)
Hash
(D7)
HMAC
(M5, K’2)
Hash
(D8)
HMAC
(M6, K’2)
Hash
(D9)
HMAC
(M7, K’3)
Hash
(D10)
HMAC
(M8, K’2)
Use K’0, Disclose none
Use K’1, Disclose none
Use K’2, Disclose K0
Use K’3, Disclose K1
M1
M5
Hash
(D5)
Hash
(D6)
Hash
(D7)
Hash
(D8)
Hash
(D9)
Hash
(D10)
Hash
(D11)
Hash
(D12)

## Slide 7: Further Improvement
More efficient method may be introduced in November meeting.