## Slide 1: MAC Service Update for NGV
Date: 2019-10-29
Authors:

## Slide 2: Abstract
The layers of the protocol stacks which operate just above the 802.11 MAC, and are intended for use in rapidly-changing radio environments, including IEEE 1609.4 and comparable standards for other regional regulatory domains, require access to facilities that are not exposed at either the 802.11 MAC_SAP or the MLME_SAP. Therefore, it is appropriate for TGbd to define extensions to 802.11 MAC services (limited to use when dot11OCBActivated = TRUE) that expose the functions needed by these higher layer vehicular protocols.

## Slide 3: Overview
Unexposed MAC facilities needed by higher protocol layers today include:
  Direct selection of many items in the TXVECTOR, including channel, data rate/MCS, and transmit power level, on a per-MSDU basis
  The ability to specify an “expiry time” which is the value of the TSF timer at which the MSDU is no longer valid and may be purged by the 802.11 MAC before transmission
  The ability to change the station’s MAC address without resetting the entire MAC
  Reporting of Channel Busy Percentage
Additional MAC facilities needed with 802.11bd:
  Control of the capabilities indicated by the NGV capability indication mechanism
  Reporting of capabilities indicated by other stations whose transmission are received
  Access to far more TXVECTOR parameters as well as reporting of RXVECTOR parameters from receptions that are reported upward

## Slide 4: Functions Added by TGbd Needing SAP Exposure
The enhanced MAC and PHY functionality being added by TGbd are going to require further extension
Selection of MAC enhancements provided by TGbd on a per-MSDU basis
Selection of PHY enhancements provided by TGbd on a per-MSDU basis
Reporting of optional facilities used to convey received MSDUs
Reporting of station capabilities, both for received MSDUs and for stations within RF range whose transmissions are detected but not addressed for reception at this station

## Slide 5: Comparison of the MAC_SAP as of 2016
IEEE 802.11-2016
  MA-UNITDATA.request (source address, destination address, routing information, data, priority, service class)
  MA-UNITDATA.indication (source address, destination address, routing information, data, reception status, priority, service class)
  MA-UNITDATA-STATUS.indication (source address, destination address, transmission status, provided priority, provided service class)
IEEE 1609.4-2016
  MA-UNITDATAX.request (source address, destination address, routing information, data, priority, service class, Channel Identifier, Time Slot, Data Rate, TxPwr_Level, ExpiryTime)
  MA-UNITDATA.indication not specified, the 802.11 primitive is used
  MA-UNITDATAX-STATUS.indication (source address, destination address, transmission status, provided priority, provided service class)

## Slide 6: Comparison of the MLME_SAP as of 2016
IEEE 802.11-2016
The subset of 802.11 MLME primitives explicitly listed in 1609.4 are:
MLME-GET
MLME-SET
MLME-TIMING_ADVERTISEMENT
MLME-GETTSFTIME
IEEE 1609.4-2016
MLME extension primitives specified in 1609.4:
MLMEX-TA / MLMEX-TAEND
MLMEX-CHSTART / MLMEX-CHEND
MLMEX-REGISTERTXPROFILE / MLMEX-DELETETXPROFILE
MLMEX-CANCELTX
MLMEX-GETUTCTIME
MLMEX-AddressChange
MLMEX-SendPrimitive
The primitives in bold require support within the 802.11 MAC (for dot11OCBActivated = TRUE)

## Slide 7: Extending the MAC Data Service Primitives
Add an NGV-specific parameter to each of the MAC Data Service primitives:
  MA-UNITDATA.request (source address, destination address, routing information, data, priority, service class, radio environment request vector)
  MA-UNITDATA.indication (source address, destination address, routing information, data, reception status, priority, service class, radio environment status vector)
  MA-UNITDATA-STATUS.indication (source address, destination address, transmission status, provided priority, provided service class, radio environment status vector)
A radio environment {request/status} vector parameter shall be present when dot11OCBActivated is TRUE and absent otherwise.
  By defining the new parameter as a vector, and describing the elements of these vectors in separate sub-clauses, the editorial impact on existing clause 5 text is minimized.

## Slide 8: Radio Environment Request Vector Contents
The Radio Environment Request Vector allows the higher layers to control the format, encoding, and MPDU handling for the 802.11bd transmission
The elements of the Radio Environment Request Vector include:
  Transmission format (legacy/NGV, data rate/MCS, etc.)
  Coding and spatial stream alternatives (LDPC, number of streams, etc.)
  Aggregation alternatives (if any)
  Number of repetitions
  PHY alternatives (band, channel, width, transmit power level, etc.)
  Expiry time (time after which this MSDU is discarded if not transmitted)
  … whatever else needs to be controlled within the NGV MAC and PHY functionality)
A value that permits selection within the MAC shall be defined for each element

## Slide 9: Radio Environment Status Vector Contents
The Radio Environment Status Vector provides to the higher layers status about the current radio environment and the most recent 802.11bd reception
The elements of the Radio Environment Status Vector include:
  Transmission format used (legacy/NGV, data rate/MCS, etc.)
  Coding and spatial stream alternatives used (LDPC, etc.)
  PHY alternatives used (band, channel, width, etc.)

## Slide 10: Reporting of Radio Environment Characteristics
The characteristics of the radio environment are reported on a periodic basis, independent of receptions of MSDUs, so need to be reported separately. This can be done using a new service primitive
MA-RADIOENVIRONMENT.indication (Channel Busy Percentage, Capability Percentage, Station Count)
  Channel Busy Percentage – as already defined in IEEE 1609
  Capability Percentage – percentage of stations indicating NGV capability
    Full definition (therein called “TechPercentage”) appears in 11-19/0783
  Station Count – number of individual stations (individual MAC addresses) detected during most recent measurement period of Channel Busy Percentage and Capability Percentage

## Slide 11: MLME SAP Extension
IEEE 1609.4 includes a set of primitives extending the MLME_SAP. These appear as MLMEX-primitives in Clause 7 of IEEE 1609.4-2016
  The MLME_SAP in 802.11bd should include a request/confirm primitive pair that corresponds to MLMEX-AddressChange
    A primitive for this purpose is needed by other 802.11 amendments and is being proposed to TGmd. If that proposal is adopted, no further work on this primitive will be needed in TGbd.
  The MLME_SAP in 802.11bd should include a request/confirm primitive pair that corresponds to MLMEX-CancelTX
    The function of this primitive is to cancel transmission of MSDUs, within a specified access category, that have already been submitted for transmission, within, but are not yet contending for transmission. It is not necessary to expunge MPDUs at the head of the queue and already involved in EDCA contention.
  It does not appear that other MLME_SAP extensions are required, but further consideration, and discussions with IEEE 1609 (and other, outside groups) is appropriate.

## Slide 12: Additional Attributes in 802.11bd MIB
Some of the NGV-specific parameter values are static, and can be managed as MIB attributes rather than service primitive parameters at the MAC or MLME SAPs. These include:
  NGV activation (the NGV equivalent of dot11OCBActivated)
  NGV capabilities (to be indicated in transmissions from this station)
  NGV bands supported
  Measurement interval for ChannelBusyPercentage (default value 100ms)
  ChannelBusyPercentage smoothing parameters (to accommodate CBR/CBP differences)
  Measurement interval for CapabilityPercentage (default value 1000ms)
  Interval between repetitions (for use when number of repetitions > 0)

## Slide 13: Straw Poll
Do you agree to add the following text into Section 3.2 of SFD?
  “The MAC service interface (MAC_SAP and MLME_SAP) shall be extended to provide higher layers with the ability to control NGV transmissions and receive status regarding NGV receptions and the radio environment when operating with dot11OCBActivated = TRUE).”
Y:
N:
A:

## Slide 14: Motion
To direct the TG editor to incorporate the proposed normative text from submission 11/19-1982r0 into the TGbd draft.
Y:
N:
A: