## Slide 1: Discussion of Miscellaneous NGV Preamble Designs
Date: 2019-11-11
Authors:

## Slide 2: Introduction
The preamble structure of NGV PPDU has been decided.
Some details are still pending:
  Legacy preamble: power boost level
  NGV-SIG content
    MCS level
    Coding
  NGV-LTF design

## Slide 3: Legacy Preamble Power-boost
In 11-19/1470, we showed that
  for BPSK modulation with DCM, LSTF+LLTF power boost by 3dB can improve decoding sensitivity by ~1dB.
  for BPSK modulation without DCM, LSTF+LLTF power boost by 3dB can improve decoding sensitivity by ~0.5dB.
We proposed to power boost LSTF+LLTF by 3dB for BPSK modulation both with and without DCM.
  Some concerns on the fairness between 11p PPDU with BPSK modulation and NGV PPDU with BPSK modulation (no DCM).
  For extended range transmission, where data is modulated with BPSK-1/2 DCM, legacy preamble power boost will be needed.
  For BPSK-1/2 without DCM, NGV PPDU enables better decoding sensitivity than 11p PPDU. The gain can not be achieved without legacy preamble power boost.

## Slide 4: NGV MCS Level
It has been agreed to add 256QAM for NGV high throughput and DCM for NGV extended range.
Propose the following MCS table:
  Reuse most VHT MCS table
  Remove BPSK, R=3/4
  Add three MCSs
    256QAM, R=3/4
    256QAM, R=5/6
    BPSK with DCM, R=1/2
MCS index | Modulation | Code rate
0 | BPSK | ½
1 | QPSK | ½
2 | QPSK | ¾
3 | 16QAM | ½
4 | 16QAM | ¾
5 | 64QAM | 2/3
6 | 64QAM | ¾
7 | 64QAM | 5/6
8 | 256QAM | ¾
9 | 256QAM | 5/6
10 | BPSK with DCM | 1/2

## Slide 5: Coding Options
LDPC has been agreed as the mandatory coding scheme for NGV.
Combined with Midamble, LDPC achieves good coding gain in the Doppler channels.
As all PHY modes will be mandatory for NGV, to simplify PHY design and verification, propose to make LDPC the only coding scheme for NGV PPDU.

## Slide 6: NGV SIG Content
Number of bits: total 24 bits
  BW: 1 bit
  MCS: 4 bits
  Nss: 1 bit
  Midamble periodicity: 2 bits
  LDPC Extra symbol: 1bit
  LTF format: 1 bit
  Reserved: TBD bits (<= 4 bits)
  Tail: 6 bits
  CRC: 4 bits
Potential bits to be included
  STBC bit, PHY version bits

## Slide 7: NGV LTF Formats
LTF formats discussed in NGV:
  NGV-LTF-2x: VHT-LTF downclock by 2.
    Normal mode with channel estimation on each loaded tone.
  NGV-LTF-1x: compressed NGV-LTF-2x.
    Efficient LTF mode for high-through cases.
  Repeated NGV-LTF (either NGV-LTF-2x or NGV-LTF-1x):
    useful for extended range transmission using DCM.
Repeated NGV-LTF-1x is NOT needed for range-extension transmission.
  Short GI in NGV-LTF-1x may not sufficient for long-delay channel
  Channel estimation SNR is similar as NGV-LTF-2x without repetition.
  Allow only repeated NGV-LTF-2x for range-extension transmission.

## Slide 8: Repeated NGV-LTF-2x Design
Repeated NGV-LTF-2x
  Similar design as L-LTF.
  Repeat the IFFT output.
  Pre-append only one CP.
  The duration of repeated NGV-LTF-2x is 14.4us (1.6us+6.4us*2).
CP
IFFT output
IFFT output

## Slide 9: NGV-LTF Pilot Location
For NGV-LTF-1x construction, only even tones are populated, and pilot tones need to be present in LTF.
In VHT 20MHz and 40MHz OFDM numerology, the pilots are all located on the odd tones.
  20MHz: [-21 -7 7 21]
  40MHz: [-53 -25 -11 11 25 53]
Need to redefine pilot tone location on even tones.
  Simple design by shifting to neighboring even tones.
  20MHz: [-22 -8 8 22]
  40MHz: [-54 -26 -12 12 26 54]
As Data field uses the same pilot location as NGV-LTF, propose to unify pilot location for all LTF formats.

## Slide 10: Reference
[1] Dungguk Lim and etc., “PHY Designs for 11bd”, IEEE 802.11-19/0332r2.
[2] Bo Sun and etc., “802.11 NGV SG Proposed PAR”, IEEE 802.11-18/0861r9.
[3] Jianhan Liu and etc., “Modulation Scheme for 11bd Range Extension”, 802.11-19/0343r0.

## Slide 11: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “NGV PPDU modulated with BPSK and DCM shall power boost L-STF and L-LTF by 3dB.”
Y:
N:
A:

## Slide 12: Straw Poll 2
Do you agree to add the following text into Section 3 of SFD?
  “NGV PPDU modulated with BPSK shall power boost L-STF and L-LTF by 3dB.”
Y:
N:
A:

## Slide 13: Straw Poll 3
Do you agree to add the following text into Section 3 of SFD?
  “NGV PPDU shall use LDPC as the only coding scheme.”
Y:
N:
A:

## Slide 14: Straw Poll 4
Do you agree to add the following text into Section 3 of SFD?
  “11bd shall define the following MCS table.”
Y:
N:
A:
MCS index | Modulation | Code rate
0 | BPSK | ½
1 | QPSK | ½
2 | QPSK | ¾
3 | 16QAM | ½
4 | 16QAM | ¾
5 | 64QAM | 2/3
6 | 64QAM | ¾
7 | 64QAM | 5/6
8 | 256QAM | ¾
9 | 256QAM | 5/6
10 | BPSK with DCM | 1/2

## Slide 15: Straw Poll 5
Do you agree to add the following text into Section 3 of SFD?
  “NGV SIG field shall include the following bits with bit order TBD:
    BW: 1 bit
    MCS: 4 bits
    Nss: 1 bit
    Midamble periodicity: 2 bits
    LDPC Extra symbol: 1bit
    LTF format: 1 bit
    Tail bit: 6 bits”
  Y:
  N:
  A:

## Slide 16: Straw Poll 6
Do you agree to add the following text into Section 3 of SFD?
  “NGV SIG field shall use 4-bit CRC.”
Y:
N:
A:

## Slide 17: Straw Poll 7
Do you agree to add the following text into Section 3 of SFD?
  “NGV-LTF and Midamble field shall use repeated NGV-LTF-2x when NGV Data is modulated using BPSK-1/2 with DCM.”
Y:
N:
A:

## Slide 18: Straw Poll 8
Do you agree to add the following text into Section 3 of SFD?
  “Repeated NGV-LTF-2x is constructed by repeating the IFFT output of NGV-LTF-2x twice and pre-append one cyclic prefix of duration 1.6us.”
Y:
N:
A:

## Slide 19: Straw Poll 9
Do you agree to add the following text into Section 3 of SFD?
  “NGV-LTF-2x, NGV-LTF-1x and Data symbols shall define the same pilot location.”
Y:
N:
A: