## Slide 1: NGV Midamble Period Other Choices
Date: 2019-11-08
Authors:

## Slide 2: Introduction
In May meeting, Midamble has been agreed to be supported in 11bd [1].
Different channel condition and MCS level prefer different Midamble periods.
Two bits have been reserved in NGV-SIG field to signal Midamble period [2]
  One of the midamble period has been decided to be 4
Additional choices for Midamble periods in 11bd are discussed in this contribution.

## Slide 3: Simulation Settings
10MHz DSRC channel @5.9GHz.
OFDM numerology: 11ac 20MHz DC2.
1x1-1ss, LDPC, 300 bytes.
CFO: uniform [-10 10]ppm on both Tx and Rx side.
Ideal timing.
Midamble
  one VHT-LTF
  Periods: 4, 6, 8, 10, 12, 16
Goodput is the maximum achievable effective data rate.
Goodput(SNR, M) = maxMCS{Rate(MCS) * (1-PER(MCS, SNR, M))* M/(M+1)}
  M is the midamble period

## Slide 4: Rural LOS
Period >=8 shows the best peak goodput.
Period 16 shows some goodput gain for low SNR region.

## Slide 5: Urban Approaching LOS
Period >=8 shows the best peak goodput.
Period 16 shows some goodput gain for low SNR region.

## Slide 6: Urban Crossing NLOS
Period 4 or 6 shows the best peak goodput.
Period 16 shows some goodput gain for low SNR region.

## Slide 7: Highway LOS
Period 4 or 6 shows the best peak goodput.
Period 16 shows some goodput gain for low SNR region.

## Slide 8: Highway NLOS
Period 4 or 6 shows the best peak goodput.
Period 6, 8 shows good performance for low SNR region.

## Slide 9: Summary
In this contribution, we compared the performance of 11bd PPDU with more Midamble periods.
The good set of Midamble periods are: 4, 8, 16.
  Easier implementation for Number of Midamble calculation.
  4 has already been adopted.
  8 is a good option for low to medium Doppler channel.
  16 can be the third option:
    Food for low MCS/SNR, where Doppler impact is smaller.
    For short safety message with < 16 symbols, 16 means no Midmable.
  Only define three options to limit the chip verification effort.

## Slide 10: Reference
[1] IEEE 802.11-19/0740.
[2] IEEE 802.11-19/1472r1.

## Slide 11: Straw Poll 1
Do you agree to add the following text into Section 3 of SFD?
  “One of the Midamble periodicity is 8.”
Y: 18
N: 0
A: 9

## Slide 12: Straw Poll 2
How many options for midamble periodicity do you prefer?
Option 1: 2 (No of Midamble bits in NGV-SIG field shall be reduced to 1 bit)
Option 2: 3
Option 3: 4
Option1: 5
Option2: 13
Option3: 4

## Slide 13: Straw Poll 3
Do you agree to add the following text into Section 3 of SFD?
  “One of the Midamble periodicity is 16.”
Y: 12
N: 2
A: 10

## Slide 14: Straw Poll 4
Do you agree to add the following text into Section 3 of SFD?
  “Only three Midamble periodicity options are defined in 11bd. The fourth option is Reserved.”
Y: 10
N: 1
A: 11