## Slide 1: Multi-link Channel Access Discussion Follow-up
Date: 2019-11-11
Authors:

## Slide 2: Introduction
Multi-link Operation
  Candidate feature being discussed in TGbe group
  Several aspects
    Transmission of frames of a TID over multiple links
    Minimizing negotiation overhead for fast link switching
Multi-link Channel Access
  Several discussions on multi-link channel access, asynchronous and synchronous operations
  A few contributions have considered multi-link operation with single primary channel
    Similar to 80 + 80 operation in which all devices perform backoff only one link
In this presentation, we follow up on multi-link channel access discussion presented in October conference call [1,2]

## Slide 3: Asynchronous Operation
Asynchronous multi-link channel access
  Per-link backoff procedure with no synchronization of multi-link transmissions
  Single link STAs and legacy STAs can operate on any link
  Simultaneous transmit and receive operation (STR)
  Shall be the default multi-link access mode
Multi-link TXOP Aggregation
  Link with backoff countdown to 0 can aggregate second link if idle (e.g. for PIFS)
  Per-link PPDU provides more flexibility due to diverse link conditions
TXOP: ML STA’s TXOP
Busy: other traffic

## Slide 4: Multi-link Operation Constraints at non-AP STA
Simultaneous Transmit-Receive (STR)
  STA may not be capable due to in-device power leakage from insufficient frequency separation
  Example: Link A operating in lower 5 GHz and link B operating in upper 5 GHz
Simultaneous Transmit-Transmit (STT)
  For some channel combinations, STA may not be capable of simultaneous transmission on those channels due to issues with intermodulation
  For some channel combinations, STA may not be capable of simultaneous transmission on those channels with a single antenna due to RF limitations
Simultaneous Receive-Receive (SRR)
  For some channel combinations, STA may not be capable with a single antenna due to RF limitations
  Fall back to single link operation under this constraints

## Slide 5: Non-AP STA Classification
In this presentation, we assume AP has STR capability
Multi-link STAs indicate STR and STT capability to AP
  Dynamic indication by ML STA based on operating links
In this context, classification of non-AP STAs on a link pair
  STR STA
    ML STA capable of STR, STT and SRR on that link pair
  Non-STR STA
    ML STA not capable of STR but capable of STT and SRR on that link pair
  Non-STT STA
    ML STA not capable of STR, not capable of STT but capable of SRR on that link pair
  Single link STA
    STA operating only on one of the links of the link pair

## Slide 6: Previous Contributions’ Recap
11-19/1405
  Mechanisms to improve multi-link channel utilization of non-STR STAs
  Opportunistic backoff recommencement (Appendix A)
  Multi-link busy status feedback indication (Appendix B)
11-19/1505
  Fairness considerations for multi-link TXOP aggregation (Appendix C)
link A
link B
3
2
1
0
TXOP
9
8
7
busy
TXOP
TXOP
6
5
4
3
busy
5
4
3
2
1
0
busy
Backoff countdown resumes with same value
ML
STA

## Slide 7: Multi-link TXOP Aggregation without TXOP alignment
Even though link is aggregated, TXOP need not be aligned on the multiple links
Padding to align TXOPs would lead to inefficient multi-link utilization
For efficient operation, TXOP utilized on aggregated link can be smaller than the main link on which backoff counter was 0
STR STA to STR STA case
  Per-link acknowledgement
  TXOP aggregation might be unfair in this scenario
Non-STR STA to AP/ AP to non-STR STA
  Unified acknowledgement (single Block ACK agreement [3]) on link with backoff counter zero
  Packet extension may be additionally utilized to account for processing overhead

## Slide 8: Proposal for Multi-link TXOP Aggregation Protection
Example snapshot at a non-STR STA
Non-STR STA transmits RTS on both links
Link A is the aggregated link in this example
Proposal
  If CTS is received on both links, transmission is performed on both links
  If CTS received only on the link with backoff counter 0 (link B), then transmission performed only on that link
  If CTS received only on aggregated link (link A), then no transmission is performed
    CF-End can be transmitted on aggregated link to reset NAV as data transmission will not be performed
    Regular backoff procedure applies on link B

## Slide 9: Downlink multi-link TXOP Aggregation with STT Constraint
Non-STT STA: Non-STR STA with STT constraint
Non-STT STA still benefits from multi-link operation
  Downlink multi-TXOP aggregation still possible as non-STT STA has simultaneous receive capability
  Multi-link gain observed from medium access on multiple channels even without STT capability
Per-link simultaneous acknowledgement is infeasible due to STT constraint

## Slide 10: Multi-link immediate response from non-STT STAs (1/2)
For high efficiency, immediate response is preferable
Due to STT constraint, feedback can be transmitted over a single link
Due to diverse link conditions, AP may explicitly recommend the link to be used for immediate response
Alternatively, non-STT STA may be locked on to a particular link for the immediate response transmission
Non-STT STA can decide which link to be used for the response transmission

## Slide 11: Multi-link immediate response from non-STT STAs (2/2)
Additional time may be needed to account for processing overhead at non-STT STA in constructing immediate acknowledgement for frames received over multiple links
Proposal: AP and non-STT STA negotiate Packet Extension for downlink multi-link TXOP aggregation mode during multi-link setup and AP uses that Packet Extension for this mode
The same PE can be used for non-aligned TXOP aggregation shown in slide 7

## Slide 12: Multi-link Aggregation Protection for non-STT STAs
Due to STT constraint, per-link CTS cannot be transmitted simultaneously
Proposal summary
  A new frame multi-link RTS (ML RTS) transmitted on both links
  Sequential CTS transmission over the multiple links
  Data transmission on none/one/both the links

## Slide 13: Proposal Details
  AP transmits multi-link RTS (ML RTS) on all links
    ML RTS includes the link sequence of CTS feedback
    The first link in sequence shall be the link on which backoff counter reached zero
  Non-STT STA transmits the CTS in the sequence provided by ML RTS
  Duration setting in ML RTS MAC header
    On link with backoff counter zero, duration set to TXOP duration as in regular procedure
    On aggregated link, duration set to end of corresponding CTS transmission on that link
  If CTS not transmitted on first link in sequence, then non-STT STA shall not transmit CTS on second link
  If AP does not receive a CTS on the first link in sequence, AP does not perform transmission on any link
    NOTE: Non-STT STA might transmit CTS on both links but AP might receive only on one link
  Backoff procedure can be resumed on both links after CTS timeout on first link in sequence

## Slide 14: Summary
Non-AP STAs indicate STR capability and STT capability to AP
Proposal for non-aligned multi-link TXOP aggregation with and without STR capability
Proposal for multi-link TXOP aggregation protection mechanism
Proposal for downlink multi-link TXOP aggregation acknowledgement from non-STT STAs
Proposal for downlink multi-link TXOP aggregation protection for non-STT STAs

## Slide 15: Straw Poll #1
Do you agree that 802.11be shall allow a multi-link device that has constraints to simultaneously transmit on a pair of links to operate over this pair of links?
  Signaling of this constraints is TBD

## Slide 16: References
[1] 11-19/1405, “Multi-link Operation Channel Access Discussion”
[2] 11-19/1505, “Multi-link TXOP Aggregation Considerations”
[3] 11-19-1262-06-00be-specification-framework-for-tgbe

## Slide 17: Appendix A: Opportunistic Backoff Countdown Resume
For certain conditions, non-STR STA resumes countdown on link B during busy state on link A
Similar to 802.11ax SRP-based spatial reuse backoff procedure
Inter-BSS PPDU (e.g. BSS Color)
  Backoff countdown can be resumed as frame not for non-STR STA
Intra-BSS Uplink PPDU
  Backoff countdown can be resumed, similar to above
  UL/DL bit in HE-SIG-A for HE SU PPDU/ER SU PPDU
  UL MU identified by HE TB PPDU
Intra-BSS Downlink PPDU
  Backoff countdown can be resumed if PPDU identified to be not destined to itself
  STA ID in HE-SIG-B for HE MU PPDU or unable to decode HE-SIG-B of HE MU PPDU
  No STA ID info in PHY preamble for SU PPDU and MAC header decoding can take long
  Proposal: STA ID info in EHT PHY preamble for SU PPDU

## Slide 18: Appendix B: Multi-link Busy State Feedback
Non-STR STA misses PHY preamble on link B during its TX on link A
Performs ED check on link B after its link A TXOP and cause collision at AP on link B
AP knows ML STA’s non-STR constraint and AP’s current reception of intra-BSS PPDU
Proposal: When non-STR STA completes transmission in link A, if AP is currently receiving intra-BSS PPDU on link B or if AP is transmitting on link B, then AP indicates Busy Status in feedback (ACK in figure) to non-STR STA on link A. Accordingly, non-STR STA suspends backoff procedure until the occurrence of an intra-BSS PPDU reception or aPPDUMaxTime countdown expiry
STA 1: Non-STR STA,
STA 2: single link STA
STA 1

## Slide 19: Appendix C: Aggregated link Backoff Procedure
In single link operation, CW resets to CW min upon successful transmission
Backoff counter did not reach zero on aggregated link prior to TXOP
Resetting CW to CW min on aggregated link can be unfair to single link STAs
Proposal: CW remains same as prior to TXOP on aggregated link and backoff counter resumes from value prior to TXOP
Failed transmission case can follow existing backoff procedure
link A
link B
3
2
1
0
TXOP
9
8
7
busy
TXOP
TXOP
6
5
4
3
busy
5
4
3
2
1
0
busy
Backoff countdown resumes with same value
ML
STA
TXOP: ML STA’s TXOP
Busy: other traffic

## Slide 20: Alternative solution for non-STT STA downlink TXOP Aggregation: Single Multi-link CTS over one link
  AP transmits multi-link RTS (ML RTS) on both links
  ML RTS includes the link ID of the link on which backoff counter was zero
    Non-STT STA transmits ML CTS on the indicated link
  ML CTS includes channel status of aggregated link
    Packet extension may be additionally required to allow for ML CTS construction overhead
  If AP does not receive ML CTS, AP does not perform transmission on either link
  If ML CTS indicates busy state on aggregated link (link A) then AP can transmit only on the link on which backoff counter was 0 (link B)
  Backoff procedure can be resumed on both links after the ML CTS timeout