## Slide 1: 1x LTF sequence for 11bd
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Eunsung Park |  |  |  | Ensung.park@lge.com
Insun Jang |  |  |  | Insun.jang@lge.com
Suhwook Kim |  |  |  | Suhwook.kim@lge.com
Jeongki Kim |  |  |  | Jeongki.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Nov. 2019

## Slide 2: Introduction
In the previous meeting, we approved the use of 2x Compressed NGV-LTF in 11bd.
However, we didn't determine the detail such as how to configure the sequence for the 2x Compressed NGV-LTF.
Thus, in this contribution, we consider the LTF sequence for 2x compressed mode and investigate the PAPR of the 2x compressed LTF sequence.

## Slide 3: Construction of 2x compressed LTF
For the 2x compressed LTF, the NGV-LTF-1x sequence can be mapped on even tone in frequency.
  For example, NGV-LTF-1x inserts non-zero values in tones [ ±2, ±4, ±6, …, ±28] in 10MHz.
The P matrix the same way as in 11ac is applied to NGV-LTF-1x, therefore it does not impact the receiver.
After IFFT (e.g., 64 FFT for 10MHz), the time domain has 2 periods per symbol, then we only transmit 1 period(3.2us)+GI.

## Slide 4: Construction of 2x compressed LTF
TX-diagram for NGV-LTF-1x in 10MHz

## Slide 5: NGV-LTF-1x sequence
NGV-LTF-1x sequence for 10MHz
  The even tone indices, i.e., [-28: 2: 28] are used to map the LTF sequence.
    NGV-LTF-1x sequence for 10MHz consists of 28 coefficients.
  And, for the configuration of NGV-LTF-1x sequence, considering ease of implementation and PAPR respectively, the following sequence can be considered:
    Option1 : sequence mapped on even tone index in VHT-LTF (i.e., VHT-LTF-28,28).
      NGV-LTF-1x(-28:2:28) = [1 1 -1 1 -1 -1 1 1 1 -1 1 1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 -1 1 1 -1]
    Option2 : the sequence has a minimum PAPR
      NGV-LTF-1x(-28:2:28) = [ -1 1 -1 -1 1 1 -1 1 1 -1 1 -1 1 -1 1 1 1 1 1 1 -1 -1 -1 1 1 -1 -1 -1]

## Slide 6: NGV-LTF-1x sequence
PAPR in 10MHz
  Only BPSK modulation is considered for NGV-Data.
  Op2 has the lowest PAPR and it even has a lower PAPR than L-STF.
  Although Op1 has higher PAPR than normal LTF but it still maintains the lower PAPR than data.
PAPR in 10MHz |  |  |  |  |  |  | 
L-STF | L-LTF | L-SIG (median) | NGV-SIG (median) | NGV-LTF (normal) | NGV-LTF(Op1) | NGV-LTF(Op2) | NGV-Data (median)
2.239dB | 3.1658 dB | 6.922dB | 6.682dB | 3.576 dB | 4.923 dB | 1.823 dB | 6.691 dB

## Slide 7: NGV-LTF-1x sequence
NGV-LTF-1x sequence for 20MHz
  For 20MHz, the tone index, i.e., [-58:2:58] is used
    The NGV-LTF-1x for 20MHz is composed of sequence with 58 coefficients.
  And by considering the similar concept with 10MHz, the following sequences can be considered.
    Option1 : sequence mapped on even tone index in VHT-LTF (i.e., VHT-LTF-58,58).
      NGV-LTF-1x(-58:2:58) = [1 -1 1 -1 -1 1 1 1 -1 1 1 1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 -1 1 1 -1 1 1 -1 -1 1 -1 1 1 -1 -1 -1 1 -1 -1 -1 -1 -1 1 -1 1 1 1 1 1 -1 1 1 1 -1 -1]
    Option2 : sequence based on 10MHz sequence (ex. M = NGV-LTF-1x for 10MHz ) and 2 coefficient
      We select the sequence having a minimum PAPR among the various combination.
        1. Based on Op1 of 10MHz,
          NGV-LTF-1x(-58:2:58) = [ 1 M 1 M ]
          = [ 1 1 1 -1 1 -1 -1 1 1 1 -1 1 1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 -1 1 1 -1 1 1 1 -1 1 -1 -1 1 1 1 -1 1 1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 -1 1 1 -1]
        2. Based on Op2 of 10MHz
          NGV-LTF-1x(-58:2:58) = [ M -1 M -1 ]
          = [-1 1 -1 -1 1 1 -1 1 1 -1 1 -1 1 -1 1 1 1 1 1 1 -1 -1 -1 1 1 -1 -1 -1 -1 -1 1 -1 -1 1 1 -1 1 1 -1 1 -1 1 -1 1 1 1 1 1 1 -1 -1 -1 1 1 -1 -1 -1 -1]
Note :The sequence for NGV-LTF-1x in 20MHz do not show the phase rotation per 10MHz.

## Slide 8: NGV-LTF-1x sequence
PAPR in 20MHz
  Assumed the phase rotation per 10MHz, i.e., [ 1 j ]
  In terms of PAPR, Op2 based on the sequence which has a minimum PAPR in 10MHz has the lowest PAPR.
  Op1 considering the simple implementation has a higher PAPR than that of normal LTF and the difference of PAPR between Op1 and data is very small. (i.e., 0.2 dB)
PAPR in 10MHz |  |  |  |  |  |  |  |  |  | 
L-STF | L-LTF | L-SIG | NGV-SIG | NGV-LTF (normal) | NGV-LTF (Op1) | NGV-LTF (Op2-1) | NGV-LTF (Op2-2) | NGV-Data (BPSK) | NGV-Data (QPSK) | NGV-Data (16QAM)
5.2497 dB | 5.7938 dB | 9.686 dB | 9.455dB | 6.3610 dB | 7.4684 dB | 6.5296 dB | 6.1651 dB | 7.678dB | 7.802 dB | 7.787 dB

## Slide 9: Pilot locations
In current data symbol, all pilot tones have odd indices
  In 10MHz – [ ±7, ±21 ]
  In 20MHz – [±11, ±25, ±53 ]
But, NGV-LTF-1x populates only even tone indices in the data symbol.
  For NGV-LTF-1x, a new pilot tone location needs to be defined.
Therefore, it is desirable to move all the pilot tones to even index in data symbol.
  The odd pilot tone index can be moved to near even tone index. For example, in 10MHz , the index [±8, ±22 ] can be used for pilot tone.
  Same number of pilot tones in data and NGV-LTF-1x symbol

## Slide 10: Conclusion
We investigated the PAPR of NGV-LTF-1x according to Bandwidth.
  In each BW, by considering the simple implementation and PAPR, separately, we can consider the following sequence for NGV-LTF-1x.
    In 10MHz,
      NGV-LTF-1x(-28:2:28) *= [1 1 -1 1 -1 -1 1 1 1 -1 1 1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 -1 1 1 -1]
    In 20MHz, according to whether the L-SIG improvement in terms of PAPR, we can consider the below sequence.
      w/o improvement
        NGV-LTF-1x(-58:2:58) **= [1 -1 1 -1 -1 1 1 1 -1 1 1 1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 -1 1 1 -1 1 1 -1 -1 1 -1 1 1 -1 -1 -1 1 -1 -1 -1 -1 -1 1 -1 1 1 1 1 1 -1 1 1 1 -1 -1]
      w/ improvement
        NGV-LTF-1x(-58:2:58) ***= [-1 1 -1 -1 1 1 -1 1 1 -1 1 -1 1 -1 1 1 1 1 1 1 -1 -1 -1 1 1 -1 -1 -1 -1 -1 1 -1 -1 1 1 -1 1 1 -1 1 -1 1 -1 1 1 1 1 1 1 -1 -1 -1 1 1 -1 -1 -1 -1]
Since NGV-LTF-1x only populates the even tone indices, the pilot tone should be moved to even indices in the data symbol.
  For example, the indices for pilot tones are [±8, ±22 ] and [±54, ±26, ±12] in 10MHz and 20MHz, respectively.
      *: Option1 in slide 5, ** : Option1 in slide 7, *** :Option2-2 in slide

## Slide 11: SP1
Do you agree to add the following to section 3 in 11bd SFD?
  For the 10MHz transmission, the NGV-LTF-1x sequence on subcarriers[-28:28] is given by following sequence
    NGV-LTF-1x(-28:2:28) = [1 1 -1 1 -1 -1 1 1 1 -1 1 1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 -1 1 1 -1]
  Y/N/A

## Slide 12: SP 2
Which approach do you prefer as an NGV-LTF-1x sequence in 20MHz?
  Approach1 ( Option1 described in slides 7)
    NGV-LTF-1x(-58:2:58) = [1 -1 1 -1 -1 1 1 1 -1 1 1 1 1 1 -1 1 -1 -1 -1 -1 -1 1 -1 -1 -1 1 1 -1 1 1 -1 -1 1 -1 1 1 -1 -1 -1 1 -1 -1 -1 -1 -1 1 -1 1 1 1 1 1 -1 1 1 1 -1 -1]
  Approach2 ( Option2-2 described in slides 7)
    NGV-LTF-1x(-58:2:58) = [-1 1 -1 -1 1 1 -1 1 1 -1 1 -1 1 -1 1 1 1 1 1 1 -1 -1 -1 1 1 -1 -1 -1 -1 -1 1 -1 -1 1 1 -1 1 1 -1 1 -1 1 -1 1 1 1 1 1 1 -1 -1 -1 1 1 -1 -1 -1 -1]
  Abs

## Slide 13: SP3
Do you agree to add the following to section 3 in 11bd SFD?
  The same number of pilot tones are used in NGV-LTF-1x and NGV-Data.
    In 10MHz, 4 pilot tones shall be inserted.
    In 20MHz, 6 pilot tones shall be inserted.
  The pilot tones use the even tone indies in data symbol.
    In 10MHz, the tone indices are [±8, ±22 ].
    In 20MHz, the tone indices are [±54, ±26, ±12].
  Y/N/A

## Slide 14: Appendix

## Slide 15: PAPR according to various combinations
NGV-LTF-1x(-58:58) based on Op1 of 10MHz
  M = NGV-LTF-1x sequence for 10Mhz
Combination | PAPR [dB] | Combination | PAPR [dB]
[1 M 1 M] | 6.5296 | [ 1 M M 1] | 6.5811
[1 M -1 M] | 6.7577 | [1 M M -1] | 6.9729
[-1 M 1 M] | 6.6768 | [-1 M M 1] | 7.4358
[-1 M -1 M] | 7.6519 | [-1 M M -1] | 7.5386
[M 1 M 1] | 7.4015 | [M 1 1 M] | 6.8066
[M 1 M -1] | 6.6552 | [M 1 -1 M] | 7.7689
[M -1 M 1] | 6.6984 | [M -1 1 M] | 6.8309
[M -1 M -1] | 7.6536 | [M -1 -1 M] | 7.0962

## Slide 16: PAPR according to various combinations
NGV-LTF-1x(-58:58) based on Op2 of 10MHz
Combination | PAPR | Combination | PAPR
[1 M 1 M] | 7.5646 | [ 1 M M 1] | 7.8197
[1 M -1 M] | 7.1964 | [1 M M -1] | 6.8466
[-1 M 1 M] | 7.2429 | [-1 M M 1] | 7.3829
[-1 M -1 M] | 6.9670 | [-1 M M -1] | 6.3759
[M 1 M 1] | 8.1600 | [M 1 1 M] | 7.8664
[M 1 M -1] | 7.2195 | [M 1 -1 M] | 7.4437
[M -1 M 1] | 7.2199 | [M -1 1 M] | 6.9092
[M -1 M -1] | 6.1651 | [M -1 -1 M] | 6.4623