## Slide 1: Signaling Support for Multi-RU Assignment
Date: 2019-11-10
Authors:
Name | Company | Address | Phone | Email
Lei Huang | Panasonic Corporation |  |  | lei.huang@sg.panasonic.com
Yanyi Ding |  |  |  | 
Urabe Yoshio |  |  |  | 
Rojan Chitrakar |  |  |  | 

## Slide 2
Background
Unlike 11ax, 11be shall allow more than one RUs to be assigned to a single STA [1].
This contribution addresses efficient signaling support for assigning one or more RUs to a single STA in a MU PPDU.

## Slide 3
Assumption
A single transmission scheme is applied to all RUs assigned to a single STA in a MU PPDU.
Like 11ax, MU PPDU for 11be comprises one or more SIG-B content channels, each consisting of a Common field, if present, followed by a User Specific field.
  Common field contains information regarding RU allocation.
  User Specific field consists of one or more User Block field(s).
    A User Block field comprises one or two User fields.
    Each User field contains user-specific allocation information.

## Slide 4
Multi-RU Assignment Signaling (1/5)
Two options for 11be User field design can be envisioned.
Opt1: 11be User fields have similar formats to 11ax User fields.
  For example, a 11be User field has 22 bits
    STA-ID (11 bits), MCS (4 bits), Coding (1 bit)
    Spatial configuration or NSTS/Tx BF/DCM (6 bits)
  All User fields corresponding to multiple RUs assigned to a STA contain same user-specific allocation information, i.e. all User fields addressed to a STA have same subfield values.
  Pros: little specification impact
  Cons: STA’s power efficiency may be disadvantaged.
    STA may need to decode and parse all of User fields in SIG-B to search for its User fields
      STA has no idea about the number of RUs assigned to it.
    STA may keep processing remaining MU PPDU even when not all of User fields addressed to the STA are correctly decoded.
      Multiple User fields addressed to the STA may belong to different User Block fields. Some of the User fields may not be correctly decoded.
      STA is not able to determine whether all of User fields addressed to the STA are correctly decoded or not.

## Slide 5
Multi-RU Assignment Signaling (2/5)
Opt2: the formats of 11be User fields are optimised for improving STA’s power efficiency. For example,
  Define two types of User fields:
    Type 1 User field contains user-specific allocation information.
    Type 2 User field does not contain user-specific allocation information, but include some information which enables a STA to position its remaining User fields in the SIG-B in case that multiple RUs are assigned to the STA.
  Both types of User fields have the same size.
  A Type 1 User field is used for assigning a single RU to a STA.
  Both Type 1 and Type 2 User fields are used for assigning multiple contiguous or non-contiguous RUs to a STA.
  Pros: STA’s power efficiency may be improved
    STA may be able to expedite search for its User fields in SIG-B.
    STA would stop processing remaining MU PPDU when determining not all User fields addressed to the STA are correctly decoded.
  Cons: more specification impact and some additional SIG-B overhead.

## Slide 6
Subfield | Number of bits | Description
STA-ID | 11 | 
UF Type | 1 | indicate the type of this User field
Single RU Assignment Flag | 1 | indicate whether a single RU is assigned to the intended STA
NSTS/Tx BF/DCM or Spatial Configuration | 6 | 
MCS | 4 | 
Coding | 1 | 
Example Type 1 User field format
Subfield | Number of bits | Description
STA-ID | 11 | 
UF Type | 1 | indicate the type of this User field
Contiguous RU Assignment Flag | 1 | indicate whether multiple contiguous RUs are assigned to the intended STA.
Number of Assigned RUs | 2 | indicate total number of RUs assigned to the intended STA.
RU Position/Next Assigned RU | 9 | indicate the position of RU corresponding to this User field among all the assigned RUs in case of contiguous RU assignment; indicate the next assigned RU in case of non-contiguous RU assignment.
Example Type 2 User field format
Multi-RU Assignment Signaling (3/5)
Opt2 has two more bits per User field than Opt1

## Slide 7: Multi-RU Assignment Signaling (4/5)
Further Note on Opt2
  A STA is able to determine decoding errors occur in at least one of its User fields when
    only a single User field addressed to the STA is identified, which is a Type 1 User field indicating multiple RUs are assigned to the STA; or
    one or more User fields including at least one Type 2 User field addressed to the STA are identified, but the number of identified User fields is not equal to the number of assigned RUs indicated in any identified Type 2 User field.
  In case of multiple contiguous RUs are assigned to a STA, the STA may be able to correctly process remaining MU PPDU even if not all of the User fields addressed to the STA are correctly decoded.
    The STA is able to obtain RU assignment and user-specific allocation information from one Type 1 User field and one Type 2 User field addressed to the STA.

## Slide 8
Example User field setting for Opt2:
  BW = 160 MHz
  SIG-B content channel 1
    RU allocations: 242-tone RU1, 484-tone RU2, 242-tone RU7
    User fields: UF11 to UF13
  SIG-B content channel 2
    RU allocations: 242-tone RU2, 484-tone RU3, 242-tone RU8
    User fields: UF21 to UF23
  RU assignment
    STA1: 242-tone RU1
    STA2 (contiguous): 484-tone RU3, 242-tone RU7
    STA3: (non-contiguous): 484-tone RU2, 242-tone RU2, 242-tone RU8
Use-Specific Field | STA-ID | UF Type | Single RU Assignment Flag | Contiguous RU Assignment Flag | Number of Assigned RUs | RU Position/Next Assigned RU
UF11 | STA1’s ID | 0 | 1 | n.a. | n.a | n.a.
UF12 | STA3’s ID | 1 | n.a. | 0 | 3 | 242-tone RU2
UF13 | STA2’s ID | 1 | n.a. | 1 | 2 | 2nd RU
UF21 | STA3’s ID | 1 | n.a. | 0 | 3 | 242-tone RU8
UF22 | STA2’s ID | 0 | 0 | n.a. | n.a. | n.a.
UF23 | STA3’s ID | 0 | 0 | n.a. | n.a. | n.a.
Multi-RU Assignment Signaling (5/5)

## Slide 9: Summary
Two options of 11be User field design for support of assigning one or more RUs to a single STA in a MU PPDU are addressed.
Option 1: 11be User fields have similar formats to 11ax User fields.
  Pros: less specification impact
  Cons: STA’s power efficiency may be reduced.
Option 2: the formats of 11be User fields are optimized for improving STA’s power efficiency.
  Pros: STA’s power efficiency can be improved
  Cons: more specification impact and some additional SIG-B overhead.

## Slide 10: Reference
11-19-1262-04-00be-specification-framework-for-tgbe

## Slide 11: SP #1
Do you prefer which option of 11be User field design for support of assigning one or more RUs to a single STA in a MU PPDU?
  Option 1: 11be User fields have similar formats to 11ax User fields.
  Option 2: the formats of 11be User fields are optimized for improving STA’s power efficiency.

## Slide 12: SP #2
Do you agree that all of 11be User fields addressed to a single STA in a MU PPDU shall have same subfield values?
Note: SP #2 will be run in case that Option 1 in SP #1 gets majority support.

## Slide 13: SP #3
Do you agree that two types of User fields shall be defined for 11be where type 1 User field includes user-specific allocation information while type 2 User field does not contain user-specific allocation information, but include some information which enables a STA to position its remaining User fields in SIG-B in case that multiple RUs are assigned to the STA?
Note: SP #3 will be run in case that Option 2 in SP#1 gets majority support.