## Slide 1: 16 Spatial Stream Support
Date: 2020-01-14
Authors:

## Slide 2: Introduction
In this contribution, we showed the benefit of supporting 16 streams for MU-MIMO and SU-MIMO

## Slide 3: MU-MIMO 16 Spatial Stream Support
MU-MIMO
  16 antenna AP vs 8 antenna AP
  10 STAs each STA has 2 antenna
  16 antennas AP almost double the throughput of 8 antenna AP
16ss support is a promising
feature to significantly increase
peak throughput
Sounding feedback overhead is the challenging problem. But there is an effective way to reduce overhead [2-3, and more]
Results from [1]

## Slide 4: SU-MIMO 16 Spatial Stream Support
SU-MIMO
  Maximum 8 vs 16 spatial streams
  Assume 16 antennas at both transmitter and receiver
  There is clear performance benefit of supporting 16 spatial streams
As shown in [3], performance impact of increased feedback overhead is not critical in SU-MIMO case

## Slide 5: Straw Poll #1
Do you support that 11be defines a maximum of 16 spatial streams for SU-MIMO?

## Slide 6: Straw Poll #2
Do you support maximum 16 spatial streams for MU-MIMO in 11be?

## Slide 7: Reference
[1] 11-18/1575r0, “Further study on potential features”
[2] 11-19/1018r1, “Feedback Overhead Reduction”
[3] 11-19/1495r0, “Further Discussion on Feedback Overhead Reduction”
[4] 11-19/0719r1, “TGbe channel model document”