## Slide 1: 802.11be Preamble and Auto-Detection Analysis and Comparison
Date: 2019-11-05
Authors:

## Slide 2: Introduction
Previously, we compare the performance using masked RL-SIG. The masked RL-SIG shows good performance regarding both miss and false probability.
We have received some feedbacks that an exact repetition of L-SIG is preferred. Here we further evaluate the performance if RL-SIG is applied.
Here we consider three options.
  Opt 0: L-SIG+RL-SIG with length % 3=0
  Opt 1: L-SIG+RL-SIG with length % 3= 1 or 2, and the second symbol after L-SIG is QBPSK
  Opt 2: L-SIG+SIG-1+RL-SIG with length %3=1 or 2, exchange the order of RL-SIG and SIG-1

## Slide 3: Three Options
Several aspects are analyzed:
  For Opt 0: false probability issue caused by 11a, 11ba.
  For Opt 1: verify that Opt 1 will not cause any issues to legacy STAs
  For Opt 2: an alternative solution, miss and false probability are shown.
  Some discussion on the contents of SIG-1 (“pre-SIG”)

## Slide 4: False probability issue of Opt 0
Let’s first consider the three formats shown below:
  Opt 0: L-SIG+RL-SIG with length % 3=0+SIG-1
  11ba: L-SIG+RL-SIG+RL-SIG with length % 3=0
  11a: L-SIG + SYM 1 + SYM 2
We can see that by only comparing L-SIG and RL-SIG, it is impossible to differentiate Opt 0 and 11ba.
We further consider the two methods based on the feedback:
  Opt 0.1 (ED): does energy detection on the four additional tones of L-SIG and RL-SIG
  Opt 0.2 (2nd repetition check): further compare the 2nd symbol after L-SIG is different from L-SIG or the 1st symbol after L-SIG

## Slide 5: False probability issue of Opt 0
We have shown that both options can help to reduce the false probability whilst the miss probability becomes terrible.
Moreover, 11a can be easily false detected as Opt 0, similar as 11ax when the MAC header of 11a is set to some specific pattern.

## Slide 6: False probability by 11ba

## Slide 7: Opt 1: Performance and Benefits
Opt 1: L-SIG+RL-SIG with length % 3= 1 or 2, and the second symbol after L-SIG is QBPSK
Opt 1 follows the same structure as 11ax in the first two symbols, and the Rx further differentiates from 11ax by detecting BPSK/QBPSK of the 2nd symbol after L-SIG.
False prob: 11baOpt1
False prob: 11axOpt1

## Slide 8: Opt 1: will not cause issues to legacy STAs
The performance has shown Opt 1 provides good performance for both miss and false probability.
Opt 1 doesn’t add any new procedure of auto-detection, relies on the existing procedures.
Opt 1 provides differentiations to all the previous standard.
Another advantage of Opt 1 is that Opt 1 also prevents 11a PPDU falsely detected as 11be PPDU.
Opt 1 provides one bit signaling in the L-SIG field.
It is said QBPSK after the 2nd symbol of L-SIG may make VHT Rx detect Opt 1 as a VHT PPDU. First of all, we don’t think it is an issue. It is beneficial regarding power save. Whilst with length % 3 = 1 or 2, VHT Rx will detect Opt 1 as a non-HT PPDU. Hence Opt 1 will not cause issues to legacy devices.
11be PPDU
If spoofed as 11a PPDU
If spoofed as 11ac PPDU
VHT device: the Rx will stop decoding until the end of the PPDU
VHT device: the Rx stops decoding after “VHT-SIG-A”

## Slide 9: Opt 2: exchange the order of RL-SIG and SIG-1
Opt2: L-SIG+SIG-1+RL-SIG with length %3=1 or 2, exchange the order of RL-SIG and SIG-1.
For Opt2, the different location of repetition provides a differentiation between 11ax and Opt2. Length % 3 = 1 or 2, provides a differentiation between 11be and 11ba.
Opt 2 also provides differentiations to all the previous standard.
Opt 2 provides one bit signaling in the L-SIG field.
False prob: 11baOpt2
False prob: 11axOpt2

## Slide 10: Contents of SIG-1
Several contribution propose to use PPDU/standard version to differentiate 11be and 11be+ PPDU.
If this is applied, we prefer the Rx can get the PPDU/standard version early enough. Hence we either prefer 1 symbol SIG-1, or 2 symbols SIG-1 where PPDU version is with its own CRC and tail in the 1st symbol.

## Slide 11
Observations and Conclusions
We have further analyze three options assuming RL-SIG is applied.
  Opt 0: L-SIG+RL-SIG with length % 3=0
  Opt 1: L-SIG+RL-SIG with length % 3= 1 or 2, and the second symbol after L-SIG is QBPSK
  Opt 2: L-SIG+SIG-1+RL-SIG with length %3=1 or 2, exchange the order of RL-SIG and SIG-1
We have shown the false probability issue caused by Opt 0, and shown the feasibility of Opt 1 and Opt 2.

## Slide 12: Straw Poll 1
Do you agree to apply the following auto-detection methods for 11be:
  L-SIG + RL-SIG with length % 3 =1 + QBPSK modulated SIG-1 symbol
  SIG-1 symbol contents are TBD.

## Slide 13: Straw Poll 2
Do you agree to apply the following auto-detection methods for 11be:
  L-SIG+SIG-1+RL-SIG with length %3=1 or 2
  SIG-1 is different from L-SIG
  SIG-1 symbol contents are TBD.

## Slide 14
[1] IEEE 802.11-19/1099r0 preamble structure in 11be, Ross Jian Yu (Huawei)
[2] IEEE 802.11-19/1142 Discussion on the Preamble for 11be, Dongguk Lim (LGE)
[3] IEEE 802.11-15/0643r0 auto-detection with signature symbol, Sriram Venkateswaran (Broadcom)
[4] IEEE 802.11-10/0549r2 TGac Preamble Auto-Detection Comparisons, Hongyuan Zhang (Marvell)
[5] IEEE 802.11-19/1214r0 Preamble Design Consideration for 802.11be, Rui Yang (InterDigital)
[6] IEEE 802.11-19/1021r1 Preamble Design Harmonization, Sameer Vermani (Qualcomm)
[7] IEEE 802.11-19/1085r0 High-level EHT Preamble Structure, Rui Cao (Marvell)
[8] IEEE 802.11-19/1486r1 Further Discussion for 11be Preamble, Dongguk Lim (LGE)
[9] IEEE 802.11-19/1556r0 Lean PHY for EHT, Miguel Lopez (Ericsson)
[10] IEEE 802.11-19/1540r0 EHT Preamble Design, Rui Cao (Marvell)
[11] IEEE 802.11-19/1519r0 Forward Compatibility for WiFi Preamble Design, Sameer Vermani (Qualcomm)
[12] IEEE 802.11-19/1516r0 11be Preamble Structure, Xiaogang Chen (Intel)
[13] IEEE 802.11-19/1511r0 preamble autodetection for 11be, Lei Huang (Panasonic)
[14] IEEE 802.11-19/1497r0 Auto-detection in 11be, Si-Chan Noh (Newratek)
[14] IEEE 802.11-19/1488r0 Auto-detection in 11be, Ross Jian Yu (Huawei)
References

## Slide 15: Simulation Configurations
Bandwidth | 20 MHz
Channel model | TGn/TGac
UL/DL | DL
Channel condition | NLOS
Antennas | 1x1
CFO | 20 ppm
To show the performance of different options, we simulate them. Some simulation configurations are shown here.

## Slide 16: Recap: Auto-Detection
Auto-detection is implemented in the dashed rectangle. The main methods include detecting RL-SIG, detecting BPSK/QBPSK, checking SIG, etc.