## Slide 1: Passive radar: a potential solution for WLAN sensing
Date: 2019-11-11
Authors:
Name | Affiliation | Address | Phone | Email
Rui Du | Huawei Technologies Co. Ltd | F3, Huawei Base, Shenzhen, China |  | ray.du@Huawei.com
Danny Tan Kai Pin |  |  |  | dannyt.pin@huawei.com
Chenchen Liu |  |  |  | liuchenchen1@huawei.com
Xiaohui Peng |  |  |  | 
Baojian Zhou |  |  |  | 
Zhichao Rong |  |  |  | 
Ping Zhang |  |  |  | 
Meihong Zhang |  |  |  | 
Yizheng Tang |  |  |  | 
Jiajin Luo |  |  |  | 
Tony Xiao Han |  |  |  | 
David Xun Yang |  |  |  | 

## Slide 2: Outline
Abstract
Definition of passive radar
Signal processing for passive radar
Range/Doppler resolution of bistatic radar
Experimental measurement
  Measurement configurations
  Evaluation platforms
  Measurement results
Potential impacts on WLAN standards
Summary
Rui Du, et al. (Huawei)

## Slide 3: Abstract
Radar and CSI had been proposed as two main potential techniques for WLAN sensing [1-2].
Measurement results of active radar for indoor scenarios at 60 GHz had been presented in September IEEE 802.11 meeting[3].
This contribution focus on WLAN passive radar at 5 GHz in indoor scenarios, relevant passive radar background and experimental results will be shown and discussed.
Rui Du, et al. (Huawei)

## Slide 4
1 Definition of passive radar
Different from active radar systems, passive radar has no dedicated transmitter. Instead, the receiver uses non-cooperative source in the environment and measures the time/Doppler difference between the signal arriving directly from the transmitter and the signal arriving via reflection from the object.
Rui Du, et al. (Huawei)

## Slide 5
2 Signal processing of passive radar
Surveillance channel signal
Reference channel signal
Clutter cancellation
Matched
filter
Time-frequency analysis
The main passive radar signal processing techniques are described as follows:
  The direct path and static clutter signals are to be suppressed from the surveillance signal;
  The matched filter is used to process the “clean” surveillance signal and reference signal ;
  Time-frequency analysis is used to analyze the micro-Doppler of the target.
Rui Du, et al. (Huawei)

## Slide 6
3 Range/Doppler resolution of passive (bistatic) radar
Range resolution:
  is the speed of light;
  is defined as the bistatic angle;
  is the bandwidth of the signal.
The relationship of target’s speed and doppler velocity and the doppler resolution:
  is the target velocity;
  is the wavelength corresponding to the carrier frequency;
  is the angle between the target’s velocity and angular bisector of bistatic angle ；
  is the coherent processing interval.
Target
Baseline
Tx
Rx
Rui Du, et al. (Huawei)
* Please note that when , the analysis above on could be applied for monostatic radar.
Dual channel passive radar

## Slide 7
4.1 Measurement configurations
Measurement configurations:
  Location: F3-5-A19R @ Huawei, Shenzhen Campus
  Measurement area: 3m×4m
  Transmitter
  Signal format: 802.11ax
  Carrier frequency: 5.35GHz
  Bandwidth: 20 MHz
  Range resolution: 7.5m (for monostatic radar)
  Antenna pattern: Omnidirectional
  EIRP: 20 dBm
  Receiver
  Number of channels: 1 reference channel and 1 surveillance channel
  Antenna pattern: V-16°, H-16°
  Antennas polarization: V-V
x
y
z
Measurement Area
Receiver
Transmitter
Reference channel
Surveillance channel
Rui Du, et al. (Huawei)

## Slide 8
4.2 Evaluation platforms
Transmitter
  The transmitter platform is based on WLAN Toolbox in MATLAB and Zynq SDR.
  IEEE 802.11ax WLAN waveforms are generated by the WLAN Toolbox, and passed to the Zynq SDR for transmission via hardware support package.
Receiver
  The receiver platform is based on Ettus USRP X310 SDR.
  The signal is received via USRP Hardware Drive(UHD), and the received signal is processed offline in matlab.
USRP X310
UHD
Offline signal processing
Reference channel
Surveillance channel
Receiver
1 Reference channel
1 surveillance channel
Transmitter
1 omnidirectional antenna
Rui Du, et al. (Huawei)

## Slide 9
4.3.1 Measurement results
A human target walking towards the passive radar, making a U-turn and walking away from the radar and so on.
Rui Du, et al. (Huawei)
Walking
http://www.clipartpanda.com/clipart_images/walk-clipart-black-and-white-38665509

## Slide 10
4.3.2 Measurement results
A human target doing a hand push and retracting at approximately 3 meters away from the passive radar.
Rui Du, et al. (Huawei)
Hand push
https://www.shutterstock.com/zh/search/pushing+hand+vector?image_type=illustration

## Slide 11
4.3.3 Measurement results
A human target squatting and standing up at approximately 3 meters away from the passive radar.
Rui Du, et al. (Huawei)
Squat
https://ya-webdesign.com/explore/squat-vector-deadlift/

## Slide 12
4.3.4 Measurement results
A human target mimicking a fall and standing up at approximately 3 meters away from the passive radar.
Rui Du, et al. (Huawei)
Falling
https://hearinghealthmatters.org/dizzinessdepot/2018/automatic-fall-detection-a-step-in-the-right-direction/

## Slide 13
5 Potential impacts on WLAN standards
Sensing result feedback
Multiple Beams
  Two beams (reference channel and surveillance channel);
  Multi beams (one reference channel and multiple surveillance channels);
  …
Multiple devices
  Idle devices (AP/STA) could participate passive sensing, the cooperation between different nodes could be discussed;
  …
Others
Rui Du, et al. (Huawei)

## Slide 14: Summary
The definition of passive radar and relevant range/Doppler resolutions are discussed.
The feasibility of detecting target with WLAN passive radar operating at 5 GHz is validated, and more tests could be conducted in the future.
The potential impacts on WLAN standards are discussed.
Rui Du, et al. (Huawei)

## Slide 15: References
[1] 11-19-1164-00-0wng-wi-fi-sensing.pptx
[2] 11-19-1500-00-0wng-wi-fi-sensing-follow-up.pptx
[3] 11-19-1551-00-0wng-wi-fi-sensing-in-60ghz-band.pptx
Rui Du, et al. (Huawei)