## Slide 1: ISTA LCI Table Updating for Passive Location
Date: 2019-11-07
      Nov. 2019

## Slide 2: Background
In the CR to support AoD in passive location [1], the following spec text is added for Passive Location LCI table element in Primus RSTA Broadcast LMR:
  “The ISTA LCI Report subfield is present if the ISTA has never transmitted it before or its content has changed and it is periodically present otherwise ”
However, in the spec there is no definition for how the ISTA updates the LCI table with RSTA if its content has changed
In this presentation possible solutions are discussed
[1] IEEE 802.11-19/0677r3 Proposed resolution to LB#240 CID 2302 on AoD for passive ranging
      Nov. 2019

## Slide 3: Discussions
      Nov. 2019
In current spec, if an ISTA supports passive location, the ISTA’s LCI table is only included in IFTMR frame during negotiation
  The LCI Report contains the Antenna Placement and Calibration subelement if the ISTA further supports AoD in passive location
In passive location measurement sequence, RSTA periodically broadcast the ISTA’s LCI table in the Primus Broadcast LMR frame
  When Passive Location LCI Table Countdown equals 0, the LCI table is included in the current availability window
In the passive ranging session, the ISTA’s LCI table may change
  ISTA may be mobile, and location information is dynamic
  ISTA may switch Tx antennas and antenna placement info is changed
ISTA shall update the new LCI with RSTA to guarantee the passive client always use up-to-date LCI for passive location

## Slide 4: Proposed Solution 1
If ISTA’s LCI table is changed, ISTA shall send FTM request frame to RSTA with new LCI table before the next passive location measurement sequence.
  Or the ISTA shall not join the following passive location measurement sequences before it sends FTM request with LCI to RSTA
After RSTA receives ISTA’s FTM request with LCI report, the RSTA shall include the LCI report in the Primus Broadcast LMR in the immediate following passive ranging measurement sequence
  Passive Location LCI Table Countdown value can be reset
      Nov. 2019

## Slide 5: Proposed Solution 2
If ISTA’s LCI table has changed, the ISTA shall send FTM request frame to RSTA to terminate the passive ranging session with RSTA
  With Triger field set to 0
The ISTA may send a new IFTMR frame to RSTA to re-negotiate a new passive ranging session
  The IFTMR frame includes the ISTA’s new LCI report
      Nov. 2019

## Slide 6: Straw Poll
To enable ISTA’s LCI update with RSTA in passive location, which option do you support?
  Option 1: ISTA sends FTM request to update LCI with RSTA
  Option 2: ISTA sends FTM request to terminate current passive location session
  and re-negotiate with RSTA using new LCI
  Y: N: Abstain:
      Nov. 2019