## Slide 1: MLO: Link management–follow up
Name | Affiliation | Address | Phone | Email
Abhishek Patil | Qualcomm Inc. |  |  | appatil@qti.qualcomm.com
George Cherian | Qualcomm Inc. |  |  | 
Alfred Asterjadhi | Qualcomm Inc. |  |  | 
Duncan Ho | Qualcomm Inc. |  |  | 
Date: 2019-11-08

## Slide 2: Overview
Past contributions [1, 2, 4] have discussed the benefits of multi-link operation and have proposed a unified framework to support packet-level aggregation and dynamic transfer of a TID between links
Other presentation have proposed a single association for multi-link setup [1][2][3]
Contribution [5] discusses TID-to-link mapping
This contribution continues link management discussions

## Slide 3: Steps involved in link management
Link setup
  Involves capability exchange, multi-link association, link configuration
  Exchanged parameters are valid through the context and duration of the ML association
  Initiated by a non-AP entity
Multi-link TID-Link mapping procedure
  Established for each TID flow
  Dynamic (i.e., remapping)
    Can change every time a TID flow is started or terminated
  Either AP or non-AP entity could initiate (re)mapping
Power-save and Link expansion
  Non-AP entity can transition to doze state on a link to conserve power (e.g., due to inactivity on that link)
    Can use existing PS Poll/APSD trigger or upon receiving EOSP from AP
  AP entity can request wake up of a dozing link(s) to expand the links quickly (e.g., due to load balancing)
    Can use new signaling

## Slide 4: TID-to-Link Mapping
Identifies the link(s) over which frames belonging to a TID can be transmitted
  This could be a subset of links that are set up between the two entities during the multi-link association step
Mapping could be performed during or after multi-link association
  The mapping can be updated later via mgmt. signaling
Either peer could trigger an update (remapping)
  Based on start of a new TID flow, or termination of an existing flow, or changes in channel condition

## Slide 5: Considerations on Power-save
A non-AP entity consumes power in monitoring a link
  Therefore the framework must provide a mechanism for the non-AP entity to save power
To achieve this, a non-AP entity is not required to monitor more than one link during idle or light traffic conditions
  The non-AP entity monitors a default link
    Default link identified by TBD means
  The STA instances on other links may enter doze state
AP always monitors the mapped links; therefore, the non-AP entity can transmit UL to the AP entity on any of the mapped link(s)
However, the AP entity needs to provide an explicit indication to the non-AP entity when it intends to service it on a link other than the default link (because the non-AP may be in the doze state on that link)

## Slide 6: Per-link power-save
Each STA instance can utilize existing PS schemes (such as EOSP=1 or MORE=0 from AP or PM=1 during inactivity from non-AP) to transition to doze or awake state
  STA instance on default link continues to monitor beacon
    Default link identified by TBD mechanism

## Slide 7: Cross-link Wake Up
AP entity signals ‘wake-up’ of other links via signaling on the default link.
Two signaling schemes are listed below:
  TXOP-to-TXOP level granularity
    Similar to OM transition changes (i.e., after the end of the TXOP)
    Possible with A-Control-level signaling to indicate wake-up on another link
  TBTT-to-TBTT level granularity
    Beacon indicates the link(s) on which the non-AP entity needs to declare that it is in awake state
      Could use per-link AID to signal via TIM element
Optional PS-POLL/APSD trigger from non-AP STA to indicate awake state on the link

## Slide 8: Summary
This contribution provides a clear delineation between TID-to-link mapping and power-states of each link
  Introduces the concept of a default link where the non-AP entity, at the least, monitors APs beacons
  Each non-AP STA instance performs transition to doze state based on activity on its associated link
  Introduces cross-link wake-up signaling

## Slide 9: SP #1
Do you support that the 802.11be amendment shall define a signaling to map and dynamically remap a TID to one or more setup links?
  Y:
  N:
  A:

## Slide 10: SP #2
Do you agree that a non-AP STA instance (of an MLLE) maintains its own power-state/mode on a link to which at least one TID is mapped?
  Y:
  N:
  A:

## Slide 11: SP #3
Do you agree that an AP MLLE can recommend wake-up of a STA instance of that non-AP MLLE by signaling to another STA instance of that non-AP MLLE?
  The AP’s indication could be via a broadcast or a unicast frame
  Y:
  N:
  A:

## Slide 12: References
[1]: 11-19-0773 Multi-link Operation Framework (Po-Kai Huang - Intel)
[2]: 11-19-0823 Multi-Link Aggregation (Abhishek Patil - Qualcomm)
[3]: 11-19-0821 multiple band discussion (Liwen Chu - Marvell)
[4]: 11-19-1082 Multi-link Operation: Dynamic TID Transfer (Abhishek Patil - Qualcomm)
[5]: 11-19-0979 Multi-link Operation Follow-up (Yongho Seok - Mediatek)

## Slide 13: Appendix

## Slide 14: TXOP-to-TXOP

## Slide 15: TBTT-to-TBTT