## Slide 1: Coordinated OFDMA
Date: 2019-11-06
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Young Hoon Kwon Manish Kumar Hongyuan Zhang Yan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: AP Coordinated OFDMA
In coordinated OFDMA (C-OFDMA), multiple APs schedule OFDMA transmission within one DL/UL MU:
  one AP is coordinator AP and other APs are coordinated APs.
  Two stages for one coordinated OFDMA transmission:
    Coordinate OFDMA announcement stage,
    Coordinate OFDMA MU transmission stage.
  Before the announcement stage, an option resource polling stage may be scheduled.
Why UL C-OFDMA is required:
  Finishing the DL C-OFDMA in one TXOP, i.e. QoS Data frames + solicited acknowledgement.
C-OFDMA
MU transmission stage
C-OFDA Announcement stage
AP1
AP2
STA21
STA22
STA11
STA12
STA23
STA24
STA13
STA14
coordinator AP
coordinated AP

## Slide 3: Coordinator AP and Coordinated AP
Coordination role setup:
  Static method: The APs creates coordination OFDMA group implicitly (or through negotiation) to do coordinated OFDMA and which one will be the coordinator AP through public Action frame.
  Dynamic method: The AP that gets the medium access right becomes the coordinator AP. The master announces the coordinated APs that can join the coordinated OFDMA transmission.
  Static group formation and dynamic coordinator:
    The APs creates coordination OFDMA group implicitly (or through negotiation) to do coordinated OFDMA.
    An AP in the group that gets the medium access right becomes the coordinator AP. The master announces the coordinated APs that can join the coordinated OFDMA transmission.
AP1
AP2
STA21
STA22
STA11
STA12
STA23
STA24
STA13
STA14
coordinator AP
coordinated AP

## Slide 4: Coordinated OFDMA Announcement/Enabling
An AP announces whether it supports coordinated OFDMA or not through management frame, e.g. Beacon.
A STA announces whether it wants to be scheduled in coordinated OFDMA.
an AP (AP1) notifies its neighbor AP (AP2) whether it allows AP2 to schedule coordinated OFDMA transmission for AP1.
  The default mode could be allowance and an AP notifies the disallowance, or the default mode could be disallowance and an AP notifies the allowance.
  An management frame is defined for this purpose.

## Slide 5: Straw Poll 1
Do you support that
  Coordinated OFDMA is supported in 11be, and
  In a coordinated OFDMA, both DL OFDMA and its corresponding UL OFDMA acknowledgement are allowed.
  Y: 53 N: 3 A: 43

## Slide 6: Motion 1
Move to add the following text to 11be SFD:
  Coordinated OFDMA is supported in 11be, and
  In a coordinated OFDMA, both DL OFDMA and its corresponding UL OFDMA acknowledgement are allowed.
  Moved by Liwen Chu